Status of OBLA
Measurements
Thomas Schietinger
FELSI Meeting, 29 January 2008

---
Measurement campaign so far
Before Christmas: first beam observed, but parts of the diagnostics not yet working, large timing jitter.
First two weeks of January mainly devoted to
hardware fixes (timing problem, diagnostics)
Observe (?) charge-up of UHV mirror
  - go from 2.5 mm to 5 mm distance from beam
Solenoids have strong effect on beam position
  - Realignment requested (done last Friday)
First attempt to estimate emittance: solenoid scan on 24 Jan., using first solenoid (MSL10=SP1, bolted to pulser, has counter coil)
Emittance monitor;
200 kV / 12 mm gap

---
Solenoid Scan with MSL10
MSL10 has counter coil. Exact field map depends on ratio main/counter coil!
  - MSL10 not very well suited for solenoid scan
To cancel B field on cathode at 12 mm gap, counter coil current must be –2.37% of main coil
  - This value is different for each gap!
For main coil current around 30–40 A, no current on counter coil:
  - field integral ∫(B/I)2dz = 28.182 kT2m/A2,
  - effective length leff = ∫(B/Bmax)2dz = 33.70 mm
Use these values for preliminary emittance evaluation

---
Solenoid Scan, 24 Jan. 2008
Å. Andersson, Y. Kim
Cathode-anode gap: 12 mm
Pulser voltage: ~315 kV
Laser x,y: 130 µm
Laser t: 16.5 ps
Pixel size: 25.8 µm
Distance solenoid-screen: 429.5 mm
I(main coil): 31 A
I(counter coil): 2 A

---
I(main coil): 32 A

---
I(main coil): 33 A

---
I(main coil): 33.5 A

---
I(main coil): 34 A

---
I(main coil): 34.5 A

---
I(main coil): 35 A

---
I(main coil): 35.5 A

---
I(main coil): 36 A

---
I(main coil): 36.5 A

---
I(main coil): 37 A

---
I(main coil): 37.5 A

---
I(main coil): 38 A

---
I(main coil): 38.5 A

---
I(main coil): 39 A

---
x = 1.17 ± 0.07 mm mrad
y = 1.12 ± 0.14 mm mrad
To be used with caution!!
(fit and plot by S. Leemann)

---
Charge: 7.6 pC
mesh: 32 × 32 × 32
macroparticles: 100k
time step: 0.1 ps (gun), 1 ps (after)
t: 16.5 ps; rx,y: 225 µm
Simulation (Impact-t)
Itot = 31 A
Itot = 31 A
Itot = 35 A
Itot = 39 A

---
Charge: 7.6 pC
mesh: 32 × 32 × 32
macroparticles: 100k
time step: 0.1 ps (gun), 1 ps (after)
t: 16.5 ps; rx,y: 450 µm
Simulation (Impact-t)
Itot = 31 A
Itot = 31 A
Itot = 35 A
Itot = 39 A

---
Older simulations (Impact-t)
Charge: 6 pC
mesh: 32 × 32 × 32
macroparticles: 100k
time step: 0.1 ps (gun), 1 ps (after)
t: 6.5 ps; rx,y: 300 µm

---
Simulation (Impact-t)
Charge: 7.6 pC
mesh: 32 × 32 × 32
macroparticles: 100k
time step: 0.1 ps (gun), 1 ps (after)
t: 16.5 ps
rx,y: 450 µm
OBLA
Itot = 31 A
Itot = 31 A
Itot = 35 A
Itot = 39 A