## Slide 1
MD week 48 report
E. Prat
SEM meeting, November 30

## Slide 2
Overview
SINSB02 power increase
Athos BPMs
Machine learning
Optics checks with bunch 2
Energy tuning with C-band
BC1 pulse shaping
Emittance with WS
Startup, design optics
Linac 3 orbit feedback
2-bunch LLRF
OTR in ACHIP
ACHIP wakefield studies
Energy spread
laser heater
optics- WS
ACHIP wakefield studies
Week roughly as planned – few changes (design optics set already on the startup and some other swaps)
No major issues
Notes: 2

## Slide 3
Tested new server deployment (can now be (re-)started via “restart_mlopt” (the GUI can still be started via “start_opt_gui.sh”
Deployed updated GUI version that now has a more sophisticated data browser and many helpful tool tips concerning the different hyperparameters
Tool is now ready to be used -> Nicole will add documentation
Tested a configuration for Athos -> works in principle, but it’s not yet easy to switch between Aramis and Athos, we will prepare a separate server for Athos to allow parallel operation
Tested a new Bayesian optimization algorithm that does more local sampling which looks also promising
Mon 23.11.2020 Night shift
Participants: Nicole Hiller, Johannes Kirschner (ETHZ)
Machine learning
Courtesy of N. Hiller

## Slide 4
C-band tuning with phase slope and offset
Goal: vary energy gain of 1 C-band module without changing energy spread with phase slope and offset – important for Athos tuning
Measurements at S10CB01/02. Energy varied between 13 to 250 MeV
Energy spread constant for different energy gains
Excellent agreement between measured and expected phase slope/offset for different energy variations
Next: create lookup table for LLRF
More info: https://elog-gfa.psi.ch/SwissFEL+commissioning/17181
Energy spread estimation vs energy gain
Model and measured phase slope vs energy gain
R. Zennaro, Q. Geng, P. Craievich, C. Kittel
Notes: 4

## Slide 5
Emittance measurements with wire-scanners
WS better than screens to measure emittance and match the optics at the linac end
Tested emittance measurements with WS at SARCL and SARMA:
  SARCL not suitable (as seen in the past): signal-to-noise ratio poor, DRPS losses
  SARMA much better: good signal-to-noise, no losses
Measurements confirmed the need to use the WS
Need work to improve robustness and easiness of the measurement
More info: https://elog-gfa.psi.ch/SwissFEL+commissioning/17182
Results at SARMA | X | Y
Screen | 740 nm, M=2.35 | 1350 nm, M=1.03
Wire | 420 nm, M=1.05 | 245 nm, M=2.0
Wire-scanner measurement in X
P. Dijkstal, E. Ferrari, B. Hermann, R. Ischebeck, S. Reiche, E. Prat
Notes: 5

## Slide 6
Pulse shaping in BC1
Scrapping the beam in BC1 can remove the horns, give a smoother current profile and more robust operation
Adjusted BC1 collimator to cut the horns (15% of the total charge). LLM limits rate to 10 Hz
RF adjusted to get symmetric profile
CDR drops a lot, normally running mostly on the horns
Pulse energy reduced from ~400 to ~200 uJ
Next: optimize compression for flatter current profile, maximize pulse energy
S. Reiche
Initial profile
After scrapping
After RF tuning
More info: https://elog-gfa.psi.ch/SwissFEL+commissioning/17196
Notes: 6

## Slide 7
Energy spread & laser heater measurements
Re-measured injector energy spread vs laser heater R56, without laser heater (now with properly calibrated R56)  lower values for R56<1.5 mm (similar as previous meas.).
From 11 to 8 keV  10-20% higher pulse energies
Measured effect of laser heater on energy spread for nominal and reduced R56
We decided to stay at R56=1.2 mm, laser heater ready to be used (laser heater did not have a positive influence on lasing when we had ~200 uJ)
https://elog-gfa.psi.ch/SwissFEL+commissioning/17286
P. Dijkstal, E. Ferrari, M. Huppert, A. Malyzhenkov, E. Prat, S. Reiche
Usual point
New point
Notes: 7

## Slide 8
Others
Increase of SINSB02 power (RF + operations, Monday morning): energy gain increased by ~10 MeV – energy at laser heater is now 150 MeV.
Athos BPMs (Boris, Monday late): scaling factors of SATUN04/06/07/08/09 calibrated in X and Y.
Startup with design optics on Thursday
Linac 3 orbit FB (Florian, Friday morning): feedback split in 3 parts to improve reliability
2-bunch RF setup (Qiao, Friday late): https://elog-gfa.psi.ch/SwissFEL+commissioning/17247
OTR in ACHIP (Pavle et al, Saturday morning): https://elog-gfa.psi.ch/SwissFEL+commissioning/17268, see separate report
Gas detector filter studies (Pavle et al, Saturday): see separate report
ACHIP shift (Benedikt et al, Saturday): https://elog-gfa.psi.ch/SwissFEL+commissioning/17272
Notes: 8