Issues
Changes in the base layout
Operational difficulties
Alternative Sources and Topics to Investigate

---
Present Tunnel Layout
end
bunch
compressor
19 m
46 m
65 m

---
Present Tunnel Layout
end
bunch
compressor
19 m
46 m
65 m
Last Changes:
Length of linac sections
  - 37 cell, 1.5 GHz TW linac
  - 132 cell, 3.0 GHz TW linac (internal load)
  - ~0.55 m between sections
Corrector coils
  - 36 horizontal correctors
  - 28 vertical correctors
Length of 30 MeV diagnostics
(originally not included)

---
Present Tunnel Layout
end
bunch
compressor
19 m
46 m
65 m
Strong solenoids needed
to cope with a
possible lower gradient
of the pulser
(A. Oppelt)
2.9 m

---
Present Tunnel Layout
end
bunch
compressor
19 m
46 m
65 m
Not finished:
250 MeV diagnostic section
  - base design on paper
  - length and specs pending

---
Previous Changes (1)
Cathode – Anode Geometry
simplified
original
flat cathode
less focusing

---
Previous Changes (2)
2-cell standing wave cavity
less focusing
reduced control over the
longitudinal bunch-shape
solenoid around coupler
limit to harmonic
field strength
pulser voltage
1.0 MV → 0.5 MV
solenoid after coupler
longer drift: 7.5 cm ► 12.5 cm ► 15.0 cm

---
Consequence of Changes:
Difficult solution for the required beam-optics:
1 MV pulser @ 250 MV/m
solution still OK
500 kV pulser @ 125 MV/m &
500 kV pulser @ 90 MV/m (modified cathode)
academic solution

---
Boundary Conditions
 for a High Brightness Accelerator
emittance compensation
specific beam waist
emittance evolution
velocity bunching
beam energy
length

---
1 MV pulser @ 250 MV/m
beam envelope:
shape of curve tuned by:
focusing (solenoids, RF, ..)
emittance:
shape of curve tuned by:
current density
need matching
at specific locations

---
Boundary Conditions
 for a High Brightness Accelerator
emittance compensation
specific beam waist
emittance evolution
CSR
beam waist
velocity bunching
beam energy
length
low emittance
tight window of permitted beam diameters

---
Approach
 for the PSI XFEL 250 MeV Injector
tune the beam optics to:
a solution, which is close enough to the optimum solution	(e-comp.)
still permits sufficient fine-tuning down-stream	(CSR)
1
2
Approach is restrictive to the beam diameter close to the gun

---
Solution Oct 2007, 1 MV pulser @ 250 MV/m

---
Solution March 2008: 500 kV @ 90 MV/m
Large !
difficulties
Focus too much:
emittance blowup due to over-focusing and space-charge
Focus too little:
emittance blowup due to non-linear focusing

---
Cause: Low Beam Energy after Pulser
Difficult to compensate divergence since the first main solenoid is far downstream
Suggest to increase the voltage of the pulser to 1 MV, such that the effect is smaller on the relative scale
(irrespective of gradient)

---
Coping with Lower Gradients
Pierce electrode
re-optimize
anode iris
to larger gap
Helps to match the electron beam to the 2-cell RF cavity
Still needs of pulsed solenoid behind the anode
OBLA
Pierce
Original

---
More Detailed Studies (Kevin Li)

---
Possible Solutions (Electron Source)
 subject to discussion
Present design with the pulser:
  - upgrade to 1 MV.
  - redesign of the anode/cathode geometry, based on a realistic gradient.
RF photo-cathode
  - 2.5 cell S-band (CERN design, available)
  - 1.5 cell S-band (copy of LCLS, SPARC, Elettra ......)
  - 1.5 cell 2-frequency (J-Y. Raguin)

---
Default Design & 1.5 cell, 2-frequency design
2.5 cell CERN gun
no change

---
identical solenoids INLB01-MSL10
Not Optimized !!
linac
3.7 m
2.5 cell CERN gun
no change
2.5 cell

---
1.5 Cell, 2-Frequency Gun

---
Source Specifications (Pulser)
500 kV
Source
    - Q	= 200 pC
    - I	= 5.5 A
    - R	= 0.30 mm
    - n	= 0.1 mm mrad
Pulser
    - G	= 90 - 125 MV/m
RF
    - 1.5 GHz:	40 MV/m
    - 4.5 GHz:	15 MV/m
1000 kV
Source
    - Q	= 200 pC
    - I	= 5.5 A
    - R	= 0.30 mm
    - n	= 0.1 mm mrad
Pulser
    - G	= 70 - 250 MV/m
RF
    - 1.5 GHz:	35 MV/m
    - 4.5 GHz:	15 MV/m

---
Source Specifications (RF Photo Cathode)
1F Cavity
Source
    - Q	= 200 pC
    - I	= 20 A
    - R	= 0.50 mm
    - n	= 0.2 mm mrad
Existing design
RF
    - 3.0 GHz:	100 MV/m
2F Cavity
Source
    - Q	= 200 pC
    - I	= 7.0 A
    - R	= 0.30 mm
    - n	= 0.1 mm mrad
Preliminary design
RF
    - 1.5 GHz:	60 MV/m
    - 4.5 GHz:	30 MV/m

---
thermal emittance
needs verification with
particle tracing code
high value caused by
velocity bunching

---
Pulser vs. RF Photo-Cathode
Pulser
large flexibility in beam manipulation
projected emittance relatively close to slice emittance
low thermal emittance
availability
(needs 1 MV)
stability ?
1F RF photo-cathode
availability
stability
projected emittance not too far from slice emittance
no field-emitters
thermal emittance (no velocity bunching)
2F RF photo-cathode
thermal emittance (velocity bunching)
longitudinal bunch-shape
no field-emitters
projected emittance
availability
stability ?
limited simulation results

---
Strategy under Consideration
Development of two injector designs, to be tested in WLHA in sequential order:
  - Intermediate emittance source, possibly with a charge up to 1 nC (for 10 – 1 nm FEL):
    - 2.5 Cell CERN gun?
  - Ultimate low-emittance gun
    - 1 MV pulser + 2 cell, 2-frequency cavity
      - - availability ?
      - - wakes < 30 MeV ?
    - 1.5 cell, 2-frequency cavity
      - - real performance analyses
      - - availability and design ?