SwissFEL Porthos, visions for the future
Thomas Schietinger :: Paul Scherrer Institut
Input from M. Calvi, S. Reiche, E. Prat
Pathways to high photon energy
Porthos Machine Working Group Meeting, 15 December 2020

---
Porthos requirements
- Gabriel Aeppli made it clear at the last SSB that Porthos must provide polarized light up to 12 keV
  - This requires a scaled APPLE-X undulator
  - Assumption is that the Athos undulator can be scaled to 20 mm period – to be verified! (Marco?)
- At the same time the majority of the photon science users ask for high photon flux at higher photon energies (at least 20 keV, better 25 keV)
  - A 20 mm APPLE-X cannot reach energies much above 12 keV.
  - We need a second undulator line to cover the high end of the photon energy spectrum.
  - It may profit from the first line as a subharmonic seed.
  - How to find the best undulator period / technology for the second line?

---
Machine design options
Original approach:
- Machine design pursues three main options, all based on a linac extension to reach 7 GeV electron energy in both Aramis and Porthos branches (S. Reiche and team):
  - APPLE-X undulator
  - HTS undulator
    technology
  - APPLE-X undulator
    with HTS afterburner

---
Electron beam parameters: E = 7 GeV, I = 2 kA,
Q = 200 pC, ε = 300 nm, σE = 1 MeV
2-stage configuration
E. Prat
Hybrid setup:
Hybrid configuration:
- Amplification of 3rd harmonic with second stage.
- Varying number of undulators in first stage (6, 7 and 8). For each configuration the field of the 2nd stage is optimized (to match the third harmonic).
- Observation: Fastest growth with 6 undulators in the first stage (black curve). In this case it takes 7 modules in the 2nd section to reach 1 GW – only two modules less than in the case of only 10 mm undulators (yellow curve)...
λu = 20 mm, K = 2.18 (6.9 keV)
“Athos” type
λu = 10 mm, K = 1.62 (20.6 keV)
“HTS” type
Ee = 7 GeV
Eγ = 20 keV
Harmonic lasing:
- Amplification of 3rd harmonic in same stage.
- For λu = 20 mm tuned to 6.9 keV photon energy (0.18 nm) for the fundamental (power curve not shown).
- NHL: non-linear harmonic lasing, no suppression of the fundamental.
- HL: harmonic lasing where the fundamental is suppressed with phase shifters (one phase shifter after every meter of undulator).
  12 random configurations tried, the best is shown.
- Observation: NHL grows faster but does not reach 0.1 GW, HL needs more space but can grow to ~0.5 GW in 90 m (80 m of effective undulator length).
z (m)

---
S. Reiche
Single-stage configuration
Electron beam parameters: E = 7 GeV, I = 2 kA,
Q = 200 pC, ε = 300 nm, σE = 1 MeV
- CHIC between undulators (75 cm every 4 m)
- Optical klystron effect not helping a lot (conservative assumption for energy spread)
- Saturation after 40 m (12.4 keV) or 80–90 m (20 keV).
- In the case of 20 keV no gain from harmonic lasing (saturation length, maximum power)
λu = 15 mm, K = 1–2.5
“Aramis” type

---
S. Reiche
Ming-Xie estimates for E = 7 GeV
Saturation power:
Saturation length:
• Dashed lines: with harmonic lasing (some potential
   for HTS 15 mm at very high photon energies!)
• Gain length does not include drifts (e.g. for CHIC)
   → effective length about 20% longer
Aramis now (with 6 GeV): 36 m, 4.5 GW at 12.4 keV

---
S. Reiche
Ming-Xie estimates for E = 8 GeV
Saturation power:
Saturation length:
• Dashed lines: with harmonic lasing (some potential
   for HTS 15 mm at very high photon energies!)
• Gain length does not include drifts (e.g. for CHIC)
   → effective length about 20% longer
Aramis now (with 6 GeV): 36 m, 4.5 GW at 12.4 keV

---
Undulator types
Photon energies 2–30 keV
(equal colors in all plots)
Max. HTS (4 mm gap)
Max. CPM (4 mm gap)
Max. HTS (4 mm gap)
Max. APPLE-X (4 mm gap)
Max. PM (3 mm gap)

---
Reaching high photon energies
Photon energies 2–30 keV
(equal colors in all plots)
Higher beam energy brings higher photon energies into reach.

---
Reaching high photon energies
Photon energies 2–30 keV
(equal colors in all plots)
- Higher beam energy brings higher photon energies into reach.
- Highest photon energy demand low K values, but we should not go below 1.2 (to avoid insufficient coupling of photons to electrons)

---
Reaching high photon energies
Photon energies 2–30 keV
(equal colors in all plots)
K0, a, b from J. Synchrotron Rad.(2018) 25, 686-705 (Aramis U15)
- Higher beam energy brings higher photon energies into reach.
- Highest photon energy demand low K values, but we should not go below 1.2 (to avoid insufficient coupling of photons to electrons)
- The choice of undulator period depends on the K values we can reach at a given period. This in turn depends on the gap we can operate at. Parameterization shown for Aramis U15 undulator.
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap

---
Cryogenic Permanent Magnet Undulator –
a possible compromise?
Courtesy M. Calvi

---
Reaching high photon energies
Photon energies 2–30 keV
(equal colors in all plots)
K0, a, b from J. Phys.: Conf. Series 425 (2013) 032017 (SLS CPMU)
- Higher beam energy brings higher photon energies into reach.
- Highest photon energy demand low K values, but we should not go below 1.2 (to avoid insufficient coupling of photons to electrons)
- The choice of undulator period depends on the K values we can reach at a given period. This in turn depends on the gap we can operate at. Parameterization shown for SLS U14 cryogenic undulator.
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap

---
Reaching high photon energies
Photon energies 2–30 keV
(equal colors in all plots)
K0, a, b from J. Synchrotron Rad.(2018) 25, 686-705 (Aramis U15)
✸
✸
✸







✸

✸

✸

✸

✸
- Higher beam energy brings higher photon energies into reach.
- Highest photon energy demand low K values, but we should not go below 1.2 (to avoid insufficient coupling of photons to electrons)
- The choice of undulator period depends on the K values we can reach at a given period. This in turn depends on the gap we can operate at. Parameterization shown for Aramis U15 undulator.
Possible choices of
undulator period (12–15 mm)
Target photon energies:
 20 keV
✸ 25 keV
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap

---
Reaching high photon energies
Photon energies 2–30 keV
(equal colors in all plots)
K0, a, b from J. Phys.: Conf. Series 425 (2013) 032017 (SLS CPMU)
✸
✸
✸







✸

✸

✸

✸

✸
- Higher beam energy brings higher photon energies into reach.
- Highest photon energy demand low K values, but we should not go below 1.2 (to avoid insufficient coupling of photons to electrons)
- The choice of undulator period depends on the K values we can reach at a given period. This in turn depends on the gap we can operate at. Parameterization shown for SLS U14 cryogenic undulator.
Possible choices of
undulator period (12–15 mm)
Target photon energies:
 20 keV
✸ 25 keV
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap
3 mm gap
3.5 mm gap
4 mm gap
4.5 mm gap
5 mm gap
6 mm gap
7 mm gap

---
Porthos switchyard: current situation
PSI drawing
No. 2R-393601 (2019)
S30CB13
S30CB14
Existing
RF stations

---
Porthos switchyard: linac-3 upgrade
PSI drawing
No. 2R-393601 (2019)
S30CB13
S30CB14
S30CB15
S30CB16

---
Porthos switchyard: beam separation
PSI drawing
No. 2R-393601 (2019)
S30CB13
S30CB14
S30CB15
S30CB16
Branch point (~2°)
Second deflection (~2°)
Separating
drift

---
Porthos switchyard: beam separation
PSI drawing
No. 2R-393601 (2019)
Resonant-kicker–septum
complex: min. 20 m?
S30CB13
S30CB14
S30CB15
S30CB16
Branch point (~2°)
Second deflection (~2°)
Separating
drift

---
Porthos undulator line: original provision
Original provision: 24 x 4.75 m = 114 m undulator line
Beam dump
(7 GeV)
PSI drawing
No. 2R-393601 (2019)

---
Porthos undulator line with C-band linac
SPOCB01
SPOCB02
SPOCB03
SPOCB04
80 m undulator line (example)
Porthos C-band linac: 6±1 GeV
Beam dump
(7 GeV)
PSI drawing
No. 2R-393601 (2019)

---
Porthos undulator line with X-band linac
SPOXB01–08
Porthos X-band linac: 6±2 GeV??
80 m undulator line (example)
Beam dump
(7 GeV)
• Klystron gallery?
• Beam dump specification?
PSI drawing
No. 2R-393601 (2019)

---
Possible decision matrix for upper management
40 m Apple-X 20 mm PM
40 m Apple-X 20 mm PM
+
40 m planar 13 mm (C)PM
Science potential: …
Science potential: …
6 GeV
Price tag: …
Price tag: …
Science potential: …
Science potential: …
7 GeV
Price tag: …
Price tag: …
Science potential: …
Science potential: …
8 GeV
Price tag: …
Price tag: …
Budget items independent of chosen solution:
Extra laser with building extension
Kicker-septum upgrades for three bunch operation
Experimental hall (building extension)
Minimal equipment for end stations

---
Additional material

---
S. Reiche
Ming-Xie studies for Eγ = 12.4 keV
Saturation power:
Saturation length:

---
S. Reiche
Ming-Xie studies for Eγ = 20.0 keV
Saturation power:
Saturation length: