SwissFEL Porthos, visions for the future
Thomas Schietinger, Martin Paraliev :: Paul Scherrer Institut
Porthos: kicker options
Porthos Machine Working Group Meeting, 15 December 2020

---
Kicker options I: no RK upgrade
- Assume that the first kicker remains the same, delivering a sine curve with 56 ns period.
- There are different ways to place the bunches along this sine curve, leading to different bunch spacings:
- Bunches placed on the zero crossing of the kicker voltage will suffer from voltage jitter.
- Swapping the bunches we can select which bunches profit from the highest stability (on-crest kicker voltage) – but this leads to weird septum designs and the need to remerge beams.
- Here’s an overview of the possible combinations and their implications / complications:
28 ns
14 ns
21 ns
AR
AT
PO
DA
0°
180°
360°
540°
90°
135°
405°

---
Bunch spacing / allocation
Bunch placement
at first kicker
Topology
Actual layout (schematic)
Kicker:
Half period &
nominal beam energy
Kicker:
Half period &
nominal beam energy
56 ns
@3 GeV
Status quo with four bunches, all on-crest
56 ns
@3 GeV
@3 GeV
56 ns
@6 GeV
@3 GeV
56 ns
@6 GeV
Additionally using zero crossings to go straight.
@3 GeV
@6 GeV
@3 GeV
@6 GeV
14 ns, swapped
@3 GeV
Additionally using zero crossings to go into the soft-X-ray branch
@3 GeV
@3 GeV
@3 GeV
@6 GeV
@6 GeV
Compromise:
one line on-crest, two lines close to on-crest (HXR), one line in the zero-crossing
@3 GeV
@3 GeV
42 ns
@6 GeV
42 ns
@6 GeV
21 ns, swapped
Compromise:
one line on-crest, two lines close to on-crest (SXR), one line in the zero-crossing
@3 GeV
42 ns
@6 GeV
@3 GeV
42 ns
@6 GeV
135°
405°
135°
405°

---
Evaluation (pulsed magnets, RF, other)
• Maximum stability for all bunches.
• 6 GeV kicker doable (twice stronger but twice lower frequency).
• New kicker and electronics need to be designed.
• Other diagnostics and (LLRF) control systems will not suffer.
• High (unacceptable?) loss of RF power at 84 ns separation.
• Maximum RF tunability, minimum wakefield effects.
• Doable from pulsed magnets point of
  view.
• Separating at 6 GeV will require (most
   likely) 4 more kickers identical to the
   existing ones – no new development
   needed.
• Other systems suffer (less separation).
• Minimal loss of RF power.
• Minimum RF tunability, maximum
   wakefield effects.
• Dual septum needs to be designed
  (feasible?).
• Poorest stability for AR and PO.
Additionally using zero crossings to go straight.
• Special septum that deflects the
  bunches at zero crossing while the
  others remain on straight orbit?
  (Feasible? Resonant kicker for
  remerging?)
14 ns, swapped
Additionally using zero crossings to go into the soft-X-ray branch
• 21 ns is a good compromise for all systems that need upgrading.
  (But may be difficult for laser systems...)
• Jitter induced by resonant kicker is reduced, but only by √2…
• Triple septum that can separate 4 different beams to be designed (feasible?).
• May have to involve dogleg in the separation (gradient septum? defocusing
  quad?) – space requirements to be evaluated.
• Semi-merge AR and PO (on two crossing trajectories), then separate them later
  with a thin septum (without kicker, to be designed…)?
• Swapped version to be preferred to have the highest-demand beam (PO) on crest
  (but poor stability for AR).
• Acceptable loss of RF power(?)
• Acceptable RF tunability, wakefield effects (?) ...to be evaluated!
Compromise:
one line on-crest, two lines close to on-crest (HXR), one line in the zero-crossing
21 ns, swapped
Compromise:
one line on-crest, two lines close to on-crest (SXR), one line in the zero-crossing
135°
405°
135°
405°

---
Kicker options II: with RK upgrade
Two possibilities to upgrade the kicker to avoid or mitigate the problems associated with shorter bunch separations:
- Faster oscillation
  - The emergence of GaN transistors means that
    higher voltages are now possible than 10 years
    ago (our current system is based on Si MOSFET
    and pushed that technology to the limit).
  - A faster kicker with the same active length will
    be challenging but should be possible (Martin).
- Addition of higher-harmonic oscillation
  - Can we create a two-resonance system with
    coupled resonators?
–
=

---
Topology
Actual layout (schematic)
Kicker:
Half period &
nominal beam energy
Kicker:
Half period &
nominal beam energy
56 ns
@3 GeV
56 ns
@3 GeV
@3 GeV
56 ns
@6 GeV
@3 GeV
56 ns
@6 GeV
21 ns, fast kicker
Status quo with four bunches, but faster kicker
42 ns
@3 GeV
42 ns
@3 GeV
@3 GeV
42 ns
@6 GeV
@3 GeV
42 ns
@6 GeV
14 ns, inflection
Using inflection points at zero crossings to go straight.
@3 GeV
+ high. harm.
@6 GeV
@3 GeV
+ high. harm.
@6 GeV

---
Evaluation (pulsed magnets, RF, other)
• Maximum stability for all bunches.
• 6 GeV kicker doable (twice stronger but twice lower frequency).
• New kicker and electronics need to be designed.
• Other diagnostics and (LLRF) control systems will not suffer.
• High (unacceptable?) loss of RF power at 84 ns separation.
• Maximum RF tunability, minimum wakefield effects.
• 21 ns is a good compromise for all systems that need upgrading. (Laser???)
• Maximum stability for all bunches
• Normal septa – we can keep the first as it is.
• No complications from remerging beams.
• Acceptable loss of RF power(?)
• Acceptable RF tunability, wakefield effects (?) ...to be evaluated!
21 ns, fast kicker
Status quo with four bunches, but faster kicker
• Good stability for all bunches
• Separating at 6 GeV will require (most likely) 4 more kickers identical to the
  existing ones – no new development needed.
• Other systems suffer (less separation).
• Minimal loss of RF power.
• Minimum RF tunability, maximum wakefield effects.
14 ns, inflection
Using inflection points at zero crossings to go straight.

---
21 ns bunch spacing – a problem for the laser?
Discussion about feasibility of 21 ns bunch spacing for laser systems (summarized by Martin):
- 21 ns spacing (or other separation that is not a multiple of 14 ns) is possible only if:
  - There is a separate laser for each beamline.
  - The timing and synchronization system is capable of reliably positioning the pulses at the required timing positions (including those of the other lasers) so the lasers could be easily interchangeable.
- Limitations and drawbacks:
  - In general one laser will not be able to simultaneously serve two or more arbitrary beamlines (loss of this backup solution).  It might be possible for bunches that are separated with multiples of 14 ns but this will increase system complexity and will require additional effort. (For example in case of 4 bunches separated with 21 ns theoretically one laser could serve simultaneously only 1st and 3rd or 2nd and 4th – separation between 1st and 3rd is 2x 21 ns = 42 ns = 3x 14 ns.)
  - We will lose the possibility to setup the timing by simply jump to next n-th laser train pulse keeping the exact RF phasing.
  - A second cathode transfer line is required. Combining 4 separate lasers in one transfer line will result in too large light losses. (Not specific to 21 ns spacing but common to all solutions with 4 separate lasers)