Simulations for the
4 MeV OBLA test stand
Kevin Li
ETH Zürich, CH-8092 Zürich, Switzerland
PSI, CH-5232 Villigen, Switzerland
Felsi Seminar
15. Juli 2008

---
Contents
Physics
  1. Target beam
  1. Sources form emittance growth
  1. Design 4 MeV test stand
Codes
Results
  1. Diode
  1. Matching section
  1. Velocity bunching

---
A compact X-FEL for Switzerland
We all know our ultimate goal:
an X-ray laser beam from
a compact source...

---
PSI-XFEL

---
A compact X-FEL for Switzerland
Nope...

---
PSI-XFEL
Okay... here we are!

---
Low emittance electron gun
Target parameters:
for the electron beam at the undulator:
- E	: 6 GeV
- s	: 0.1 mm mrad
- Q	: 220 pC
- I	: 1.5 kA
	- accelerator length	: 435 m
- undulator length	: 80 m
- other sections	: 265 m
- total length	: < 800 m
results in an output laser light of:
- 	: 1–100 Å
- B	: 0.01–1 × 1033 [U]
- f	: 10–100 Hz
- High energy, low emittance beams deliver short wavelength laser output
 only low emittance is compatible with a compact facility
Design parameters for a low emittance electron gun:
E	: 3.5 MeV
s	: 0.1 mm mrad
Q	: 220 pC
I	: 30 A
Linear longitudinal phase space

---
Sources for emittance growth
The phase space is an even-dimemsional manifold naturally endowed with a symplectic structure (i.e. volume 2-form)
The evolution of any vector in phase space is generated by a Hamiltonian vector field
 canonical flux
A conanical flux preserves the symplectic structure
 volume preserved
Dynamics is described by symplectic maps
The emittance is the mean area in phase space and is not necessarily preserved
Projected emittance: projection is not a symplectic map
 emittance increase
Slice emittance: nonlinear forces (space charge, external fields) lead to filamentation of the phase space
 emittance increase
Images courtesy of A. Streun: pempp

---
Design of a low emittance gun
Space charge induced emittance dilution dominated by perveance:
 combine low current with high gradient
Emittance dilution from external fields dominated by ratio of the diameter so the beam and of the surrounding cavity boundaries
 minimise beam diameter by adequate matching scheme
Low current prevents lasing in the undulator and reduces brightness of photon beam
 need to increase low current by aggressive bunch compression
 velocity bunching in the RF cavity
Bunch profile must not be changes at this early stage to enable further handling of the beam
 linearisation of the longitudinal phase space
 superposition of third harmonic mode in the RF cavity

---
Contents
Codes

---
“Numerical regions”
Matching section &
velocity bunching:
pulsed coil &
RF cavity
Diode
MSLs
E-Meter
Quads
Dipole
MAFIA:
space charge dominated region
 space charge model crucial
no approximations for space charge forces:
exacts solutions of Maxwell's equations
 Lienard-Wiechert potentials with user defined boundaries
GPT:
space charge forces suppressed
 space charge model less crucial
space charge forces solved on a grid in the rest frame  Poisson equation  after Lorentz transformation: exacts solutions of Maxwell's equations with retardation, but:
with identical velocity for all particles
without radiation terms

---
Additional codes
HOMDYN: Beam envelope tracker
space charge calculated in rest frame with subsequent Lorentz transformation
 retardation but no radiation terms
each slice reduced to a single point in phase space
 all transverse effects are linearised
 very fast tracking
Raistlin and Caramon (Twins from Dragonlance® Chronicles and Legends novels)
RAISTLIN (RAdial field Integration by Slice Tracking with LINear space charge)
written in C++
tracks a single slice  fast
space charge forces linear, external fields from SUPERFISH T7 maps
 evaluates contribution from nonlinear external fields to slice emittance increase
CARAMON (Charged Axisymmetric Radiofrequency Accelerated Macroparticles ON-axis)
written in GNU Octave
tracks single macroparticle beamlet on-axis  fast (for multi-dimensional parameter space scans for velocity bunching)
RF fields given analytically by the user
 independent on field maps
 synchronisation can be investigated by quick evaluation of different RF configurations (varying cell length, distance of peaks)

---
Contents
Results

---
Diode: 2D design

---
Diode: 2D design (500 kV also have 1 MV)
I: 5.5 A
For large gaps:
strongly diverging beam
 nonlinear transverse diode fields integrate to yield a net focusing that counteract space charge defocusing

---
Diode: 2D design (500 kV)
Choice for technical feasibility:
125 MV/m seems possible

---
Diode: 2D alternative
3.5 - 1.0 mm
for increased focusing

---
Diode: 2D alternative
Emittance compensation at an early stage improves emittance:
projected by factor 3
slice by factor 1.5

---
Diode: 3D design
beam offset
cathode offset

---
Diode: 3D beam offset
Insensitive up to 100 microns

---
Diode: 3D cathode offset
More sensitive but still tolerable up to 100 microns

---
MAFIA - GPT
Dump at 2 mm

---
Pulsed coil design

---
Pulsed coil: emittance oscillation
Homdyn
place booster cavity here!

---
Coil with cavity: beam matching
good matching obtained for
r = 0.500 mm
Emax = 33.0 MV/m
B = 0.250 T
transverse RF effects invisible

---
Compression: Two-frequency cavity
 Compression factor ~ 5

---
Compression: Two-frequency cavity
Caramon
fundamental: 36 MV/m, -39 degrees
all particles concentrated in head
 makes further beam handling very hard

---
Compression: Two-frequency cavity
Caramon
fundamental: 47 MV/m, - 40 degrees
harmonic: 10 MV/m, + 154 degrees
bunch profile symmetric

---
Compression: Two-frequency cavity
GPT
fundamental: 48 MV/m, - 36 degrees
harmonic: 14 MV/m, + 148 degrees
bunch profile symmetric

---
Momentum measurements
Measured
Deduced
Measured
Deduced
Simulation
%delta_i = (%delta p_i) over (%delta p_m)

---
Momentum measurements
Measured
Deduced
Measured
Deduced
Simulation
%delta_i = (%delta p_i) over (%delta p_m)
FEL-LK84-002-01

---
Conclusions
Physics
  1. Design done
Codes
  1. Codes implemented, prepared and ready to use
  1. Additional codes added
Results
  1. Usable set of parameters evaluated for achieving the target beam