## Slide 1: FCC-ee injector update & Positron source test at PSI
Paolo Craievich on behalf of the collaboration team :: Paul Scherrer Institut
SwissFEL Progress Meeting, 30th March 2021

## Slide 2: Outline
Introduction
    Motivations and Swiss CHART Funding
    FCC-ee Injector Complex Update Overview
Positron sources
  FCC-ee Injector parameters and overview of the positron sources
  Adiabatic Matching Devices
  Studies for FCC-ee
Positron source experiment at SwissFEL
    Transfer line and area for the experiment
    Experiment layout
    First simulation results
Conclusion and outlook

## Slide 3: Outline
Introduction
    Motivations and Swiss CHART Funding
    FCC-ee Injector Complex Update Overview
Positron sources
  FCC-ee Injector parameters and overview of the positron sources
  Adiabatic Matching Devices
  Studies for FCC-ee
Positron source experiment at SwissFEL
    Transfer line and area for the experiment
    Experiment layout
    First simulation results
Conclusion and outlook

## Slide 4: Motivations – just an attempt
First idea to involve PSI came up at FCC week in June 2019 (FCC project leader and GFA management)
  Cost estimate for the Injector Complex as in CDR0 published in 2018: PSI RF technology for RF guns and accelerating structures – PSI had some on-going collaborations
  Proposal to use a SC solenoid instead of a flux concentrator in the positron source. This approcah would also profit from synergies with the CHART activities on superconducting high-field magnets for FCC-hh.
  In addition using large acceptance S-band accelerating structures for the positron capture system
Kick–off meeting in October 2019
  Definition of the organizational structures and administrative aspects  proposal for CHART
  Proposal for a positron source at SwissFEL  synergy with the Porthos beamline (transfer line and beam dump)
End 2019, RF section in charge to write the proposal to be submitted to CHART II

## Slide 5: What is CHART?
Curtesy L. Rivkin
Chairman CHART-Council: Prof. Dr. Hans Rudolf Ott (ETH)
Chairman CHART Executive Board: Prof. Dr. Leonid Rivkin (PSI)
Coordinator CHART activities: Stefan Keller (PSI)
12 on-going projects funded by CHART-2, at PSI: HTS bulk undulator, MagDev1, FCC-ee Injector

## Slide 6: CHART proposal at a glance
The CHART council approved the proposal in June 2020 to finance the FCC-ee Injector update studies and the proof of principle experiment for a positron source at PSI/SwissFEL facility
  Collaboration between PSI and CERN with several external partners (IJCLab, INFN-LNF, BINP, KEK…)
  Duration 4 years (from September 2020) + to be considered 1 year extension 😅
  Goals:
    review of the actual CDR0/Injector and write a CDR+/Injector with cost estimate (published in 2018) – deadline end 2023
    Positron source at PSI/SwissFEL – deadline end 2024

## Slide 7: Introduction (FCC-ee Injector Complex Update)
Main Ring and booster ring (98 km) – 45 GeV
e-/e+ linac up to 6 GeV, 1.54 GeV Damping Ring
SPS as a Pre-Booster Ring (6 - 20GeV)
Booster Ring (20  45 GeV)
The main 6 GeV linac hosts the e+ source. The positrons are produced with 4.46 GeV e- beam
Baseline in CDR0/Injector
As alternative options for the FCC-ee Injector, a 20 GeV or a 40 GeV linacs are proposed to provide the direct injection into the main booster or main ring

## Slide 8: Work packages Overview
WP0. Coordination (PSI/CERN)
Task 0.1 Coordination
Task 0.2 Overall parameter optimization
WP1. e+/e- 6 GeV Injector Linacs
A. Grudiev (CERN)
WP2. Electron and positron Linac extension study (Linac 4)
J.-Y. Raguin (PSI)
WP3. Positron source: target and capture system
(IJCLAB/PSI)
I. Chaikovska (IJCLab)
WP4. Damping ring and transfer lines
C. Milardi (INFN/LNF)
WP5 CDR+, all partners
WP6. Proof of Principle positron source and capture in SwissFEL
R. Zennaro (PSI)
Addendum between CERN and PSI

## Slide 9: Layout of the injector 6 GeV (20GeV)
Outcome from WP0.2 meetings leading by A. Grudiev
S-band
S-band
Electron production
Positron production
C-band

## Slide 10: FCC-ee Injector Parameters
Charge both species 3.4 nC
Damping ring
The normalized emittances of the positrons produced by the source is of the order of 8000-10000mm  necessary a damping ring to reduce the emittances by orders of magnitude
Luminosity in e-e+ colliders is proportional to the bunch population and to the average flux of particles and inversely proportional to the interaction point beam sizes. A main limitation on the optimization of all these parameters is the positron source!

## Slide 11: Outline
Introduction
    Motivations and Swiss CHART Funding
    FCC-ee Injector Complex Update Overview
Positron sources
  Overview of the positron sources
  Adiabatic Matching Devices
  Studies for FCC-ee
Positron source experiment at SwissFEL
    Transfer line and area for the experiment
    Experiment layout
    First simulation results
Conclusion and outlook

## Slide 12: Overview of (some) Positron Sources
SLC (not in operation anymore) is the positron source model for existing and future colliders: DAFNE, KEKB, PEP-II, Beijing Tau-charm, SuperKEKB, FCC-ee, CLIC, ILC and LHeC
SuperKEKB has recently commissioned the upgraded injection system and has achieved a positron yield of 0.5 at 3.5 GeV (status of art of the positron source in operation)  assuming this as a baseline for FCC-ee positron source, this means we need an electron bunch of 6.8 nC to generate the positron!
 |  | SLC | LEP | KEKB | SKEKB | DAFNE
Type |  | Linear | Circ. | Circ. | Circ. | Circ.
Drive e- beam | GeV | 33 | 0.2 | 4.3 | 3.5 | 0.19
Charge | nC | 4.8-8 | 0.8-48 | 10 | 10 | 1.9
Rep. rate | Hz | 120 | 100 | 50x2 | 50x2 | 50
Beam power | kW | 20-30 | 1kW (max) | 4.3 | 3.5 | 18
Poistron yield |  | 1.1 | 0.003 | 0.1 | 0.4 | 0.016

## Slide 13: How the Adiabatic Matching Device (AMD) work
SLC positron source is based on a high current S-band e- linac with DC thermionic gun, a focusing triplet, a high-Z target and a capture system
The capture system:
RF structures and NC focusing solenoids
AMD
target
Electrons from the linac
Electrons hit a small portion of the High-Z target (i.e. tungsten or tungsten alloy)
Positrons are created through bremsstrahlung and following pair conversion
Small spatial and temporal distribution but large angular and energy distribution (shower process and multiple scattering)
Reduction of angular spread with strong axial magnetic field (AMD)
Magnetic field is adiabatically decreased (gradient)  divergence decrease
Matching to the aperture of the RF capture structure (physical limit for the transverse beam size)
2 options to be considered for the Adiabatic Matching Device (AMD): Flux concentrator (Pulsed magnet) and SC solenoid (new approach)

## Slide 14: Flux concetrator (Super KEKB Positron Source)
Courtesy of Y. Enomoto (SuperKEKB)

## Slide 15: Adiabatic Matching Devices: possible solutions
PSI approach is to use a SC AMD as alternative to the pulsed magnet flux concentrator
Courtesy of Pavel Martyshkin BINP
Elliptical cylinder 120x180 mm
Total length is 140 mm
Conical part length is 70 mm
Min cone diameter is 8 mm
Max cone diameter is 44 mm
Cone angle is ≈29 degrees
Cylindrical hole diameter is 70 mm
Coil has 13 turns
Peak field: 7 T
DC solenoid: 0.5-0.7 T
Field on target: ~3 T
Also studies for a 5 Tesla peak field
DC Solenoid: 0.5 T (uniform field)
Electrons or radiation
Target
Flux concentrator (FCCee)
HTS Solenoid
HTS: tape-shaped conductor
https://ieeexplore.ieee.org/document/7762812
Courtesy of Jaap Kosse and Bernhard Auchmann (PSI)
8 Coils
spacers
z
r

## Slide 16: Conventional and Hybrid schemes under investigation
Limitations (numbers to be verified):
Peak Energy Deposited Density (PEDD) for a Tungsten-Rhenium alloy (W74Re26) is 35 J/g
Target Heat Load (THL) is not higher than 15 kW
3) Rotating target, solution for CLIC, ILC and FCC-ee in case of bunch train

## Slide 17
Courtesy of I. Chaikovska and Y. Han (IJCLab)
Studies on the positron production (work in progress)
Electron beam energy 4.46 GeV (FCC-ee Injector baseline in CDR0)
  On going simulations…
We (Riccardo) is performing simulations considering a SC solenoids and new RF capture strcutures (more related to WP6) – following slides
CERN (Yongke) with support from IJCLab (Iryna) and PSI (Riccardo) is performing simulations for the Hybrid scheme

## Slide 18: Outline
Introduction
    Motivations and Swiss CHART Funding
    FCC-ee Injector Complex Update Overview
Positron sources
  FCC-ee Injector parameters and overview of the positron sources
  Adiabatic Matching Devices
  Studies for FCC-ee
Positron source experiment at SwissFEL
    Transfer line and area for the experiment
    Experiment layout
    First simulation results
Conclusion and outlook

## Slide 19: Transfer line to the positron source experiment
Transfer line at the linac end: The idea (from Sven) is to have a simple outcoupling and a double bend achromat layout to close the dispersion in the straight line. This solution is the least invasive to the main SwissFEL line, where only the first dipole is placed in the beamline in S30CB16.
8 QFM quadrupoles up to the target to change the beam size at the target itself
b-function 15m-150m
dipoles
S30CB13/14
quadrupoles
Courtesy of S. Reiche
target

## Slide 20
End of Linac 3
Area for the experiment
S30CB013
S-band mod.
Klystron gallery (upstairs)
30-40 m
S-band HV klystron modulator: a full S-band RF system is required, new modulator for the Injector (SF consolidation) and the old one will be used for the experiment/S-band test facility

## Slide 21: Experiment layout
Crystal in/out
Beam stopper
and permanent magnet
SC solenoid with embedded target
RF cavities and NC solenoids
SwissFEL 6 GeV electron beam
beam dump or beam stopper + beam dump? (huge e- energy distribution)
Radiation from the crystal
Spectrometer
electron beam
positron beam
electron beam
Diagnostic not defined yet (charge measurement)
Both e- and e+ have huge energy spread, beam dump design and shielding problems.
Option: operate with extremely low beam charge <<200 pC, <<100 Hz
Goal: have a comparative study between conventional and hybrid schemes and to test the SC solenoid
Courtesy of R. Zennaro

## Slide 22: S-band RF module (positron capture)
1400
150
40
89.7
50
3
Status:
RF design nearly ready (for b=2) (l/4 waveguide impedance matching missing)
mechanical design well advanced
“conventional PSI” brazing design (machining at VDL)
Ready for ordering the OFE copper
Phase shifter
Klystron 35 MW, 3.5 ms
HV modulator
Circulator
2x SW p-mode cavitiy (18MV/m@15MW for b=2)
25 cells max., 2998.5 MHz, Q= 21000
b to be defined, in this example 2
R/Q=939 (for b=2)
mode separation 3.8 MHz
Courtesy of R. Zennaro

## Slide 23: Preliminary simulation results
9+52 SW 3 GHz cavities 18 MV/m, 1st and 2nd AS @-30°
7 T peak field for the SC solenoids (5.6 T at target)
26% e+ in the FCC-ee DR longitudinal acceptance (±3.8% dE/E, ±8.9 mm in z-position)
 Total Positron Yield 13.8*0.26= 3.6 ✓
e+ distribution at target (Geant4, courtesy of I. Chaikovska);
Positron Yield at target = 13.8 e+/e- with tungsten target-converter 5X0 (~ 1.75 cm);
Conventional scheme (electrons directly hint the target);
e- energy = 6 GeV;
Bunch length (rms) = 1 mm
Beam divergence (rms) = 1e-5;
Energy spread (rms) = 1e-3;
Beam size on target (rms) = 1.5 mm;
Codes: Astra up to 200 MeV, LiTrack up to 1.5 GeV (just to estimate the positron yield at the DR injection)
Goal: validation of the SC solenoid and S-band SW cavities (both under development at PSI)
Courtesy of R. Zennaro

## Slide 24: Positron distributions at target and “transmission”
e+ at the target output face:
Total e+ distribution
Only e+ that will reach the capture linac output (200 MeV)
X distribution
12 mm
Xp distribution
3 rad
pz distribution
100 MeV
20 MeV
Courtesy of R. Zennaro
 1/3 ot the total positrons created at the target reach the linac end. The particles are cut by the iris of the first RF structure and the divergence remains high ( DR necessary)

## Slide 25: e+/e- separation by spectrometer
Spectrometer:
0.2 T; 0.5 m(z) X 0.6 m (x);
gap = 0.1 m
e+
e-
e+
e-
Diagnostic in vacuum or in air? Scintillation fiber?
Special faraday cup?
2.7 m
40 MeV
Spatial separation
Energy separation
Courtesy of R. Zennaro
X [mm]
y [mm]
z [m]
z [m]
0
4.5
0
4.5
-500
15
0
Just an example (not optimized)

## Slide 26: Where are we now? And wehere are we going?
Detailed list with hardware: RF structures, SC and solenoids, beam stopper, diagnostic, support girder… the shopping list
Update the time scheduling based on the procurements of the components and integration in SwissFEL (compatibility with SF operation and SLS-2 project)
Radiation environment studies  impact on SF (…and on SC solenoid)
  Simulation/evaluation of the radiation environment
  Target area shielding
  Energy deposition simulation (average and PEDD) for 6 GeV e- drive beam (target, AMD, acc. structures) => reliability and specifications
Experts have to be already involved in this phase:
  Beam dynamics, Magnet group, Electron instrumentation – photon diagnostic for the hybrid scheme, Target, beamline und simulations (8140), CERN experts can support us on this point
We are hiring two staff members: Accelerator physicist/RF engineer and magnet expert (SC solenoid), a PhD student also starts soon (hopefully)

## Slide 27: Outline
Introduction
    Motivations and Swiss CHART Funding
    FCC-ee Injector Complex Update Overview
Positron sources
  FCC-ee Injector parameters and overview of the positron sources
  Adiabatic Matching Devices
  Studies for FCC-ee
Positron source experiment at SwissFEL
    Transfer line and area for the experiment
    Experiment layout
    First simulation results
Conclusion and outlook

## Slide 28: Conclusion and outlook
I gave you the motivations for this project at PSI
    Question: are the motivations still valid?
FCC-ee Injector Complex Update
  Big efforts in coordination of the WPs (linacs design, DR, transfer lines and positron source development), even more to draft the CDR+ with the cost estimate
Positron sources
    Basically still an interesting and challenging work to do on this topic
Positron source experiment at SwissFEL
  It is not a demonstrator for the FCC-ee positron source (lower charge and repetition rate)
  But it will be a test bench for the conventional and hybrid schemes using a SC solenoid, mainly for the positron yield (and maybe for the positron beam quality as well)
  Really promising results from Riccardo’s simulations (good agreement with CERN’s results)

## Slide 29: Credits
The ideas/outcomes presented in this contribution has been carried out in the last months/year. An acknowledgment goes to all the colleagues who contribute to it: I hope, cited in a right way here and in the talk
R. Zennaro, J.-Y. Raguin, M. Pedrozzi, H. Braun, S. Sanfilippo, B. Auchmann, J. Kosse, S. Reiche, E. Ferrari – PSI
I. Chaikovska, A. Faus-Golfe – IJCLab
A. Grudiev, F. Zimmermann, S. Ogur, M. Benedikt, S. Gilardoni, A. Latina, S. Doebert, T. Gilles, A. Lechner, P. Hilser, Y. Zhao, T. Brezina, H. Pommerenke – CERN
K. Oide, Y. Enomoto, K. Furukawa – KEK
P. Martyshkin – BINP
C. Milardi, O. Blanco, A, De Santis – INFN-LNF
L. Bandiera, M. Soldani, A. Sytov – INFN Ferrara
B. Dalena, A. Chance - CEA

## Slide 30: Wir schaffen Wissen – heute für morgen
Thank you for the attention!
Any questions?