## Slide 1: SwissFEL/Porthos energy linac upgrades (first thoughts)
Paolo Craievich et al. :: RF section :: Paul Scherrer Institut
Porthos meeting, 22 Jan 2021

## Slide 2: Locations considered for an energy linac upgrade
End of Linac 3
Porthos Linac (only in the Porthos beamline)
Injector

## Slide 3: Linac 3 energy upgrade
Extension Linac 3 klystron gallery
Option C.2: 10-12 structures with 1 klystron with 2 structures, 5-6 klystrons  875-1050 MeV (20-24m) – same consideration on the available space into the tunnel
Option X.3: 5 klystrons with 4 cavities per module  1 GeV (16 m)
Actual klystron gallery (no change)
Final consideration will depend on the available space in the bunker!! We can change the number of structures for klystron.
We have space for 3 additional HV modulators in the klystron gallery
Option C.1: 2-3 C-band klystrons (actual C-band module)  500-750 MeV – limited by the available space in the tunnel
Option X.1: 3 X-band klystrons with 4 cavities per module  600 MeV – High gradient
Option X.2: 3 klystron with 8 cavities instead of 4 (~850 MeV) – Low gradient - complex waveguide network – to be checked the space into the tunnel

## Slide 4: New Porthos Linac
First question: What is the space available? 30 m (transfer line) + 30 m before undulators?
New service area (HV modulators, power supplies, etc…) is necessary
Linac up to 2 GeV (only Porthos Linac), we can easily scale to 1 GeV:
  Option P.1: C-band, 1 klystron, 4 structures, 8 RF modules (31.5 MV/m), 64 m – (actual SwissFEL linac)
  Option P.2: C-band, 1 klystron, 2 structures, ~11 RF modules (44 MV/m), 44 m
  Option P.3: X-band: 1 klystron, 4 structures, 10 RF modules (62 MV/m), 32 m
We can have different configurations with energy between 1 GeV and 2 GeV
Cost estimate for RF systems is on-going

## Slide 5: Energy upgrade at the Injector
For each option the energy gain reduction due to the RF tuning for 4-bunches has to be estimated
SINSB05:
  1 C-band SF module 240 MeV, bunch compression at 540 MeV – to be check the space into the tunnel (+240 MeV)
  1 S-band FERMI module (RF pulse compressor) ~200 MeV, bunch compression at 500 MeV (+ 200 MeV)
SINSB03-04 with FERMI module and RF pulse compressor: +200 MeV
New C-band injector, 3 RF module, bunch compression at ~<700 MeV – also new RF gun, +400 MeV, similar situation in S-band frequency considering the upgrade of SINSB03-04-05
  To be checked the bunch compression, linearization and BC1 magnets
 S-band RF structures + BOC is simpler and less cost effective solution to have ~400 MeV more energy at the injector