SwissFEL Porthos, visions for the future
Thomas Schietinger :: Paul Scherrer Institut
Outline of a Porthos baseline concept
Porthos Machine Working Group Meeting, 19 February 2021

---
Machine choices
Three major choices to be made:
Repetition rate and bunch separation
  - RF energy losses mandate a shorter bunch spacing (than the current 28 ns).
  - Baseline concept: shorten bunch spacing to 21 ns with a faster kicker (from 56 ns to 42 ns period).
  - Alternative option: 14 ns bunch spacing using zero-crossings in 56 ns kicker period (only for 3 bunches?).
Electron beam energy (linac upgrade)
  - Baseline concept: upgrade to 7 GeV by adding 3 more C-band stations.
  - Further upgrade, e.g. with an X-band Porthos linac, to 8 or 9 GeV very attractive but will require building extensions and therefore probably too expensive (Porthos upgrade?).
Undulator type and configuration
  - Interundulator chicanes are a given (CHIC concept).
  - Hybrid undulator concepts found to be not attractive.
  - Two competing undulator concepts: pure Apple-X undulator (baseline) or planar undulator with phase retarder to enable some polarization control.

---
Resonant kicker upgrade

---
Kicker upgrade options:
Two possibilities to upgrade the kicker to avoid or mitigate the problems associated with shorter bunch separations:
- Faster oscillation
  - The emergence of GaN transistors means that
    higher voltages are now possible than 10 years
    ago (our current system is based on Si MOSFET
    and pushed that technology to the limit).
  - A faster kicker with the same active length will
    be challenging but should be possible (Martin).
- Addition of higher-harmonic oscillation
  - Can we create a two-resonance system with
    coupled resonators?
21 ns
28 ns
14 ns
14 ns
–
=
0°
180°
360°
540°
AR
AT
PO
DA
AR
AT
PO
DA
0°
180°
360°
540°
AT
AR
DA
PO
90°
AT
AR
DA
PO
90°

---
Bunch spacing / allocation
Bunch placement
at first kicker
Topology
Actual layout (schematic)
Kicker:
Half period &
nominal beam energy
Kicker:
Half period &
nominal beam energy
DA
28 ns
28 ns
DA
AT
56 ns
@3 GeV
Status quo with four bunches, all on-crest
AT
56 ns
@3 GeV
AR
AR
28 ns
@3 GeV
56 ns
@6 GeV
28 ns
@3 GeV
PO
56 ns
@6 GeV
PO
DA
21 ns, fast kicker
21 ns
DA
AT
Status quo with four bunches, but faster kicker
42 ns
@3 GeV
AT
42 ns
@3 GeV
AR
AR
21 ns
@3 GeV
42 ns
@6 GeV
21 ns
@3 GeV
PO
42 ns
@6 GeV
PO
14 ns, inflection
DA
14 ns
DA
AR
AT
Using inflection points at zero crossings to go straight.
AR
28 ns
@3 GeV
+ high. harm.
28 ns
@6 GeV
PO
AT
28 ns
@3 GeV
+ high. harm.
28 ns
@6 GeV
PO
0°
180°
360°
540°
AR
AT
PO
DA
AT
AR
DA
PO
90°
AR
AT
PO
DA
0°
180°
360°
540°

---
Bunch spacing / allocation
Bunch placement
at first kicker
Evaluation (pulsed magnets, RF, other)
• Maximum stability for all bunches.
• 6 GeV kicker doable (twice stronger but twice lower frequency).
• New kicker and electronics need to be designed.
• Other diagnostics and (LLRF) control systems will not suffer.
• Unacceptable loss of RF power at 84 ns separation.
• Maximum RF tunability, minimum wakefield effects.
28 ns
28 ns
Status quo with four bunches, all on-crest
• 21 ns is a good compromise for all systems that need upgrading. (Gun laser...)
• Maximum stability for all bunches
• Normal septa – we can keep the first as it is.
• Acceptable loss of RF power(?)
• Acceptable RF tunability, wakefield effects (?) ...to be evaluated!
21 ns, fast kicker
21 ns
Status quo with four bunches, but faster kicker
• In principle good stability for all bunches
• Three-way Lambertson may be difficult to realize!
• Separating at 6 GeV will require (most likely) 4 more kickers identical to the
  existing ones – no new development needed.
• Minimal loss of RF power.
• But: minimum RF tunability, maximum wakefield effects, other systems suffer.
14 ns, inflection
14 ns
Using inflection points at zero crossings to go straight.
0°
180°
360°
540°
AR
AT
PO
DA
AT
AR
DA
PO
90°
AR
AT
PO
DA
0°
180°
360°
540°

---
Feedback 14 ns vs. 21 ns bunch spacing
Assuming that the decision for the bunch spacing will be between 14 ns and 21 ns, the system responses so far are:
RF/LLRF (Z. Geng, P. Craievich):
  - Higher energy loss at 21 ns (presentation Qiao, 27 October 2020). Example C-band loss: 129 MeV (21 ns) vs. 73 MeV (14 ns) (compare to 200 MeV at 28 ns).
  - Tuning range (RF step) considerably reduced at 14 ns (e.g. S-band phase: ±0.5° versus ±0.2°)
  - Higher wakefield effects at 14 ns (no quantitative estimate yet).
Laser (A. Trisorio):
  - In general preference for multiples of 14 ns for the bunch spacing.
  - 21 ns is possible, but requires a separate laser for each beam line (one laser will not be able to serve two or more arbitrary beam lines).
Resonant kicker (M. Paraliev): both cases require some technological development. Beyond that:
  - 21 ns: can use existing beam topology (incl. Lambertson, septum)
  - 14 ns: three-way Lambertson/septum needed – how to remerge the beams? Many uncertainties.
Diagnostics (except BPMs) (R. Ischebeck):
  - Difference is only relevant for detectors that actually have a time constant in that range.
  - Readout challenges to be discussed with AEK – Porthos would represent a good opportunity to overhaul all our readout electronics (the designs date back to 2010). Clearly 14 ns will be more challenging than 21 ns.
BPM (B. Keil):
  - No quantitative statements possible without considerable work (and specifications)
  - Qualititative estimate: at 21 ns there is a chance to re-use the existing hardware, at 14 ns we will most likely
    need to replace the hardware (where bunch seperation is needed).
Timing & Synchronization (C. Sydlo):
  - The bunch spacing makes no difference.
  - In principle, once we have a digital laser lock (end of 2021), the timing can be set with almost arbitrary precision (0.1 fs).
  - For some systems, spacing given by the rep. rate of the amplification chain (typically 7 ns)

---
Feedback 14 ns vs. 21 ns bunch spacing
Assuming that the decision for the bunch spacing will be between 14 ns and 21 ns, the system responses so far are:
RF/LLRF (Z. Geng, P. Craievich):
  - Higher energy loss at 21 ns (presentation Qiao, 27 October 2020). Example C-band loss: 129 MeV (21 ns) vs. 73 MeV (14 ns) (compare to 200 MeV at 28 ns).
  - Tuning range (RF step) considerably reduced at 14 ns (e.g. S-band phase: ±0.5° versus ±0.2°)
  - Higher wakefield effects at 14 ns (no quantitative estimate yet).
Laser (A. Trisorio):
  - In general preference for multiples of 14 ns for the bunch spacing.
  - 21 ns is possible, but requires a separate laser for each beam line (one laser will not be able to serve two or more arbitrary beam lines).
Resonant kicker (M. Paraliev): both cases require some technological development. Beyond that:
  - 21 ns: can use existing beam topology (incl. Lambertson, septum)
  - 14 ns: three-way Lambertson/septum needed – how to remerge the beams? Many uncertainties.
Diagnostics (except BPMs) (R. Ischebeck):
  - Difference is only relevant for detectors that actually have a time constant in that range.
  - Readout challenges to be discussed with AEK – Porthos would represent a good opportunity to overhaul all our readout electronics (the designs date back to 2010). Clearly 14 ns will be more challenging than 21 ns.
BPM (B. Keil):
  - No quantitative statements possible without considerable work (and specifications)
  - Qualititative estimate: at 21 ns there is a chance to re-use the existing hardware, at 14 ns we will most likely
    need to replace the hardware (where bunch seperation is needed).
Timing & Synchronization (C. Sydlo):
  - The bunch spacing makes no difference.
  - In principle, once we have a digital laser lock (end of 2021), the timing can be set with almost arbitrary precision (0.1 fs).
  - For some systems, spacing given by the rep. rate of the amplification chain (typically 7 ns)
→ Overall preference for
    21 ns bunch spacing

---
Linac upgrade

---
Porthos switchyard: current situation
PSI drawing
No. 2R-393601 (2019)
S30CB13
S30CB14
Existing
RF stations

---
Porthos switchyard: beam separation
PSI drawing
No. 2R-393601 (2019)
Resonant-kicker–septum
complex
S30CB13
Branch point (~2°)
Second deflection (~2°)
Separating
drift

---
Three additional C-band stations
PSI drawing
No. 2R-393601 (2019)
Resonant-kicker–septum
complex
S30CB13
S30CB14
SPOCB01
SPOCB02
Branch point (~2°)
Second deflection (~2°)
Separating
drift

---
Three additional C-band stations
PSI drawing
No. 2R-393601 (2019)
Resonant-kicker–septum
complex
S30CB13
S30CB14
SPOCB01
SPOCB02
Branch point (~2°)
Second deflection (~2°)
Separating
drift
Additional 3 C-band stations (3 × 250 MeV)
Increased gradient in existing C-band stations
(100 MeV? What about dark current?)
Injector upgrade (150 MeV?)
...may realistically give total beam energy of 7 GeV

---
Undulator design

---
Undulator concepts
Simultaneous desire for high photon energy and polarization control can be satisfied by different concepts (none of which is entirely convincing):
Pro
Con
Concept

Planar undulator followed by a helical afterburner
• Difficult to tune two undulator segments
• Only partial polarization (60–70%) can be
  achieved, polarization must be measured.
• Limited flexibility (special modes).
• Simple and cost effective.
• Difficult to tune two undulator segments
• Only little gain from subharmonic preamplifier
  → you end up building two undulator lines capable of full
        saturation (expensive and inefficient)
• No gain from going to smaller period
   (coherence loss)

Apple-X followed by a planar high-energy afterburner
• Limited, efficient use of Apple-X
  (cost, mechanics,..).
• Afterburner can be optimized for
  highest photon energies.
• Polarization control up to highest
  energies – maximum flexibility
  (but also a bit of an overkill...)
• Single undulator series
• Expensive solution (many Apple-X modules)
• Cannot easily reach highest photon energies
  (with 15 mm period)
 • Challenging mechanics/controls.
Apple-X undulator

• Best quality beam for high-energy
  photon beams while still allowing
  for some polarization studies.
• Polarization is generated close to
  experiments.
• Single undulator series, mechanically straightforward.
• Insufficient flexibility for complex experiments.
Planar or helical und., polarization with phase retarder


---
Electron beam parameters: E = 7 GeV, I = 2 kA,
Q = 200 pC, ε = 300 nm, σE = 1 MeV
2-stage configuration
E. Prat
Hybrid setup:
Hybrid configuration:
- Amplification of 3rd harmonic with second stage.
- Varying number of undulators in first stage (6, 7 and 8). For each configuration the field of the 2nd stage is optimized (to match the third harmonic).
- Observation: Fastest growth with 6 undulators in the first stage (black curve). In this case it takes 7 modules in the 2nd section to reach 1 GW – only two modules less than in the case of only 10 mm undulators (yellow curve)...
λu = 20 mm, K = 2.18 (6.9 keV)
“Athos” type
λu = 10 mm, K = 1.62 (20.6 keV)
“HTS” type
Ee = 7 GeV
Eγ = 20 keV
Harmonic lasing:
- Amplification of 3rd harmonic in same stage.
- For λu = 20 mm tuned to 6.9 keV photon energy (0.18 nm) for the fundamental (power curve not shown).
- NHL: non-linear harmonic lasing, no suppression of the fundamental.
- HL: harmonic lasing where the fundamental is suppressed with phase shifters (one phase shifter after every meter of undulator).
  12 random configurations tried, the best is shown.
- Observation: NHL grows faster but does not reach 0.1 GW, HL needs more space but can grow to ~0.5 GW in 90 m (80 m of effective undulator length).
z (m)

---
Arguments pro and contra phase retarder
Arguments favoring a phase retarder solution (mostly from E. Ferrari):
- Cost: fixed polarization undulators are much less expensive than variable polarization ones
- Field quality: can be made much better with fixed polarization
- Mechanical simplicity: no need for complex undulator movements prone to failure when doing dichroism experiments
- Gap control: we will most likely run at a fixed (maximum?) K anyway and may even go to fixed-gap undulators.
- Polarization losses due to transmission to the beamline: even with a circularly polarized source, at the end you end up with ellipitically polarized light at the experiment (LCLS-II went for vertically polarized undulators for hard X-rays to benefit from the better transmission to the beamlines).
Arguments against a phase retarder solution (favoring a hybrid solution instead) (mostly from G. Aeppli):
- Insufficient flexibility: phase retarders quickly reach a limit when it comes to broad-band mode, sub-femtosecond pulses etc., needed for complex experiments.
  - In particular bandwidth is a big limitation (but efficiency increases when operating in high-brightness mode or after a monochromator)
- Full polarization control is only needed up to 10 keV – for higher energies can still use a fixed-polarization afterburner or...
- ...in the long run, we could have one hard-X-ray line focusing on high photon energies with linear polarization for biology, chemistry and imaging, and a second one limited to 12 keV with fancier options (polarized light, CHIC) used for “physics” – but in this case, Aramis should cover the high energies → complete linac overhaul?

---
Ming Xie estimates (planar, fixed energy)
- Ming-Xie parameterization for saturation length/power (Proc. PAC’95, p.183–185)
- Photon energy given by FEL resonance condition
- Coherence parameter (Saldin, Schneidmiller, Yurkov, Opt. Commun. 281 (2009) 1179)
          We want ζ ≥ 0.7.
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
Ming Xie estimates (planar, fixed energy)
- Ming-Xie parameterization for saturation length/power (Proc. PAC’95, p.183–185)
- Photon energy given by FEL resonance condition
- Coherence parameter (Saldin, Schneidmiller, Yurkov, Opt. Commun. 281 (2009) 1179)
          We want ζ ≥ 0.7.
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15,
M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)
To be evaluated the smallest gap we can aim for (losses, wakefields,...)

---
Ming Xie estimates (planar, fixed energy)
- Ming-Xie parameterization for saturation length/power (Proc. PAC’95, p.183–185)
- Photon energy given by FEL resonance condition
- Coherence parameter (Saldin, Schneidmiller, Yurkov, Opt. Commun. 281 (2009) 1179)
          We want ζ ≥ 0.7.
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
cryogenic permanent magnet
(example SLS cryo U14,
M. Calvi et al., J. Phys.: Conf. Series 425 (2013) 032017)
To be evaluated the smallest gap we can aim for (losses, wakefields,...)

---
Ming Xie estimates (planar, fixed energy)
- Ming-Xie parameterization for saturation length/power (Proc. PAC’95, p.183–185)
- Photon energy given by FEL resonance condition
- Coherence parameter (Saldin, Schneidmiller, Yurkov, Opt. Commun. 281 (2009) 1179)
          We want ζ ≥ 0.7.
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator vs. gap:
superconducting undulator
(simulation data, M. Calvi, privat communication)
To be evaluated the smallest gap we can aim for (losses, wakefields,...)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
   – i.e. at 7 GeV, 300 nm, no point in going to
      10 mm undulator period!
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
permanent magnet
(example Aramis U15, M. Calvi et al., J. Synchrotron Rad.(2018) 25, 686-705)

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy!
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy!
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy!
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy, or
   – further reducing the emittance
Electron beam parameters:
I = 2 kA, ε = 200 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy, or
   – further reducing the emittance
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy, or
   – further reducing the emittance
Electron beam parameters:
I = 2 kA, ε = 400 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy, or
   – further reducing the emittance
- The effect of energy spread is relatively small.
  (Only affects saturation length, no effect on coherence.)
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 0 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy, or
   – further reducing the emittance
- The effect of energy spread is relatively small.
  (Only affects saturation length, no effect on coherence.)
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
The path to higher photon energies
- Let’s assume 7 GeV beam energy available and permanent magnet undulators.
- Our parameter space is limited by three boundaries, given by:
   – available undulator space (saturation length)
   – loss of coherence
   – achievable undulator strength (K at minimal gap)
- Higher photon energies call for:
   – smaller undulator period
   – smaller K values
- The main obstacle towards higher photon energies
  is the loss of coherence!
- The only ways to reach higher photon energies are by:
   – increasing the beam energy, or
   – further reducing the emittance
- The effect of energy spread is relatively small.
  (Only affects saturation length, no effect on coherence.)
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 2 MeV, β = 10 m

---
The case for high K
S. Reiche
To reach high photon energy at a given (maximum) electron energy, you have to aim for low K values.
Nevertheless, it makes sense to aim for large K values:
At a given wavelength and undulator period, the FEL power increases significantly with higher K value.
  - But this means the electron energy has to increase accordingly!
  - If the electron energy is limited, can only profit at longer wavelengths.
1. If both K and E are higher, the relative energy spread σE/E is smaller, the beam can be compressed more (higher peak current), giving even more power.
2. High K values provide a large tuning range for two-color operation!

---
Cryogenic Apple-X with 15 mm period
– a good compromise?
- Can cover 10–20 keV (with polarization control!) at 7 GeV beam energy under the assumption of 300 nm emittance and K values analogous to the SLS cryo U14.
- Lower energies easily accessible with lower photon energies (very low energies may require coordination with Aramis).
- But is it feasible?
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
cryogenic permanent magnet (example SLS cryo U14, M. Calvi et al., J. Phys.: Conf. Series 425 (2013) 032017)

---
Cryogenic Apple-X with 15 mm period
– a good compromise?
- Can cover 10–20 keV (with polarization control!) at 7 GeV beam energy under the assumption of 300 nm emittance and K values analogous to the SLS cryo U14.
- Lower energies easily accessible with lower photon energies (very low energies may require coordination with Aramis).
- But is it feasible?
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m
Undulator K vs. gap:
cryogenic permanent magnet (example SLS cryo U14, M. Calvi et al., J. Phys.: Conf. Series 425 (2013) 032017)

---
Cryogenic Apple-X with 15 mm period
– a good compromise?
- Can cover 10–20 keV (with polarization control!) at 7 GeV beam energy under the assumption of 300 nm emittance and K values analogous to the SLS cryo U14.
- Lower energies easily accessible with lower photon energies (very low energies may require coordination with Aramis).
- But is it feasible?
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
Cryogenic Apple-X with 15 mm period
– a good compromise?
- Can cover 10–20 keV (with polarization control!) at 7 GeV beam energy under the assumption of 300 nm emittance and K values analogous to the SLS cryo U14.
- Lower energies easily accessible with lower photon energies (very low energies may require coordination with Aramis).
- But is it feasible?
Electron beam parameters:
I = 2 kA, ε = 300 nm, σE = 1 MeV, β = 10 m

---
Apple-X 15–20 mm period, calculations
Marco Calvi
- Magnetic calculations by M. Calvi show that for an Apple-X the K values cannot be made quite as high as was achieved for Aramis U15 (room temperature permanent magnet) or SLS U14 (cryogenic permanent magnet), but still competitive…
- Maximum K (at 3 mm gap) would be about 1.35 at room temperature, 1.75 at cryogenic temperature.
- No full parameterization for K(gap) available yet.
- To be pursued in more detail.
gap (g)
2.1 mm
>20 mm
2.1 mm
2.5
K = 2.0
1.5
K = 2.00
2.50
1.50
2.25
1.75
2.75

---
Apple-X 15–20 mm period, calculations
Marco Calvi
- Magnetic calculations by M. Calvi show that for an Apple-X the K values cannot be made quite as high as was achieved for Aramis U15 (room temperature permanent magnet) or SLS U14 (cryogenic permanent magnet), but still competitive…
- Maximum K (at 3 mm gap) would be about 1.35 at room temperature, 1.75 at cryogenic temperature.
- No full parameterization for K(gap) available yet.
- To be pursued in more detail.
gap (g)
2.1 mm
>20 mm
2.1 mm
1.5
1.50
1.75
2.75
2.5
K = 2.0
K = 2.00
2.50
2.25

---
Porthos undulator line: original provision
Original provision: 24 × 4.75 m = 114 m undulator line
Beam dump
(7 GeV)
PSI drawing
No. 2R-393601 (2019)

---
Porthos undulator line: possible configuration
Space for future Porthos linac
(e.g. X-band) or
beam manipulation devices
20 × (3+1) m undulator modules
≈100 m undulator line
(total,with large chicane)
Beam dump
(7 GeV)
PSI drawing
No. 2R-393601 (2019)

---
OSFA building extension
Ivo Widmer & A. Gottstein
- First estimate making maximum use of space reserve.
- Additional building volume of 23’300 m3 (about 35% of existing OSFA!)
- First cost estimate is
  35–40 MCHF.
- Careful: building costs cannot be changed later!

---
Very first, very rough budget estimate
- Machine:
  - Undulators: 20 3-m Apple-X modules à 1 MCHF, add 100 kCHF each for cryogenics and interundulator stuff: 20 × 1.2 MCHF = 24 MCHF
  - Cryogenic plant for undulators: 2 MCHF
  - New gun laser lab (incl. building extension): 6 MCHF
  - Kicker upgrade and new kicker hardware: 2 MCHF
  - Diagnostics upgrades for dealing with 21 ns bunch spacing: 2 MCHF
  - RF upgrade (3 C-band stations, injector upgrades): 9 MCHF
  - Electron beamline components (vacuum, diagnostics etc.): 5 MCHF
  - Machine total: 50 MCHF
- Front end and photon beam transport (optics, monochromators, diagnostics etc.): 10 MCHF(?)
- End stations: 10–15 MCHF per station – start with 1–2 stations? → 20 MCHF
- IT & controls (general system upgrades and extensions): 5 MCHF
- Building extension: 35–40 MCHF first estimate → 40 MCHF
→ Porthos total: 125 MCHF

---
Conclusions
- Rough baseline concepts identified for the three main parts of the Porthos machine:
  - Resonant kicker for bunch separation: faster kicker with 21 ns bunch spacing
  - Linac upgrade: 3 additional C-band stations in linac-3 and Porthos arm, injector upgrade
  - Undulator: 60 m of 15 mm Apple-X undulators
- With this, can start designing a 100-Hz, 7-GeV machine delivering 4–18 keV, maybe 20 keV photons, with full polarization control.
- Feasibility of Apple-X undulators (with stringent field quality requirements at hard X-rays) still to be demonstrated.
  - Therefore fall-back solution with planar undulators and phase retarder.
- Very first budget estimate based on main components costs: 120 MCHF – a reasonable envelope?
- Note: The only robust way to reach higher photon energies is by increasing the electron energy!
  - Starting at 6 GeV, SwissFEL will never be competitive in that area! (It was not our goal.)
  - SwissFEL Porthos will be unique in terms of polarization control up to very high photon energies.

---
Next steps (roadmap process)
- Tonight (16:30):	meeting with directorate to discuss RI priorities for PSI
  - SwissFEL Porthos or TATTOOS/HIMB, or both?
- early March 2021:	Internal deadline for PSI evaluation (two-page fact sheet with supporting material)
- 21 April 2021	ETH council meeting: first discussion of project ideas.
  ⇒ for this a two-page fact sheet is needed! (close to what actually goes into the roadmap)
- early July 2021	ETH closed session (“Klausur”): in-depth discussion of projects
- September 2021	Notification of SNF on ETH projects planned for the '23 roadmap
- January 2022	Submission of final requests to SNF for evaluation

---
Roadmap process (general)
- The process towards the roadmap 2023 is expected to be very similar to the process that led to the last roadmap (2019).
- From the “Leitfaden” to the roadmap 2019, as well as an SBFI communication from 3 Feb. 2020, we may infer the following timeline (translated to the 2025–28 ERI period):
Phase	Date	Procedural steps
Preparatory phase	during 2020	SCNAT prepares discipline specific roadmaps
	Dec. 2020–Feb. 2021	SERI prepares the roadmap process.
Phase I	March–Dec. 2021	First assessment by ETH board and swissuniversities for facilities in their respective areas – requires a two-page fact sheet
Phase II	Jan.–Aug. 2022	Scientific evaluation by SNF – requires a conceptual design report! Only the highest ranked facilities proceed to the next level
Phase III	Jan.–Dec. 2022	In-depth assessment of technical and financial feasibility, again by ETH board and swissuniversities for their respective facilities
Phase IV	Jan.–Aug. 2023	SERI finalizes the roadmap report and presents it to the federal council.
Decisions	Dec. 2024	Federal council presents ERI dispatch with recommended support for facilities to parliament, which votes on the dispatch. (The decision to actually build or upgrade a facility still rests with the ETH board or swissuniversities.)
Implementation	2025–2028	Realization by ETH institutions / universities

---
Acknowledgements
Thank you