## Slide 1: SwissFEL/Porthos energy linac upgrades (version 2)
Paolo Craievich, Marco Pedrozzi et al. :: RF section :: Paul Scherrer Institut
Porthos meeting, 19 Feb 2021

## Slide 2: Energy upgrade and cost estimates - Injector
SINSB03
SINSB04
SINSB05
SINXB01
BC1
SINDI
SINSB03
SINSB04
SINSB05
SINXB01
BC1
SINDI
Injector 1
New S-band structures 3-m long and SBOC and 1 HV mod and klystron
Energy upgrade:
+ 360 MeV at BC1
Costs: 2.6 MCHF
SINSB03
SINXB01
BC1
S10CBnew2
Injector 2
BC1 will be moved upstream, 2 C-band modules after BC1 and new S-band structures + BOC
Energy upgrade:
+ 480 MeV
Costs: 4.1 MCHF
S10CBnew1
Reference: PORTHOS-PM84-cost_evaluation_RF_modules
Part of the RF consolidation at the injector
Bunch compression improvement

## Slide 3: Energy upgrade and cost estimates – Linac 3
Linac 3 end
4 X-band modules
C-TDS will be moved after Aramis und.
Energy upgrade:
+ 720 MeV
Costs: 10 MCHF
Linac 3 builiding extension
4 C-band modules in the transfer line
Energy upgrade:
+ 960 MeV
Costs: 8.2 MCHF (RF)+ 2.2 MCHF (building and infrastructures)
S30CB14
(TDSs)
S30CB13
S30CB15
S30CB16
XB13
S30CB15
S30CB14
XB14
XB15
XB16
S30CB13
S30CB16
S30CB15
S30CB16
Extension klystron gallery: Length 40 m, width 9 m, height 4m
Reference: PORTHOS-PM84-cost_evaluation_RF_modules