OBLA Simulations:
OPAL vs ASTRA
Thomas Schietinger, PSI
FELSI Meeting, 5 May 2009

---
Content
Motivation / history
LEG geometries
Comparison OPAL/ASTRA
  - For one working point, with current geometry/laser
OPAL optimizations for Ti:Sapph laser
  - For all geometries
  - But only for elliptical electrodes (as currently installed)

---
Motivation / history
OBLA retreat: both KL and TS who simualtions for Ti:Sapph laser (200 pC, flat-top with 9.9 ps FWHM) produced electron beam at OBLA
KL (ASTRA): 0.8 mm mrad for currently standard elliptical electrodes, 0.4 mm mrad for specially designed “nose” electrodes
TS (OPAL): ~4 mm mrad for elliptical electrodes
Where does the difference come from?
  - different codes (OPAL vs ASTRA)
  - different geometries?
Purpose of this meeting to sort out the difference!

---
LEG geometry as is now

---
LEG geometry as is now
Distance anode-cavity: 166.1 mm

---
LEG geometry as is now
More detailed drawing (but with flat electrodes)

---
LEG geometry according to drawing on the web

---
LEG geometry according to drawing on the web

---
LEG geometry according to drawing on the web
Distance anode-cavity: 150 mm

---
LEG geometry as designed once

---
LEG geometry as designed once
Distance anode-cavity: 119.8 mm

---
LEG geometries: summary
Three geometries have been considered:
For the OBLA-ASTRA comparison, use the geometry corresponding to the current reality (166 mm drift), with the current laser (JAGUAR)
Distance to cavity:	120 mm	150 mm	166.1 mm
Distance to pulsed sol.:	40 mm	47.5 mm	63.6 mm
used by Thomas for OBLA retreat simulations
used by Kevin for OBLA retreat simulations
Current reality

---
Working point 1 (166 mm drift geometry)
low charge
high charge
Bunch charge:	10 pC	100 pC
Laser spot diameter:	0.6 mm	1.4 mm
Laser t	14.8 ps
Pulser voltage:	300 kV
Pulser gap:	6 mm
Pulsed solenoid:	145 mT	144 mT
RF phase:	~on-crest (adjustable)
RF gradient:	42 MV/m
Double sol. 10	120 mT	121 mT
Double sol. 20	90 mT
Use these two points for OPAL/ASTRA comparison!

---
Known differences OPAL-ASTRA
OPAL
ASTRA
General:
Tracking:	3D	2.5D
Mirror charges at emission:	yes	yes
Wakefields:	no	no
Specific (this simulation):
Mesh	32x32x64	20x20x30
Number of particles:	100k	2k
Time step (diode):	0.1 ps	0.1–1 ps
Time step (beamline):	1 ps	0.1–1 ps
Energy bins at emission:	10	1
Longitudinal emission energy:	1 eV	1 eV
Transverse emission energy:	0 eV	0 eV
i.e. no thermal emittance!
Fieldmaps are exactly the same!

---
Fieldmap for pulsed solenoid

---
Comparison OPAL-ASTRA
For “working point 1” with 10 pC
Elliptical electrodes
Current lattice (166 mm drift between anode and RF cavity)
Jaguar laser (Gaussian profile, t = 14.8 ps)
RF phase in OPAL adjusted to match ASTRA curves

---
Comparison OPAL-ASTRA
For “working point 1” with 10 pC
Elliptical electrodes
Current lattice (166 mm drift between anode and RF cavity)
Jaguar laser (Gaussian profile, t = 14.8 ps)
RF phase in OPAL adjusted to match ASTRA curves

---
Comparison OPAL-ASTRA
For “working point 1” with 100 pC
Elliptical electrodes
Current lattice (166 mm drift between anode and RF cavity)
Jaguar laser (Gaussian profile, t = 14.8 ps)
RF phase in OPAL adjusted to match ASTRA curves

---
Comparison OPAL-ASTRA
For “working point 1” with 100 pC
Elliptical electrodes
Current lattice (166 mm drift between anode and RF cavity)
Jaguar laser (Gaussian profile, t = 14.8 ps)
RF phase in OPAL adjusted to match ASTRA curves

---
Conclusion: OPAL/ASTRA comparison
For the OBLA setup, when using the same geometry, the two codes give very similar results
The differences can probably be attributed to differences in the emission process.
  - Would take more effort to find out – is it worth it?
In any case the differences seem irrelevant for OBLA
  - Agreement within a few percent
  - The problems are elsewhere!

---
Ti:Sapph optimizations
Ti:Sapph laser: flat-top longitudinal profile with 9.9 ps FWHM and 0.7 ps rise and fall time
200 pC charge (~20 A), 1.08 mm laser spot diameter
Optimization = adjustment of solenoid strengths and RF phase to get lowest emittance between 2 and 3 meters distance (range covered by the emittance monitor)
  - Pulser gradient constant at 400 kV / 4 mm = 100 MV/m
  - RF gradient constant at 50 MV/m
Do this for the three geometries: 120, 150 and 166 mm drift between anode and RF cavity

---
Ti:Sapph laser
166 mm drift
Elliptical electrodes
Current lattice (166 mm drift between anode and RF cavity)
Ti:Sapph laser (flat-top profile, FWHM = 9.9 ps, trise = 0.7 ps)
Smallest projected emittance is about 9 mm mrad
Pulsed solenoid: 170 mT

---
Ti:Sapph laser
150 mm drift
Elliptical electrodes
Current lattice (150 mm drift between anode and RF cavity)
Ti:Sapph laser (flat-top profile, FWHM = 9.9 ps, trise = 0.7 ps)
Smallest projected emittance is 1.4 mm mrad
Pulsed solenoid: 194 mT

---
Ti:Sapph laser
120 mm drift
Elliptical electrodes
Current lattice (120 mm drift between anode and RF cavity)
Ti:Sapph laser (flat-top profile, FWHM = 9.9 ps, trise = 0.7 ps)
Smallest projected emittance is 0.55 mm mrad
Pulsed solenoid: 225 mT

---
Growth in energy spread?
Longitudinal phase space (z-pz) at various points along the beamline:
s = 1 m
s = 2 m
s = 3 m
s = 4 mm
s = 8 cm
s = 50 cm

---
Conclusion: Ti:Sapph optimization
Minimum reachable emittance between 2 and 3 m, in mm mrad:
Drift distance from anode to cavity:
Cathode shape
120 mm
150 mm
166 mm
Elliptical cathode:	0.55	1.4	9.0
Nose cathode:	0.4?	?	?
Nose cathode simulations not yet done with OPAL (problem with fieldmap) – see Kevin's ASTRA simulations!

---
Conclusion: Ti:Sapph optimization
Emittance extremely sensitive to drift distance in front of cavity
  - The longer the drift distance, the less focusing we can apply with the pulsed solenoid
With standard elliptical cathodes (“doorknobs”) cannot expect emittance below 1 mm mrad for drift distance around 150 mm (at 20 A current).
Only shortened drift distance, or redesigned cathode (or, better, both) can give a substantial reduction in emittance.
  - Huge effort needed to get down to 0.4 mm mrad (where we start to compete with the RF photo-injector...)
At lower current, the emittance becomes correspondingly smaller
  - () still makes sense to measure!