## Slide 1: Athos Project
Romain Ganter :: Athos Machine Project Leader :: Paul Scherrer Institut
LAB meeting – 25.06.2021

## Slide 2: Outline
Athos key components
Athos commissioning
Budget & Timeplan

## Slide 3: Athos: Laser im weichen Röntgenbereich
Athos
phase
2017–20
Aramis
phase
2013–16
Two times more experiment (100 Hz)
Soft x-ray domain (250-1900 eV)
Athos
Soft x-ray
Aramis
Hard x-ray
SwissFEL Tunnel

## Slide 4: SwissFEL
Athos
  Soft X-ray FEL, variable polarization
  First users 2021
  Main parameters of Athos
  Photon energy 250 – 1900 eV
  Pulse duration 1 fs - 20 fs
  e- Energy 2.65 – 3.4 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz
Aramis
  Linear polarization, variable gap, in-vacuum Undulators
  First users 2018
1st Construction Phase
2013-16
Linac 3
Linac 1
Injector
Linac 2
Aramis 0.1-0.7 nm
0.35 GeV
2.1 GeV
3.15 GeV
2.1-5.8 GeV
user stations
BC1
BC2
2nd Construction Phase 2017-20
8 UE38 + Chicanes
8 UE38 + Chicanes
Athos 0.65-5nm
dechirpers
2-color chicane

## Slide 5: SwissFEL
Athos
  Soft X-ray FEL, variable polarization
  First users 2021
  Main parameters of Athos
  Photon energy 250 – 1900 eV
  Pulse duration 1 fs - 20 fs
  e- Energy 2.65 – 3.4 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz
Aramis
  Linear polarization, variable gap, in-vacuum Undulators
  First users 2018
1st Construction Phase
2013-16
Linac 3
Linac 1
Injector
Linac 2
Aramis 0.1-0.7 nm
0.35 GeV
2.1 GeV
3.15 GeV
2.1-5.8 GeV
user stations
BC1
BC2
2nd Construction Phase 2017-20
8 UE38 + Chicanes
8 UE38 + Chicanes
Athos 0.65-5nm
dechirpers
2-color chicane
Mizar
Gun Laser

## Slide 6: Athos Gun Laser: Mizar
Amplifier
Oscillator
LAM
Pulse picker
Gun, LH & diagnostics
outputs
Duration 400 fs
Spectrum
Energy stability<0.2%
M2=1.1
Pointing 5.3 urad
Beam profile
Courtesy of C. Vicario

## Slide 7: Two identical bunches extracted from Photocathode
Bunch 2 with Mizar (Screen near gun)
Bunch 1 with Alcor (Screen near gun)
Bunch quasi identical same quality !

## Slide 8: Tuning Bunch „Two“ energy
Both bunches in same RF macropulse
Courtesy of Z. Geng
=> RF extra-step to tune Bunch „Two“ only !
time
RF
power
1 μs

## Slide 9: SwissFEL
Athos
  Soft X-ray FEL, variable polarization
  First users 2021
  Main parameters of Athos
  Photon energy 250 – 1900 eV
  Pulse duration 1 fs - 20 fs
  e- Energy 2.65 – 3.4 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz
Aramis
  Linear polarization, variable gap, in-vacuum Undulators
  First users 2018
1st Construction Phase
2013-16
Linac 3
Linac 1
Injector
Linac 2
Aramis 0.1-0.7 nm
0.35 GeV
2.1 GeV
3.15 GeV
2.1-5.8 GeV
user stations
BC1
BC2
2nd Construction Phase 2017-20
8 UE38 + Chicanes
8 UE38 + Chicanes
Athos 0.65-5nm
dechirpers
2-color chicane
Resonant Kicker

## Slide 10: Separation of the two bunches
Two resonant kickers separate the 2 bunches (vertically)
LC resonator
Courtesy of M. Paraliev
Chart: 
A
t
Bunch Athos kicked Up (~ 1 mrad)
Bunch Aramis kicked Down
56 ns

## Slide 11: Kicker + Septum
Septum deflects 2nd bunch 10m downstream
Fast kickers with DC correctors in SwissFEL
Courtesy of M. Paraliev
FEL position stability constant with / without kickers (0.18 μm rms) !
Influence of Kicker on Orbit stability ?
5 minutes

## Slide 12: SwissFEL
Athos
  Soft X-ray FEL, variable polarization
  First users 2021
  Main parameters of Athos
  Photon energy 250 – 1900 eV
  Pulse duration 1 fs - 20 fs
  e- Energy 2.65 – 3.4 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz
Aramis
  Linear polarization, variable gap, in-vacuum Undulators
  First users 2018
1st Construction Phase
2013-16
Linac 3
Linac 1
Injector
Linac 2
Aramis 0.1-0.7 nm
0.35 GeV
2.1 GeV
3.15 GeV
2.1-5.8 GeV
user stations
BC1
BC2
2nd Construction Phase 2017-20
8 UE38 + Chicanes
8 UE38 + Chicanes
Athos 0.65-5nm
dechirpers
2-color chicane
Dechirper

## Slide 13: Dechirpers: to control FEL Bandwitdh
To tilt the bunch
To remove CHIRP
Gap: 1-20mm
8 dechirpers (8 m)
installed in tunnel

## Slide 14: SwissFEL
Athos
  Soft X-ray FEL, variable polarization
  First users 2021
  Main parameters of Athos
  Photon energy 250 – 1900 eV
  Pulse duration 1 fs - 20 fs
  e- Energy 2.65 – 3.4 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz
Aramis
  Linear polarization, variable gap, in-vacuum Undulators
  First users 2018
1st Construction Phase
2013-16
Linac 3
Linac 1
Injector
Linac 2
Aramis 0.1-0.7 nm
0.35 GeV
2.1 GeV
3.15 GeV
2.1-5.8 GeV
user stations
BC1
BC2
2nd Construction Phase 2017-20
8 UE38 + Chicanes
8 UE38 + Chicanes
Athos 0.65-5nm
dechirpers
2-color chicane
APPLE X + CHIC

## Slide 15: Undulator Apple X – UE38
Characteristics:
12 Tons; Iron cast frame (easier to machine)
Positioning via cam shaft movers (20 um precision)
Radial motion with wedge system (K tuning)
Longitudinal motion with spindle (Polarization tuning)
PLC control (Beckhoff) with EPICS interface
Gap reproducibility < 1 um
Minimum Gap / slit: 3 mm with a 6.5 mm aperture
Polarization Control: circular – elliptical – linear
Kmax~3.65
Possibility of transverse gradient
12 tons

## Slide 16: Magnetic Characterisation of the Apple X
Courtesy of M. Calvi

## Slide 17: Tunnel Installation
16 Undulator & 15 CHIC chicanes in Tunnel

## Slide 18: CHIC magnetic chicanes

## Slide 19: SwissFEL
Athos
  Soft X-ray FEL, variable polarization
  First users 2021
  Main parameters of Athos
  Photon energy 250 – 1900 eV
  Pulse duration 1 fs - 20 fs
  e- Energy 2.65 – 3.4 GeV
  e- Bunch charge 10-200 pC
  Repetition rate 100 Hz
Aramis
  Linear polarization, variable gap, in-vacuum Undulators
  First users 2018
1st Construction Phase
2013-16
Linac 3
Linac 1
Injector
Linac 2
Aramis 0.1-0.7 nm
0.35 GeV
2.1 GeV
3.15 GeV
2.1-5.8 GeV
user stations
BC1
BC2
2nd Construction Phase 2017-20
8 UE38 + Chicanes
8 UE38 + Chicanes
Athos 0.65-5nm
dechirpers
2-color chicane
Maloja
Furka

## Slide 20: FEL beamline Athos
Pump laser
infrastructure
Pump laser
infrastructure
(1st floor)
Aramis
Athos
Endstation Alvra
Endstation Bernina
Endstation Cristallina
Endstation Diavolezza
Endstation Maloja
Endstation Furka
2 (3) Endstations: Maloja & Furka
Soft x-ray science from CK, TML , to SiK
Chemical to solid state research

## Slide 21: Maloja Commissioning Results
Courtesy of C. Botstedt

## Slide 22: Outline
Athos key components
Athos commissioning
Budget & Timeplan

## Slide 23: Magnetic chicanes between undulators
2 m
2.8 m
CHIC Chicanes: - to delay the electrons
- to shift the orbit transversally
- to compress the electron bunch
APPLE X:
Transverse Gradient Undulator
Polarization control
Goal: to have flexibility like a table top laser

## Slide 24: Athos CHIC Mode #1: Optical Klystron
SASE speed up with Optical Klystron !
2 to 3 Undulators
Courtesy of E. Prat
Optical Klystron: Speed up of lasing process
2 m
2.8 m

## Slide 25: Athos CHIC Mode #2: Two colors mode
Two color Chicane
Two colors in Maloja‘s Spectrometer
531 eV
543 eV
Courtesy of K. Schnorr & E. Prat

## Slide 26: Athos CHIC mode #3: Short, high power pulses
Short, high power pulses
(superradiance)

## Slide 27: Dechirper as longitudinal bunch diagnostic
Athos Lasing 220 uJ
No streaking
Athos Lasing 220 uJ
Streaking
No Lasing
Streaking
Energy spread increase due to Lasing electrons
time
Energy
Dechirper to tilt the beam (time resolution)
Beam Dump Dipole magnet to see energy spread of lasing electrons
Measurements E. Prat et. al.

## Slide 28: Athos CHIC Mode #3: Short, high power pulse
no lasing
Lasing
Time
Electron energy
Pulse duration control
with tilted beam (dechirper) !
850 uJ
50 fs rms 100Hz
175 uJ
20 fs rms 25Hz
80 uJ
<10 fs rms
10 Hz

## Slide 29: Towards superadiant mode of operation
Shifting the lasing portion of the bunch
Short, high power pulses
(superradiance)
Fresh electron slice after each undulator

## Slide 31: Outline
Athos key components
Athos commissioning
Budget & Timeplan

## Slide 32: Budget
Machine budget distribution

## Slide 33: Athos milestones
Most milestones reached on time before 2020
3 Months delays due to Covid

## Slide 34: Conclusion
Positive:
Most milestones reached on time !
Optical klystron very efficient: 1st lasing with only 2 undulators !
Undulators, dechirpers & chicanes are operating as expected.
CHIC modes are promising (e.g. 2 colors mode; tilted beam; …)
Issues:
3 MCHF for Regie not in first budget (=> cut by Furka Endstation)
X band RF modulator: 2 years delay (Company made banckrupt => in house devt)
Repetition rate limited by beam losses:
    5 mm vacuum pipe -> probably 3 mm real clearance !

## Slide 35: Wir schaffen Wissen – heute für morgen
Many thanks for your attention
Many thanks to the Athos Team

## Slide 36: Athos Operation since summer 2020
2 mJ at 870 eV
Operation to 100Hz more frequent
Photon Energy
Variation by users

## Slide 37: Wir schaffen Wissen – heute für morgen
Mein Dank geht an
Vorname Name
Vorname Name
Vorname Name