## Slide 1: The WaveDAQ System
Stefan Ritt :: Paul Scherrer Institute :: Muon Physics Group
LTP Seminar October 2021
Markus Fischer, PSI

## Slide 2: The Challenge: MEG II @ PSI
µ+→e+ɣ at with sensitivity ≈ 6 x10-14
108 m/s
t
< 52.8 MeV
0.511 MeV
~100ns
Calorimeter Signal:
µ+→e+ɣ Eg = 52.8 MeV
µ+→e+neng ⨽AIF Eg < 52.8 MeV
Liquid Xenon Calorimeter

## Slide 3: Digitizing detector signals
TDC
Detector
QADC
ADC
250 MSPS
125 MHz
ADC
2 GSPS
Signal:
1 MHz - 1 GHz
(0.3 ns risetime)

## Slide 4: DRS4 Chip 2008
8+1 channels
1-5 GSPS / 12 bits
Typical 140 mW
USB
Evaluation
Board

## Slide 5: MEG Electronics 2008-2013
PMT
Active
Splitter
Trigger
DRS4
DAQ
HV
Trigger Bus
Clock distribution
Power
Separated DAQ & Trigger & HV
VME based system
DRS4 piggy-back on general purpose FPGA board

## Slide 6: MEG on-line waveform display
“Virtual Oscilloscope”
template fit
S848 PMTs
Liq. Xe
PMT
1.5m
g
m

## Slide 7: MEG vs. MEG II electronics
MEG Experiment 1999-2013
Separated DAQ & Trigger
3000 Channels DRS4 (0.8 GSPS / 1.6 GSPS)
1000 Channels Trigger (100 MSPS)
5 Racks
SiPM
TDAQ
MEG II Experiment 2015-
9000 Channels
Same rack space
  Avoid dead space between boards
  Combine DAQ & Trigger
  Integrate high voltage
Timing requirement
  O(10 ps) between any two channels
PMT
Active
Splitter
Trigger
DRS4
DAQ
HV
Trigger Bus
Clock distribution
Power
?

## Slide 8: WaveDREAM Baord
Drs4 based REAdout Module
80 MSPS
5 GSPS

## Slide 9: Details of the WDB
Trigger
TDC
Scaler

## Slide 10: WaveDREAM Board > 2000 parts!

## Slide 11: WaveDREQM High Voltage

## Slide 12: Standalone System
Direct biasing of SiPMs
Preamps / Shaping for 16 SiPM signals
Power-over-Ethernet (PoE+)
“Web Oscilloscope”

## Slide 13: Web Oscilloscope
http://elog.psi.ch/scope
70 frames/s display rate
Integrated measurements with histogramming
Runs on any browser

## Slide 14: WaveDAQ Crate Standard

## Slide 15: Power Supply (400W) & Crate Controller

## Slide 16: Trigger Scheme
DRS4
ADC
80 MHz
S
FPGA
S
Trigger FPGA
16 inputs
serial links
256 inputs
total
Trigger after ~400 ns
WaveDREAM
Board
serial links

## Slide 17: MEG II System
Trigger Boards INFN Pisa

## Slide 18: Full system ~9000 channels

## Slide 19: MIDAS at work
~7 Hz event rate
130 MB/s and 50 MB/s compressed  20 TB / week
Tons of slow control (accessible remotely through web)

## Slide 20: Gamma pile-up
SiPM (MPPC)
PMT

## Slide 21: MEG II event gallery

## Slide 22: Beam Profile Monitors using WaveDAQ
MatriX, A. Papa et al.
SciFi, A. Papa et al.
SiMon, A. Soter at al.

## Slide 23: Plans for BPM
Easy-to-use, compact, stand-alone system
Different detector front-ends (fibres, pixels, …), configurable
Use proton RF signal for particle ID
Integrated web server for direct profile display
Build several units for our secondary beam lines

## Slide 24: Conclusions
WaveDAQ system successfully deployed in MEG II after 9 years of development
System design is not specific to MEG
Single board (16 chn) and single crate (256 chn) systems useful for many applications at PSI
Web browser based software constantly extended
8.8 ps

## Slide 25: WaveDAQ @ PSI
My thanks go to
Roberto Dinapoli
Ueli Hartmann
Elmar Schmid
Luca Galli
Marco Francesconi
INFN Pisa