## Slide 1: The Fermilab Muon g-2 Experiment Status and Outlook
erhtjhtyhy
Simon corrodi
Argonne National Laboratory
on behalf of the Muon g-2 collaboration
PSI 2022
October 16 - 21, 2022

## Slide 2: The magnetic Moment of the muon
Magnetic moment connected to spin via dimensionless factor g: gyromagnetic ratio
the anomalous magnetic moment

## Slide 3: The magnetic Moment of the muon: history
Stopped Muons
Stop muons in a magnetic field measurement of directly
Storage Ring
Dilated lifetime measurement of , more precise

## Slide 4: The magnetic Moment of the muon: history
full stats
Run 1 (2021)
Stopped Muons
Stop muons in a magnetic field measurement of directly
Storage Ring
Dilated lifetime measurement of , more precise
FNAL goal: 4 x improvement

## Slide 5: The bottom line up front… our run-1 result
WP20

## Slide 6: April 7th: Fermilab Muon g-2 experiment announced the first result
PRAB
PRA
PRD
PRL

## Slide 7: The magnetic Moment of the muon: from theory
Dirac g=2 (1928) for s=1/2 particles
Schwinger (1948) 1st order QED
Vacuum polarizations
Higher order QED
Hadronic HVP: 6845(40) x 10-11 HLbL: 92(18) x 10-11
Electroweak
153.6(1.0) x 10-11
aμ(SM)=
116
59
1
810
(43) x 10-11
Muon g-2 Theory Initiative
uncertainty: 0.1 x 10-11

## Slide 8: The magnetic Moment of the muon: from theory
Very active theory community
Lots of current work ongoing to understand possible discrepancy, comparison of intermediate time regions
Lattice results:
lots of current work ongoing to understand possible discrepancy
comparison of intermediate windows

## Slide 9: measure in a storage ring
μ+
B=1.45T

## Slide 10: measure in a storage ring
momentum
spin
Cyclotron frequency
Spin precession
NMR:

## Slide 11: Storage ring: How we store the muons
}
~0
}
~0
pitch corrections:
E-field corrections:

## Slide 12: measure in a storage ring
10.5 ppb uncertainty (hydrogen maser)
Metrologia 13, 179 (1977)
bound state QED calc., exact
Phys. Rev. A 83, 052122 (2011)
2022: 0.13ppt, arXiv 2209.13084
0.28 ppt uncertainty
Phys. Rev. Lett. 82, 711 (1999)
22 ppb uncertainty
(Muonium hyper fine split.)
TDR goal: 140 ppb
(4 fold improvement over the BNL result)

## Slide 13: measure in a storage ring
beam dynamics corrections
Magnetic transients corrections
blinding factor
absolute field calibration
magnetic field sampled by the muon distribution
precession

## Slide 14: The magnet: the big move

## Slide 15: The muons
8 GeV protons in recycler
Target
p/π/μ beam, p kicked away, π decay
Store muons for ~700us (~10 lifetimes)
for
2 x 8 shots
95% polarized muons

## Slide 16: How to store muons: magnetic field
μ+

## Slide 17: How to store muons: magnetic field
Shimming
Fermilab: ~15 ppm RMS (~75 ppm peak-to-peak)
BNL E821: ~35 ppm RMS (~200 ppm peak-to-peak)

## Slide 18: How to store muons: The inflector
μ+
Need to cancel field in beam channel
- prevents strong deflection of the beam
d=77mm

## Slide 19: How to store muons: The kicker
μ+
Incident beam center 77 mm off from center of storage region
- tears muon onto store orbit
d=77mm
μ+
Upgrade since run 1: New kicker cable allow for proper kicker, reducing the equilibrium radius.

## Slide 20: How to store muons: focusing
μ+
Radial focus: 1.45T vertical B field
Vertical focus: electrostatic quadrupoles (43% of the ring)
+18kV
+18kV
-18kV
-18kV
Upgrade since run 1: Broken high voltage resistors in run 1 led to an additional early-to-late effects.

## Slide 21: The measurements: calorimeters ( )
μ+
24 Calorimeters with 54 (9x6) Cherenkov
PbF2 crystals read out by SiPMs
arrival time (~100ps) & energy of e+ (~5% at 2GeV)
Laser system for gain response calibration throughout data taking
(stability 10-3, rate difference 104)

## Slide 22: The measurements: calorimeters ( )
μ+
e+
- Parity violating decay (Michel)
- Highest-energy e+ emitted preferentially along muon spin
    e+
    µ+
νe
ν̄µ
⇒
⇒
⇒
⇒

## Slide 23: Measurements:
time

## Slide 24: Measurements:
22 parameter fit
Example from dataset 1d
*CBO: Coherent Betatron Oscillation

## Slide 25: trackers: beam dynamics
2 straw-tracker stations (each 8 modules, 4 layers of 32 straws, 50:50 Ar:Ethane, res ~100um)
Muon distribution + field maps:
Handle on beam dynamics
μ+

## Slide 26: trackers: beam dynamics
*CBO: Coherent Betatron Oscillation
Upgrade since run 1: Additional RF on the ESQ since the end of run 4 allows to reduce the CBO.

## Slide 27: Nuclear magnetic resonance (NMR)
- Flip spins of a sample by delivering a π/2-pulse - measure Free Induced Decay (FID)
Free Induced Decay (FID)
time [s]
Petroleum Jelly probes
H20 calibration probe ()

## Slide 28: The Field measurement
154mm
378 Fixed Probes
- Outside of the storage region - 72 position, ~5deg apart
60mm
90mm
2
35 mm
70 mm
90 mm
Trolley
- inside the storage region, ~3 days - 17 probes, moves around the ring
~49cm
Electronics
NMR probes

## Slide 29: The Field measurement
See poster: “The precision magnetic field in the Muon g-2 Experiment at Fermilab”
378 Fixed Probes (from the outside)
Track the field between field maps
Trolley (every ~3 to 5 days)
Field inside the muon storage volume
Uncertainty: random walk model (Brownian bridge)
Upgrade since run 1: Thermal insulation (run 2) and improved AC (run 3) increased the field stability.

## Slide 30: Back to the master formula
beam dynamics
corrections
Magnetic transients corrections
unblinding factor
absolute field calibration
magnetic field sampled by the muon distribution
precession

## Slide 31: The run-1 result
Upgrade since run 1: Extensive campaigns to measure the magnetic field transients more precisely.

## Slide 32: More to come: the Beyond run 1 analysis
results ~6% of full stats, 434 ppb stat ⊕ 157 ppb syst errors
Run 2/3 analysis in progress, aiming to reduce experimental error by 2 by spring. Systematics on track for < 100 ppb.
Run 4/5/6, aiming for another factor of ~2 reduction in error

## Slide 33: Even More to come: run 6
results ~6% of full stats, 434 ppb stat ⊕ 157 ppb syst errors
Run 2/3 analysis in progress, aiming to reduce experimental error by 2 by spring. Systematics on track for < 100 ppb.
Run 4/5/6, aiming for another factor of ~2 reduction in error
Run 6 starts in ~2 weeks - originally planned, canceled - lower priority at FNAL than mu2e

## Slide 34: The collaboration
United Kingdom
  Lancaster/Cockcroft
  Liverpool
  Manchester
  University College London
Run-1 unblinding ceremony
USA
  Boston
  Cornell
  Illinois
  James Madison
  Kentucky
  Massachusetts
  Michigan
  Michigan State
  Mississippi
China
  Shanghai Jiao Tong
Germany
  Dresden
  Mainz
Russia
  Budker/Novosibirsk
  JINR Dubna
  North Central
  Northern Illinois
  Regis
  Virginia
  Washington
USA National Labs
  Argonne
  Brookhaven
  Fermilab
Italy
  Frascati
  Molise
  Naples
  Pisa
  Roma Tor Vergata
  Trieste
  Udine
Korea
  CAPP/IBS
  KAIST