## Slide 1: Radiation protection issues related to IMPACT
S. Harzmann, WG Safety
Department of Radiation Safety and Security
IMPACT - Infoveranstaltung
PSI, March 19th 2025

## Slide 2
Radiation protection requirements

## Slide 3: Dose Limits by Radiation Protection Ordinance
Category of people | Quantity | Limit
Occupationally exposed to radiation Category A | effective dose | 20 mSv/ year*
 | skin dose | 500 mSv/ year
 | Eye lens dose | 20 mSv/ year*
Occupationally exposed to radiation Category B | effective dose | 6 mSv/ year
 | skin dose | 150 mSv/ year
 | lens dose | 15 mSv/ year
Age 16 until 18 | effective dose | 6 mSv/ year
Pregnant women | effective dose for unborn child | 1 mSv
General public | effective dose | 1 mSv/ year
 | skin dose | 50 mSv/ year
 | lens dose | 15 mSv/ year
Personal dose outside company premises due to direct radiation | effective dose | 0.1 mSv/year
* With permit of regulating authority, limit can be increased by exemption to 50 mSv/year if the cumulative dose of 5 successive years is below 100 mSv.

## Slide 4: Dose Limits by Radiation Protection Ordinance
Category of people | Quantity | Limit
Occupationally exposed to radiation Category A | effective dose | 20 mSv/ year*
 | skin dose | 500 mSv/ year
 | Eye lens dose | 20 mSv/ year*
Occupationally exposed to radiation Category B | effective dose | 6 mSv/ year
 | skin dose | 150 mSv/ year
 | lens dose | 15 mSv/ year
Age 16 until 18 | effective dose | 6 mSv/ year
Pregnant women | effective dose for unborn child | 1 mSv
General public | effective dose | 1 mSv/ year
 | skin dose | 50 mSv/ year
 | lens dose | 15 mSv/ year
Personal dose outside company premises due to direct radiation | effective dose | 0.1 mSv/year
* With permit of regulating authority, limit can be increased by exemption to 50 mSv/year if the cumulative dose of 5 successive years is below 100 mSv.

## Slide 5: Ambient Dose Rates ADR
Optimization: 10% of ADR in controlled areas

## Slide 6: Ambient Dose Rates ADR
Especially important during dismantling

## Slide 7: Radiological zoning concept
In supervised (zone 0) and controlled areas: 1 mSv/year possible
CS: nuclide specific guidance value for surface contamination [Bq/cm2]
CA: nuclide specific guidance value for airborne contamination [Bq/m3]
                Radiation protection clothing accordingly
+ Classification by area types
according to the local dose rate
+ Restriction of stay
#Radiation Protection Ordinance SR 814.501, appendix 10
#
Notes: Radiological Zoning Concept due to potential expected contamination

## Slide 8
Radiation protection requirements:
HIMB

## Slide 9: Overview of experimental hall WEHA
0 I II III IV
Zone types
Target M
II
*
*
Cooling Time: 85 days, dose rates in µSv/h ; AB: «Arbeitsbereich», working area; HS: Hot Spot
contamination:  10 CS (main nuclide: Sb-124)  zone type II
Notes: Befinden uns auf der Bedienebene, d.h. Stahlabschirmung direkt um Target + weitere Betonabschirmung nach wie vor vorhanden

## Slide 10: Dismantling Target M station
Contamination inside target chamber:
 330 CS
Main nuclides:
  Be-7: 300 CS (30‘000 Bq/cm2)
  Na-22: 30 CS (90 Bq/cm2)
 Contamination: highest zone type IV
 Dose rate: Remote Handling necessary
Measurement position | Dose rate [mSv/h]
1 | 15-20
2 | 170
3 | Max. 4000
Beam direction

## Slide 11: Dismantling Target M station
Double door system with negative air pressure staging
(I  IV)
Outside the enclosure:
Zone I: < 1 CS
(experimental hall)
Position of the cameras for remote handling
Zone IV
negative air pressure staging (I  IV)
Zone III
Zone I
manlock
Zone III
Zone I
Material lock

## Slide 12
Radiation protection requirements:
TATTOOS

## Slide 13: Zoning concept TATTOOS (current status)
Gamma
Laboratory Type A
II
III
0
I
IV
EG

## Slide 14: Zoning concept TATTOOS (current status)
Gamma
Laboratory Type A
II
III
I
IV
EG
0

## Slide 15: Zoning concept TATTOOS (current status)
Gamma
Laboratory Type A
II
III
0
I
IV
OG 2
(TATTOOS hall)

## Slide 16: Ambient dose rate photons (current status)
Gamma
EG
Photons
Ambient dose rate (photons)
[Sv/h]

## Slide 17: Ambient dose rate neutrons (current status)
Gamma
EG
Neutrons
Ambient dose rate (neutrons)
[Sv/h]

## Slide 18
Measurement campaigns

## Slide 19: Measurement campaigns for IMPACT
piE1: shielding investigations for its readaption in the frame of IMPACT. [*]
pK1: shielding studies considering the splitter operation in view of TATTOOS. [*]
PiM1.3: neutron dose rate assessment in these areas for a pre- VS post-HIMB comparison.
“Gusti-Loch”: dose rate (n + γ) study when the current splitter is in action, to determine the shielding needed for the TATTOOS building.
MuE4: Normalization measurements necessary for Monte-Carlo-shielding calculations; beamline similar to MuH2
[*] Measurements corroborated by MC simulations

## Slide 20: piE1 campaign
heavy concrete
normal concrete
Neutron ( LUPIN detectors) and gamma ( NAUSICAA detectors) dose measurements.
Beam stopped on shielding in two configurations: 1) 50 cm of heavy concrete, 2) 50 cm of heavy concrete (HC) + 50 cm of normal concrete (NC).
Highlights:
Crucial to verify experimentally the beam spot and size for proper instrument positioning and dose measurement.
High gradient of the field (dose) in space  need for precise positioning
Normal concrete not sufficient for the new shielding

## Slide 21: MuE4 campaign
Characteristics of beam line are similar to the new MuH2 for IMPACT
Normalization measurements necessary for Monte-Carlo-shielding calculations
Active and passive
  dose(rate)measurements
Challenges: narrow space constraints
Necessity: correct positioning of (neutron) dosimeters

## Slide 22: MuE4 campaign
neutrons (PADC) photons (BeO)
Dose integration time: ~2 h during normal operation
mGy

## Slide 23
Many thanks to the whole IMPACT team, especially to:
D. Kiselev, R. Eichler, A. Knecht, A. Koschik
Many thanks for the contributions for this talk, especially to:
S. Mayer, E. Hohmann, C. Harm, M. Bolzonella, L. Pedrazzi, M. Tisi, M. Müller, P. Meyer, A. Ivanov C. Nyfeler, C. Schmid, N. Preiss, M. Baumann
…many thanks to many more!