## Slide 1: SATMA02 TDS commissioning results
Paolo Craievich, Fabio Marcellini :: Paul Scherrer Institute
Evening shifts 10.02.23 and 10.03.23

## Slide 2: Shift goals
Suppress the kick in the plane orthogonal to the streaking plane due to input power unbalance or misaligned phases of the 3 phase shifters.
Verify deflecting voltage vs. input power (TDS efficiency).

## Slide 3
Deflecting field in a PolariX TDS is the combination of two rotating, one clockwise and the other counterclockwise, modes. Direction of rotation depends on the input for the RF power.
In Cartesian coordinates:
Clockwise mode: L cos (ωRFt + φL)x + L sin (ωRFt + φL)y
Counterclockwise mode: R cos (ωRFt + φR)x - R sin (ωRFt + φR)y (*)
Ideally the amplitudes at the TDS inputs are balanced, L=R, and the polarization plane depends on the phase difference between the inputs φL+φPS-φR, where φPS is the variable phase set through a phase shifter.
(*) from Pau Gonzalez (FlashForward – DESY) thesis
ϕPS

## Slide 4
In SATMA02 we use two TDS according to the scheme
Deflection in x and y will be:
Dy=R1*sin(φRF+φR1)-L1*sin(φRF+φRWVG110+φL1)+R2*sin((φRF+φRWVG200+φR2)-L2*sin(φRF+φRWVG200+φRWVG210+φL2)
Dx=R1*cos(φRF+φR1)+L1*cos(φRF+φRWVG110+φL1)+R2*cos((φRF+φRWVG200+φR2)+L2*cos(φ+φRWVG200+φRWVG210+φL2)
φRF is the RF phase, φRWVG are the 3 phase shifters phase that one can set from the panel “Athos RF X-Band Phase Shifters”.
L1, L2, R1, R2, φL1, φL2, φR1 and φR2 are fixed and unknown.
x and y positions measured with a downstream BPM proportional to Dx and Dy.

## Slide 5
In the february shift, first we validated the idea to reduce the kick in the vertical plane adjusting the phases of the three waveguide phase shifters.
360° RF phase scan:
X and Y positions measured with SATBD01-CBPM020
Vertical kick reduced by about a factor of 2
Then, we saved a number of acquisition readings of the first 3 BPMs downstream the TDSs for many different values of the phases of the 3 waveguide phase shifters.
The goal was to use these data to find the L1, L2, R1, R2, φL1, φL2, φR1 and φR2 values and have a model to predict the optimal set of the 3 variable phases of RWVG110, RWVG200 and RWVG210.

## Slide 6
Fitting the measured X and Y positions of the beam, as a function of φRF and for many different values of the phases of the 3 phase shifters, the 8 unkowns have been estimated.
For this measurements we had to reduce as much as possible the TDS input power to take the beam losses below a still acceptable threshold BOC detuned, no compressed RF pulse, very low LLRF signal amplitude.
All quads and correctors downstream the TDS switched off  beam moves in a drift after getting kicked by the the TDS.
Example of measured beam positions and fit result

## Slide 7
With the values of the 8 unknowns, we were able to calculate a set of 3 phase shifter phases to get beam deflection in one plane only (no more orthogonal kick when streaking in a given plane).
H polarization
V polarization
Kick (and beam size without quadrupoles) was probably too large for a correct beam position measurements with
SATBD01-CBPM060 and SATBD01-CBPM100.

## Slide 8
Tuning back the BOC, increasing klystron output power to 24 MW, the beam has been observed on SATBD01-DSCR120.
Horizontal polarization of TDS.
The beam takes a vertical kick giving a displacement of 22um at the screen.
RF OFF
RF ON (streaking)

## Slide 9
90°
150°
0°
10°
20°
30°
40°
50°
120°
105°
80°
70°
60°
180°
165°
135°
Last measurements past Friday.
Streaking at different polarities.
We did not operate exactly at zero crossing to avoid overlap of beam image with unexplained presence of a halo.

## Slide 10: Deflecting voltage
Similar setup as used for suppression of orthogonal kick:
  BOC detuned = +400 kHz
  DAC level = 10
From readout of klystron output power, taking into account the losses of waveguide network we estimated the single TDS input power to be 116kW.
With a scan of the RF phase we measured the max beam deflection 4.2 mm with SATBD01-CBPM020.
Distance between SATBD01-CBPM020 and center of the two TDS is 2.97m.
Beam energy ~3.1 GeV
VꞱ = 4.2/2970*3100 = 4.38 MV  Power to voltage coefficient = 2.19/sqrt(0.116) = 6.4 MV/sqrt(MW) for a single TDS.
From HFSS simulation we obtained 5.8 MV/sqrt(MW), from the A. Grudiev estimate 6.1 MV/sqrt(MW).
Estimate of both the RF power and the waveguide attenuation done with some degree of approximation. This can explain the discrepancy between nominal and measured coefficient.

## Slide 11: Wir schaffen Wissen – heute für morgen
My thanks go to
Christoph Kittel
Eduard Prat
Zheqiao Geng
For their support in setting the machine during the shifts.