## Slide 1: A physics-guided recurrent machine learning model for long-time prediction of quench dynamics
N. Breault, J.-H. Fournier-Lupien, C. Lacroix, F. Sirois
June 12th, 2024
Laboratory of Superconductivity and Magnetism (LSM)
Polytechnique Montréal, Montréal, QC, Canada

## Slide 2: Problematic: High computational cost for 3D simulations
Silver
Interfacial Resistance
HTS
Substrate
Main problems with FEM:
Simulation time: Several hours
Numerical instabilities
Few meters tape simulation: Impratical
Modelling approach:
Electrothermal (FEM)
Nonlinear E-J relation
Local defect in HTS (quench)
Solve for T(x,y,z,t) and V(x,y,z,t)
Exemple of HTS architecture
(not to scale)
Local defect
x
y
z
length
width
Buffer
A continuation of J.-H. Fournier-Lupien’s work. Heat problem only.
Notes: Critical phenomena must be taken into account

## Slide 3: How to SPEED UP simulation: the main idea
Silver
HTS
Substrate
length
x
y
Solution inside the HTS (thin layers)
T(x,t) and V(x,t)
A
A’
2D or 3D Problem (side view)
Dimension Reduction
1D Problem
Low Computational cost
A
A’
How to maintain accuracy?
length
Machine learning: Learn physics & Dimension reduction impacts
In practice: length ~ m, width ~ mm, and heigth ~ µm
Local defect
Notes: Critical phenomena must be taken into account

## Slide 4
Overview: workflow AND SPEED UP
2D or 3D Quench Simulations
(FEM solver)
Classical 1D models for quench dynamics
Machine learning techniques
Solution
T(x,t) & V(x,t)
Time-consuming
Physics-Guided Machine Learning Model
Data Generation
Training set
Fast
Test set
Notes: Critical phenomena must be taken into account

## Slide 5: Problem definition for data generation
2-D Problem to solve with FEM:
Electrical: Current continuity equation
Thermal: Heat Equation
Silver
HTS
Substrate
Coupled and nonlinear system
Notes: Critical phenomena must be taken into account

## Slide 6: DATA GENERAtion: randomness & parameters
Random inhomogeneities in critical current:
Position
Numbers
Amplitude
Width
Example of 2-D FEM solution
Tape Architecture:
Width : 0.04m
Height : 2 µm (HTS, ag) & 50 µm hastelloy
Rinter : 1 µΩcm2
FEM Model information:
Δx = 58 µm, Nx = 1201
Δt = 8 µs, Nt = 1201
Simulation time ~ 1h30min
Notes: Critical phenomena must be taken into account

## Slide 7: Classical FDM 1D model
G.A Levin., K.A. Novak and P.N. Barnes. “The effects of superconductor-stabilizer interfacial resistance on the quench of a current-carrying coated conductor”, Supercond. Sci. Technol., 23(1), p. 014021, 2010.
2-D problem (Silver, YBCO & Hastelloy layers) represented as 1-D problem:
Newton-Raphson method
Dufort-Frankel
discretization scheme
Homogenization
Sequential decoupled resolution:
:
…
Current sharing
equation
Heat equation
: Our Implementation
Current density inside HTS
Temperature inside HTS
Notes: Critical phenomena must be taken into account

## Slide 8: Physics-guided machine learning model
Dufort-Frankel discretization:
Function of T
Incorporation of Machine learning:
Let’s re-define:
Prefactors : Functions learned during training!
Heat equation
Machine learning: Only for heat equation
Notes: Critical phenomena must be taken into account

## Slide 9: schematic view of the model
PGRML cell
Physics-Guided Recurrent Machine Learning (PGRML) model
,
Key attributes:
General for any initial states
Independant of tape length (for a given architecture)
Only dependant on temperature seen in training
Neural Network
Inside the cell
Inputs
Outputs
Notes: Critical phenomena must be taken into account

## Slide 10: Model size & related information
For each NN:
[5,60,60,60,1]
Training time: ~12h
Activation function: ReLU
Dropout for hidden layers
MinMax Normalization
Not a fine tuned model
31 simulations:
23 training
1 validation
7 test
Loss function & recurrent predictions:
PGRML cell
k times
Optimization with respect to T !
Notes: Critical phenomena must be taken into account

## Slide 11: Solution on test set: PGRML vs FDM
FEM ~ 1h30min : (Δx , Δt) = (58 µm, 8 µs)
PGRML ~ 45s : (Δx , Δt) = (58 µm, 25 µs)
FDM: not accurate
Notes: Critical phenomena must be taken into account

## Slide 12: solution on test set: PGRML over time
t = 1.2 ms
t = 4.0 ms
t = 8.0 ms
Notes: Critical phenomena must be taken into account

## Slide 13: solution on test set: Current sharing
I = 177.3 A
I = 89.5 A
PGRML model is not trained on the current profile!
Notes: Critical phenomena must be taken into account

## Slide 14: solution on test set: Electric potential profile
I = 177.3 A
I = 89.5 A
PGRML model is not trained on the electrical potential !
Notes: Critical phenomena must be taken into account

## Slide 15: Long tape prediction with solution: METHODOLOGY
Test set
10x
2-D simulations
Spatial
Concatenation
Simu. 1
Simu. 2
Simu. 3
…
Simu. 10
0
L
2L
10L
x
Position along length
PGRML prediction as a whole:
1 initial condition, 1 simulation
0
10L
x
Position along length
Notes: Critical phenomena must be taken into account

## Slide 16: Long tape prediction with solution: Temperature
Simulation time:
FEM : 10x 1h30 = 15h
PGRML: 10min
90x Faster !
Notes: Critical phenomena must be taken into account

## Slide 17: Long tape prediction with solution: electric potential
Error accumulation:
Notes: Critical phenomena must be taken into account

## Slide 18: Conclusion
What’s next:
Complete cooling after hot spots appear
Variable interfacial resistance
Real critical current density distribution
3-D simulations and CFD architecture
Highlights:
Model based on a reduction in physical dimensionality & Machine learning
General for any initial state
No re-training required for length changes given an architecture
90x times faster than FEM
Notes: Critical phenomena must be taken into account

## Slide 19: Neural networks outputs values
5 inputs function!
+ 0.5
+ 1
+ 1.5
+ 2
T = [77, 320]
Notes: Critical phenomena must be taken into account