## Slide 1: Overview of the muon facility in MLF J-PARC
BRIDGE2023, 19/Oct/’23
J-PARC, MLF Div., Muon Sec. Naritoshi Kawamura

## Slide 2: Ｊ－ＰＡＲＣ
400 MeV linac
3GeV synchrotron (RCS)
30GeV synchrotron (MR)
Materials and Life Science Facility
Hadron facility
Neutrino facility
Nuclear transmutation research
(under design)
4 facilities
3 accelerators

## Slide 3: Materials and Life Science Facility
RCS (3GeV333mA)
MLF
Beam transport tunnel
Exp. Hall #1
Exp. Hall #2
Muon target
Spallation neutron target
Exp. Hall #1
Exp. Hall #2
100%
>90%
graphite
mercury
m
n
Cascade target
4 kW
21015 p/s

## Slide 4: Muon Facility in MLF, MUSE
Decay and surface muon （100 keV - 50 MeV） to answer a variety of users’ demands with mSR spectrometer (D1) general purpose (D2)
Ultra slow muon （0.1 - 30 keV） surface/sub-surface /interface sciences (U1A) Test-bench for TmM (U1B)
D-line
U-line
µ+
Surface muon （4 MeV）
dedicated to bulk µSR in 4 experimental areas w/ various sample env:
ultra-low temperature
high magnetic field
pulsed excitations etc.
S-line
µ+
High-intensity surface and high-energy cloud muon （<4 - 50 MeV） for general purpose “fundamental physics”
requiring high precision, high sensitivity
H-line
µ+/µ-
µ+/µ-
General Use
4 areas Simultaneous use
High Intensity General Use
Ultra Slow Muon
Surface/Interface

## Slide 5: MLF tour
Exp. Hall #2
#1
#2
Exp. Hall #1

## Slide 6
To disperse the radiation damage, 1% shrinkage / 1DPA (~0.5-year irradiation under 1 MW), and to prolong the lifetime, a rotating system has been applied since 2014.
Common property
  2-cm thick IG-430U from Toyo Tanso Inc., consuming 5% of protons
Different property
  direct water cooling (fixed) vs. radiation cooling (rotating)
  Max temp.: 1500 deg C (fixed) vs. 700 deg C (rotating)
Fixed target: ’08-’14
Num. of P.: 2500 MWhr.
Rotating target #1: ’14-’19
Num. of P.: 5800 MWhr.
Muon Production Target
S. Matoba’s poster

## Slide 7
Target: Collaboration between PSI and MUSE
The rotating muon production target was developed in a collaboration with PSI, which had developed the rotating target in advance. In PSI, they replaced the bearings with a new one developed in J-PARC, and one year of stable operation was achieved the last December, which is the best after a long period of several bearing failures. To commemorate it, PSI, KEK, and J-PARC jointly released the press.
A very good example of positive spiral between PSI and J-PARC.
We hope to keep this relationship.

## Slide 8: D-line: A decay/surface muon beamline
to D1
to D2
600 ns
100 ns
View of the control room
Improved performance with a new superconducting solenoid.
Larger warm bore (f12cm → f24cm) without window foils
D2: General purpose (open space) area
D1: mSR
Solenoid magnet replaced in FY2015
Kicker magnet
Septum magnet
p
m
Double pulse structure due to accelerator bunch
Each pulse is distributed to D1 and D2 areas with a kicker magnet.
Cold bore S.C. magnet (old)
Warm bore S.C. magnet (new)
Thermal-shield foils
m
p
m
p

## Slide 9
Y. Tanaka et al., Proc. 13th annual Meeting of Part. Accl. Soc. Jap.
(in Japanese)
D-line: The new S.C. solenoid magnet

## Slide 10: U-line: The highest intensity beamline for USM
NC large aperture capture solenoid
SC curved solenoid
SC focusing solenoid w/ wien filters
All beamline magnets are axial focusing
The world strongest pulsed muon: 2108 m+/s, 1107 m-/s
proton

## Slide 11
Y. Makida et al., CEC/ICMC2013 proceedings
DOI:10.1063/1.4860734
U-line: The S.C. curved solenoid magnet

## Slide 12
Y. Makida et al., CEC/ICMC2013 proceedings
DOI:10.1063/1.4860734
U-line: The S.C. focusing solenoid magnet

## Slide 13: U-line: Generation of Ultra slow muon (USM)
W(2000C)
S. Kanda’s poster
USM is generated by the laser resonant ionization method synchronized with the muon beam pulse.

## Slide 14
S-line: A surface muon beamline
Pulse mSR: Highly segmented spectrometer is necessary to avoid the distortion of time spectrum due to pileup.
Cf. 5-T magnet needs 3008-ch
S line is dedicated to transport surface muon beam. By using two kicker system, S line provides muon beams to all 4 areas simultaneously. At present two experimental areas, S1 and S2, were completed.
In the S1 area, a mSR spectrometer was placed.
The S1 area is one of the busiest ones, and users are switching every few days.
The S2 area is partially funded by Okayama-univ. group to perform high rescission measurement of the Mu 1s-2s level.
S1
S2
S3
S4
The 1st spectrum of 5-T magnet
S1
S2
Kicker
Kicker
P. Strasser’s poster

## Slide 15: H-line: Generic-purpose High-intensity beamline
Capture solenoid (HS1)
Bending magnet (HB1)
Gate valve (HGV1)
Transport solenoid
(HS2 and HS3)
↑beam transport tunnel
Kicker magnets and/or wien filers are installable
Septum or bending magnet (HB2)
Experimental area #2 and #3
+B
-B
Conceptual design was proposed by J. Doornbos, TRIUMF.
Adopting a new beamline concept which is confirmed by a particle tracking simulation, H line is designed to provide a high intensity beam with a wide-range momentum tunability to each of several areas.
This concept is inherited to 2nd TS.
Experimental area #1
3GeV proton
T. Yamazaki’s poster

## Slide 16
H-line: feature prospects
H1: fundamental physics studies
MuSEUM: high precession measurement of Mu HFS
DeeMe: m-e conversion search
…Mu1s-2s, Mu-antiMu, etc.
H2: realizing the muon re-acceleration from USM method for g-2/EDM and transmission muon microscope

## Slide 17
Accumulation
H line bldg. （plan）
g-2/EDM exp. Searching for BSM.
ＭＬＦ bldg.
H line
H2
H1
Transmission Muon Microscope
Observation of whole living cell owing to high penetration power of muon
H-line: feature prospects
Ｈ line bldg.
Ｈ1
Ｈ line
Y. Nagatani’s talk
M. Otani’s poster
Acceleration
Cooling

## Slide 18: “Specialties” of MUSE
High-intensity pulsed beam → beam distribution by kicker systems (S line) → devices synchronizing the pulse → flashlight etc. for mSR spectroscopy (SE) → ultra slow muon generation by pulse-laser → g-2/EDM exp., transmission muon microscope
pion generation by 3-GeV proton beam → relatively high yield of p- and thus m- → promotion of non-destructive elemental analysis → application to archeological artifacts etc.

## Slide 19
D-line
n + p  p- + X
p + p  p- + X
MUSE utilizes 3GeV proton, and the p- yield is higher than the other meson factories.

## Slide 20: Negative muon yield in MLF J-PARC
High negative muon yield owing to
• Beam transport with a window-less super-conducting solenoid
• Relatively high negative muon yield by 3 GeV proton
As low as 3.5 MeV/c
(58 keV)
For practical use
“The world’s strongest pulse” and “high negative muon yield” are our specialties that differentiate the other meson factories in the world.

## Slide 21
D-line: D2 area
In recent years, applying to archeological artifacts, etc, the fraction of the elemental analysis studies by m- has been getting increased in the D2 area.
HAYABUSA2 return sample, rocks of the asteroid RYUGU was analyzed in 2021.
the hemisphere chamber for the elemental analysis
100-pixel Ge
To answer such demands, the apparatus for the elemental analysis study has been developed.
m-
M. Tampo’s talk

## Slide 22: Four secondary beamlines
D line since 2008
  A decay muon beamline with a 6-m solenoid magnet for the p-m decay section, 2 experimental areas
U line since 2014
  Composed of only axial focusing magnets The highest-intensity surface muon beamline in MUSE dedicated to the Ultra Slow Muon beam
S line since 2014(S1) and 2021(S2)
  A surface muon beamline, 4 experimental areas (plan) answering a lot of users’ demands
H line since 2022(H1) and 2023(H2)
  A newly constructed beamline with a new concept realizing high intensity and high versatility

## Slide 23: Feature prospects
MLF 2nd target station
Combination of muon and neutron target inspired by F. Berg et al., PRAB 19, 024701 (2016)
“Target studies for surface muon production”
The first proposal was in 2017...

## Slide 24: MLF Target Station2
Muon:：
10 (target) x 5~10 (Muon capture solenoid)  50 ~100 times gain of flux
Neutron:
10 (target) x 2 (device)  20 times gain of brightness
Moderator & reflector
Neutron Focusing Devices
Neutron Detectors
Proton beam
Rotating tungsten target
Muon Capture Solenoid
Integrated neutron and muon target
6e+14
5e+14
4e+14
3e+14
2e+14
1e+14
0
0 2000 4000
Emission time (ms)
Brightness (n/cm2/sr/Å/s)
SNS TS2
ESS
J-PARC
TS1
SNS
J-PARC
TS2
Neutron Brightness
TS1
3GeV RCS
J-PARC TS2
TS2
Integration of neutron and muon sources (world's first)
J-PARC proton accelerator intensity (1 MW) increased to 1.5 MW
1 MW (17 Hz) for TS1 and 0.5 MW (8 Hz) for TS2
Brightness of MLF TS2 will be the world's highest compared to the next plan of overseas facilities
Chart: Energy [MeV]
This project was selected as one of “The Medium- to the Long Term Academic Research Strategy” by the Science Council of Japan although the budget has not been guaranteed yet.

## Slide 25: R&D for TS2
Integrated flux：7.71020 n/m2/y (@1 MW)
AVG. neutron flux at the top 100 mm of the coil
MC by PHITS
The requirement to TS2 Capture solenoid
Heat deposit: 650 W
Neutron flux: 7.71021 n/m2 for 10 yr.
Absorbed dose: 130 MGy
c.f. COMET-PCS (NbTi): 1~3MGy, 250W
HTS S.C. magnet must be realized.
REBCO (Copper oxide S.C.)
Irradiation test by TU Wien and KEK cryo. center
Conceptual design of HTS solenoid
The world‘s first practical HTS magnet Low operation and maintenance cost
Toward a sustainable facility

## Slide 26: Summary
So far, I hope my talk could be just a trigger to stimulate further discussions.
I am not confident in answering your questions correctly. But I am sure that I can introduce the responsible/suitable personnel.
Even if we can not answer at present, we can keep discussing it after this workshop.

## Slide 27
S-line: A surface muon beam line
S line provides muon beam to all 4 areas simultaneously.
Kicker+SY
Kicker+SY
S1
S2
S3
S4

## Slide 28
S-line: S2 area
The S2 area is partially funded by Okayama-univ. group to perform high rescission measurement of the Mu 1s-2s level.
S2
S1
The 1st beam was delivered to the S2 area on 14/Jul/’21.

## Slide 29: Time transient measurement
Application to time transient phenomenon
Transient response ranging 0.1 sec – 2-3 hour
Light exposure
pressurization
charging/discharging of battery etc.
Newly developed
New measurement method realized by 1-MW beam
5-h data

## Slide 30
(9.9±1.0)x107 μ+/s @1MW
~99% of the simulation
Preliminary
Surface muon intensity
Fitting function
Negative (cloud) muon intensity
σx = 44 mm
σy = 24 mm
A typical profile of surface μ+
Momentum of surface muons
estimated from μ+ range in Al target
P = 28.0 MeV/c
(RMS 1.2 MeV/c)
H-line: Commissioning of H1

## Slide 31: SC magnets in MUSE
Name | Aperture /mm | Length /mm | Ctr Field/T /Current/A | Bore type | Cooling method | Const. Cost /USD | electric/kW (op. cost) | Constructor
DS1 (old) | 120 | 6000 (50012) | 5/730 | Cold | Online facility He compressor +cooler | ? | ? | Mitsubishi
DS1 (new) | 216.3 | 6000 (50012) | 3.5/415 | warm | Online facility He compressor +cooler | 2M | 200 (cryo.) | Hitachi
HS2/HS3 | 597.6 | 1500 | 0.56/200 | Warm | GM cc 1 | 1M | 7.5 (GM) | Hitachi
U CS | Next page |  |  | Cold | GM cc 5 | 2.4M (w/o GM) | 7.5 5 (GM) | Toshiba
U FS | Next next page |  |  | warm | GM cc 6 | 2.5M (w/o GM) | 7.5 6 (GM) | Toshiba
 |  |  |  |  |  | P.S. is not included. | P.S. is not included. | 

## Slide 32: Near-Feature prospects
1st target station upgrade to 1.5 MW operation rewind the
Essentially, accelerator (ion source - RCS), proton beam transport (incl. M2 tunnel), neutron target, and their utilities will be modified.
Replacement of Q-triplets with SC solenoid magnets was also studied.
This may be similar to Super-μE4 except the final focusing magnet.

## Slide 33: Merit of (opposite field) solenoid
D
Epsx=37.5p cm mrad
Epsy=75.0p cm mrad
Epsx=235.2p cm mrad
Epsy=368.9p cm mrad
Epsx=554.0p cm mrad
Epsy=561.6p cm mrad
The fringe fields of Q magnets cause a large emittance growth.
H
Epsx~350p cm mrad(RMS)
Epsy~350p cm mrad(RMS)
Epsx~680p cm mrad(RMS)
Epsy~340p cm mrad(RMS) (The growth is due to FF Qs)
The use of Q magnet is minimized in the H line.