## Slide 1
Peter Kammel
Overview of piE5 Beamline
Intro
Test beam 2022 results
Modelling the beamline
Major upgrade studies

## Slide 2: Requirements Phase I
Rate
  300k π/s stopped in ATAR
Momentum bite
  ∆p/p <2%
Momentum
  lowest p preferred 55-70 MeV/c
Spot size
  smaller than ATAR Size of 20mm x 20mm
Particle contamination
  µ/e less than 10% of π

## Slide 3: Requirements and achieved results from test run
Rate 300k π/s stopped in ATAR 😁 ok at 65 MeV/c Momentum lowest p preferred 55-70 MeV/c
Momentum bite ∆p/p <2% 🙂 Probably not, requires more data analysis/beam modeling
Spot size smaller than ATAR 🙄 No, difficult, requires beam design and modeling experimental design, active collimation
Particle contamination µ/e less than 10% 🙂 Not yet, requires additional magnets, beam modeling and design
Take away
  Serious effort and resources for beam team required, beam design and simulation
  Student can make a big difference, see Stefan’s phase space analysis
  New machine learning approach, very promising but additional beam design effort required

## Slide 4: piE5 @ PSI - World’s Brightest Stopped Pion Beam
PIONEER
MEG
Mu3e
experimenters have full control over beam line (after first bend)
        carefully studied for fundamental muon experiments
still surprises for pions, unique PIONEER requirements

## Slide 5: Simple Transport Model
Compare Δp/p= 3/0 %
1st order only
  2nd order diverges
  other discrepancies to PIONEER Run ‘22
upstream part in shielding
    indirect diagnostics with slits
beam envelope in V-H planes
V
H
extraction, momentum selection and achromat
particle separation, focus on target
MEG tune adjusted to PIONEER geometry, P-R Kettle
BxE
D
20 cm
20 cm
p+
dipoles
separator

## Slide 6: Puzzles from beam test
Explore/explain most striking puzzles, problems
strong
dispersion
beam meandering
significant dispersion
insufficient focus
cannot achieve PID separation and target focus simultaneously

## Slide 7: Summary of findings
Final focus
PID
Dispersion? at target
Δp/p two methods
  TOF
    16m beamline
    1% Δp/p ~ 1 ns (65 MeV/c)
  Direct stopping measurement with range curve
    pion signal amplitudes with different degraders
    use π→ μ sequence to identity stops
  analysis needed

## Slide 8: G4BL steps
Production
  brute force high-statistics runs of (inefficient) pion production 25k ev/s, but only 3E-5 eff.
  phase space stored at virtual plane before first piE5 quad
Transport through channel to target
  Slower, but more efficient 1060 ev/s, 327E-5 eff.
  reasonable parameter variations guided by experimental tunes
More resource links in backup

## Slide 9: Initial studies, January 2023
Global properties
  twiss and sigma
    twiss mu3e_pion
    twiss orig_mu3e
    sigma mu3e_pion
Histograms (all 65 MeV/c)
  Tune Mu3e_22, HSC42 off MeV/c
    all vs pi
    pi vs pi_end
  Pioneer_65 MeV/c
    all vs pi
    pi vs pi_end
  Pioneer_22 vs Mu3e_22
    pi
    pi_end
  Orig_18 vs Mu3e_22
    pi
    pi_end
end QSK73
no strange beam effects a'la Zack

## Slide 10: Global properties: Envelopes
G4BL
TRANSPORT

## Slide 11: Higher order effects: X vs X’
very preliminary
π to target cut

## Slide 12: Higher order effects: X vs Pz
Dispersion?
very preliminary
π to target cut

## Slide 13: Major upgrade: Extend Beam with Two Vertical Foci
For particle separation and target focus two separate foci required, so that background is rejected outside of detector
  1st focus separates particles after ExB velocity filter and reject μ and e on collimator
  2nd focus is a double x/y focus aimed at ATAR
First attempt with s-t promising
  large final magnet
  phase space
    initial x: 2.40 π mm r y: 0.09 π mm r
    promising final focus
200
!

## Slide 14: Upgrade: Smaller Momentum Bite
exercise in history

## Slide 15: Beam Development Plan
Major upgrade studies needs beam designer
  Two vertical foci
  Large final magnet for small focus?
  upstream retune for large dispersion
  dE/dx π/μ/e separation?
Higher order calculations and corrections
  modern programs: G4BL,COSY
  more careful G4BL
    are non-linear effects correct and real?
Beamline
  downstream
    easier as more accessible
    measure phase space right after bends
    Based on PIONEER run '22, we cannot improve quality with downstream tuning alone
  upstream (Andy et al)
    systematic simulation campaign
    systematic measurement campaign to verify simulation and magnet characteristics
  phase space measurements need large tracker
Run analysis of low hanging ? fruits
  Δp/p
  dispersion dependencies

## Slide 16: Backup
10/14/2023 1:25 PM

## Slide 17: G4BL overview
Status
  complete model based on previous PSI work
  Repo of input field maps
  Reconstructed different historical I to B translations
  see beam team TWiki
Resource links
  Urs
  displays
  production

## Slide 18: Good Enough Focus ?
Beam behaves as expected (basic p scaling)
  we measured 28 MeV/c muons and
  pions of 55, 65 and 75 MeV/c
Pions better focus than surface muons
But only 46% of beam in ATAR box
AST/ASC combination not problematic
Not yet

## Slide 19: Sufficient Rate and Small ∆p/p ?
Cannot answer without determination of ∆p/p
First impression
  55 MeV/c insufficient
  65 MeV/c enough rate
Longitudinal phase space (i.e. ∆p/p), two methods being analyzed
Time of flight
16m beamline
1% Δp/p ~ 1 ns (65 MeV/c)
Direct stopping measurement with range curve
pion signal amplitudes with different degraders
use π→ μ sequence to identity stops
degrader
scintillator
signal amplitude in scint.
μ
π

## Slide 20: Particle Separation Good Enough?
In area restricted to ATAR
(optimistic accounting)
e: 25.0%
μ: 32.1%
π: 42.9%
amplitude in scint.
TOF (ns)
No location of collimator !
Separator HV can be increased
π
μ
e
Patrick
Josh

## Slide 21: Dispersion at Target Location?
TOF changes when when detector moves 5 cm to the left
X=X(P), significant dispersion D at target location, deteriorates focus.
Patrick

## Slide 22: Dispersion at Target Location?
D~1 cm/%
similar to dispersive section??

## Slide 23: Higher order effects: X vs X’
very preliminary

## Slide 24: Dependence on tune
Mu3e tune
Pioneer tune

## Slide 25: Dependence on tune
Mu3e tune
Pioneer tune

## Slide 26
PIONEER