## Slide 1
Peter Kammel, Tim van Wechel, David Peterson
Readout Board and Mechanical Support for Atar
16-channel
5000 channels
This is planning exercise
to stimulate internal discussion
Strategy for development path

## Slide 2: Sensor “packaging” options: LGAD modules
Proposal
  20 x 20 x 5.76 mm
  48 sensor layers with 120 µm thickness
  12 flex cables to each side
Doug: Pacman
BNL
Xin

## Slide 3: Sensor “packaging” options impact design
Peter
Simone: combine several sensors to module with TSV
Double LGAD, F. Carnesecchi et al.
50 µm sensors connected on strip, HV plane
Smaller pi/mu ΔE seen by each gain layer
50µm
100µm

## Slide 4: Strategy
Start
UCSC board and FAST2 chip
Step1
Flat proto frontend board pFEB, UW
Step2
pFEB with minimal board spacing. Few mm gaps between pFEBs and sensor modules.
Step3
Step4
FEB0, Rigid-flex board with minimal thickness retracked behind ATAR.
pFEB with flex between sensor and amplifier. No gaps.
First transmission LGAD board
Baseline goal before 2026 shutdown
Stretch goal before 2026 shutdown
Pre-production prototype

## Slide 5: Start: UCSC board and FAST2/3
Hardware
Specs (Tim's talk)
  Dynamic range limited FAST2/FAST3
  Other ASICs in future
    Anadyne
    Nalu
16

## Slide 6: Step1: Flat pFEB, Quadrant
Layout
  Status
    Design done
    Routing in progress, review this week
Geometry
LGAD, 100 strips
2 FAST3 chips,
Total 32 channels
Micro-coax analog signals
Bias, to be soldered later
Digitial and support
Micro coax connector 1 mm
Board height 1.5mm
Wire bonding

## Slide 7: Step2: Complete Flat pFEB
Goal of pFEB:
  4 sensors,
  32 channels/sensor, 128 total (need LGAD,FAST3 production funding)
  Full particle transmission
  Mechanics
  Test run with pi/mu in 2026
Not a tight stack
  mm gaps between 4 sensor modules
FEB stack will be mounted on mother board
4 boards= 1/3 ATAR, 1/6 electronics

## Slide 8: Step3: pFEB with flex and tight sensor stack
Need to design working flex cables LGAD – FAST chip (or FAST close to LGAD?)
Increase board opening and connect to tight stack
16 LGADs, 0.12*16= 1.92 mm
flex cables
flex cables

## Slide 9: Step4: Rigid-to-flex board with minimal thickness
Tilt boards relative to LGAD stack
  Rigid-to-flex construction
  4-8 board modules with TSV big advantage
    wire bonds in planes separated by 0.5-1 mm
    Bias on same plane for all LGADs in module
    All modules identical wire bonding and cabling
  Mounting structure which supports flex cables
ATLAS
1 LGAD and flex per FEB.0 quadrant

## Slide 10: FAST 2/3 ASIC
Each chip
  two groups of 8 channels, 16 channels total
Each channel has two gain stages
  variable gain transimpedance amplifier (TIA)
  second stage output amplifier with ac coupling between stages and gain ~4.8.
Each transimpedance amplifier:
  three software selectable feedback resistors, 5.3, 11.6 (nominal), 31.6 kΩ.
  Nominal gain
    TIA stage is11.6 kV/A
    at the output is ~ 55 kV/A.
    The bandwidth at the nominal gain setting is 550 kHz to 470 MHz.
Noise: At the nominal gain setting the noise voltage
  at the TIA output was simulated to be 770 uV RMS
  and 2.7 mV RMS at the output.

## Slide 11: Design consideration and implementation I collaboration UW-UCSC
pFEB has two FAST2/3 chips, 32 channels, UCSC demo board single FAST2 chip
The design was split into two boards (trying to minimize electronic close to LGAD)
  the triangle shaped front end board (pFEB)
  Motherboard with most of the support
Boards connected by two CABLINE-CA multi conductor Micro-Coaxial cable assemblies
  40 position cable for the output and test pulse signals
  30 position cable for the power, control and bias signals
pFEB board

## Slide 12
Motherboard/Breakout board
  ac coupling capacitor
  MMCX connector output channel to digitizers.
  FAST2/3 outputs are ac coupled due to ~700 mV dc bias on the output signals.
Separate TIA Ibias current for each section of eight channels Original board had the TIA Ibias inputs of both sections connected together so not well defined how current splits between the two sections.
Design consideration and implementation II collaboration UW-UCSC

## Slide 13: Schematics
pFEB
Motherboard

## Slide 14: Very preliminary layout
to be reviewed this week

## Slide 15: Backup
10/13/2023 8:48 PM