## Slide 1: Evolution of Alternative ATAR Design
Xin Qian
BNL

## Slide 2: Comparison of Key Parameters
Previous Design
120 um layer thickness, 48 layers, 200 um strip pitch, 100 strips per face, two-sided X-Y readout
PIN technology
Separate readout  9600 channels
6 ns shaping time electronics
Distance between adjacent layers ~25 um
Rectangular Geometry
New Design
120 um layer thickness, 48 layers, 200 um strip pitch, 100 strips per face, two-sided X-Y readout
PIN technology
Shared readout  4900 channels
~20 ns shaping time electronics, cold electronics technology preferred
Distance between adjacent layers ~ 2 um
Pyramid Geometry

## Slide 3: Considerations of Alternative ATAR Design
Requirement of in-situ πeν tail measurements for all positron directions
  Relax requirements on the dead materials that need to be minimized
Acceptance of πμν and πeν both defined by ATAR only
  Pion stopping point + positron direction (e.g. 5-hit)
Trigger scheme of πeν events
  Coincidence time and position, also energy (not dE/dx) cut based on topology to suppress πμν
< 100 um position resolution
2D position determination for each layer enabled by 2-sided readout  better dE/dx
O(100) ps track timing resolution
Good energy resolution to separate π vs. μ and (μ+e) vs. e through dE/dx
  Suppress μDIF, πDIF, DAR for tail determination
  No complication of gain
  Aim for the lowest electronics noise > 9:1 (90:1) S/N for MIP (μ/π)
  Also important for the trigger design

## Slide 4: Detector Capacitance Estimation
Important for the electronics noise (S/N > 9:1 for MIP >~ 1.25 fC or 7800 electrons)
  Viability of PIN vs. minimal gain of LGAG
6 e- /pF@ 1 us shaping @ room temperature
  @ 20 pF, 20 ns shaping time gives us ENC 850 or > 9:1 for MIP w. PIN
  At LXe temperature (~4 e/pF), ENC ~ 570 or >13:1 for MIP w. PIN
Low detector capacitance is preferred
Cold electronics is preferred
Sensor from Gabriele Giacomini
FLEX cable from Simone
Equivalent Noise Charge

## Slide 5: Considerations of (Electronics) Cross Talk
Cross talk from the readout electronics
  Cct: coupling capacitance ~ 3 pF for adjacent chs
  Rin: input inpedence ~ 40 Om
  tp: shaping time of electronics
@ 1 ns tp, the cross talk will be ~ 20%
  Also, potential coupling with channels far away
  Significant effort in calibration is required
@ 20 ns tp, the cross talk will be ~1%
Sensor from Gabriele Giacomini
FLEX cable from Simone

## Slide 6: Impact of 20 ns Shaping Time
Required by small electronics noise level for PIN and minimization of the electronics cross talk
Difficulties in separating double hits, if time separation << 20 ns
Existing studies suggest that we can identify two hits with
  Tail fraction does not depend on !
  Lower but still sufficient statistics for tail determination [20,78] ns  41% of pion decays Pienu experience [5,35] ns  56% of pion decays Need more than 2% overall efficiency after selection assuming 1% πeν tail fraction

## Slide 7: Considerations of Gaps between ATAR layers
Existing simulation assumes a very small ~ 1 um gap between adjacent ATAR layers
Current reference design has 25 um gap
Existing study suggests that gap would hurt the background rejection (x2-3 worse)
Minimize the gap in ATAR design
Also, consideration of detector capacitance
  For the original 2-sided readout (9600 channels), minimizing the gap between layers will lead to significant increase of the detector capacitance  PIN option is no longer viable
  Shared readout concept (4900 channels)
e
h
h
e
A
B
C
ab
bc
We have the following signals
  All information are recorded and can be solved (e.g. Wire-Cell concept in LArTPC)

## Slide 8: Consideration of Mechanical Structure
Pyramidal structure is required
  Guard rings that avoid breakdowns at the edge of sensor
  Wire bonding for signal readout

## Slide 9: R&D Needed for the Alternative ATAR Design
Development of Electronics
Modification of LArASIC for PIONEER
  Redesign LArASIC from 180-nm to 65-nm technology is in progress
    Minimal shaping time 500 ns
    Dynamic range & linearity over 12-bits
    Optimized for 200 pF det. capacitance ENC ~ 600
  Modification of shaper circuit can satisfy the need of PIONEER (~ 20 ns)
  Preamp part does not meet the need though
  Modification of preamp is needed, but no showstopper observed
Mechanical Structure (Concept)
From Gabriele
Also input from Aleksey
Key is to minimize the gap between the adjacent layers ~ 2 um

## Slide 10: Expected Milestones of Physics Performance of Alternative Design
Demonstrate the in-situ tail fraction measurement with the current design parameters
  Iteration with variations on design parameters
Demonstrate the acceptance difference between πμν and πeν using ATAR only
Provide guidance and requirements on the Trigger Scheme
Requirement of in-situ πeν tail measurements for all positron directions
  Relax requirements on the dead materials that need to be minimized
Acceptance of πμν and πeν both defined by ATAR only
  Pion stopping point + positron direction (e.g. 5-hit)
Trigger scheme of πeν events
  Coincidence time and position, also energy (not dE/dx) cut based on topology to suppress πμν

## Slide 12
A variety of flip-chip techniques can be used
Interconnecting large area strips seems like a simple task – we need to find a suitable technic and tune the process
  How it works: Small bumps, balls, or solder preforms are deposited on metalized strips of the first die
  The second die is inverted to bring the solder bumps down onto strips of the first die
  Solder is re-melted to produce bonding, typically using a thermosonic bonding or alternatively reflow solder process, T < 300 C
  Just a few bonds will be enough, e.g., to bond a 1x1 cm2 SiPM for nEXO we use 6 50-micron bumps
An important question is about gaps between the dies
Test for thermal expansion
Bonding materials:
Solder – use fluxless solder, potential diffusion in Si
Conductive epoxy – potential contamination of LAr
Bumps
Interconnecting Si strip detectors
Solder balls
Solder preforms
Done Pinelli (pinelli@bnl.gov) is an expert in bonding and interconnection at Instrumentation
James Clayton President & CEO at Polymer Assembly Technology, Inc.
From Aleksey

## Slide 13
P(N)-strips
oxide
aluminum
ENIG
1) Complete the fabrication of the layers of micro-strips, test and select good devices.
2) Deposit an Under Bump Metallization (UBM) by ENIG (Electroless Nickel Immersion Gold) soon available at BNL.
3) Evaporation of thin layer of Indium in lift-off process
Thick photoresist
Indium

## Slide 14
4) Lift-off (removal of photoresist and indium externally to pads)
Indium
5) Flip-chip and connection of two strip layers together