## Slide 1: Magnetic Measurement Activities by the ID Group at the National Synchrotron Light Source-II
6-11 October, 2024
IMMW23
Toshi Tanabe (NSLS-II Insertion Devices Group Leader)

## Slide 2: NSLS-II:ID Group Staff
  Sr. Physicist (Group Leader)
    Toshi Tanabe Ph.D.
  Sr. Physicist (Deputy)
    Dean Hidas Ph.D.
    (Spectral calc., Controls)
  Physicist
    Marco Musardo (Mag. Meas)
  Lead Mechanical Engineer
    James Rank (Ring WCC, LOTO, Maintenance)
4
  Electrical Engineer
    Brian Eipper
  Mechanical Engineer
    Thomas Brookbank
  Electro-mechanical Technician
    Dan Migliorino
  Electro-mechanical Technician
    Bryan Holland

## Slide 3: Outline
National Synchrotron Light Source-II (NSLS-II) Current Status
  Storage Ring Status & Beamlines
  Installed Insertion Devices and Other Magnetic Devices
Magnetic Measurement Facility
  Flip Coil bench upgrade
  Pulsed wire bench upgrade
HEX-Superconducting Wiggler
  Device, Operation and Maintenance Issues
  Measurement system
SC-Adaptive Gap Undulator
  Concept & Development Plan
  Magnetic Measurement Plan
Other Development for Future Upgrade
  Complex Bend Lattice for Upgrade
  New Flip Coil, Rotating Coil and In-Vacuum Pulsed Wire bench
Summary

## Slide 4: NSLS-II Current Status
Storage Ring Status & Beamlines
Installed Insertion Devices and Other Magnetic Devices

## Slide 5: NSLS-II Storage Ring &Beamlines
https://www.bnl.gov/nsls2/
 | Bare Lattice | 3DW Lattice | All-ID w.o SCW | All-ID with SCW
Energy (GeV) | 3 |  |  | 
Circumference (m) | 791.958 |  |  | 
Emittance ex (pm-rad) | 2086 | 957 | 747 | 657
Energy Spread sd (%) | 0.0514 | 0.0818 | 0.0799 | 0.093
Energy Loss per Turn U0 (keV) | 286.4 | 649.1 | 831.8 | 958
Length of Long Straight (m) | 9.3 |  |  | 
Length of Short Straight (m) | 6.6 |  |  | 
bx, by at Long Straight Center (m) | 20.1, 3.4 |  |  | 
bx, by at Short Straight Center (m) | 1.8, 1.1 |  |  | 
Betatron Tunes nx, ny | 33.2, 16.26 |  |  | 
Natural Chromaticisty xx, xy | -98.5, -40.2 | -98.4, -39.8 | -98.4, -39.9 | -98.2, -40.1
Momentaum Compaction ac | 0.000363 |  |  | 
Radiation Damping Time tx,ty, ts (ms) | 55, 55, 28 | 24, 24, 12 | 19, 19, 9.5 | 16.6, 16.6, 8.3
RF Frequency (MHz) | 499.681 |  |  | 
Number of RF Buckets | 1320 |  |  | 
Number of Bunches | 1056 |  |  | 
Time between Bunches (ns) | 2 |  |  | 
Total Beam Current (mA) | 400 (500) |  |  | 
Average bunch current (mA) | 0.47 |  |  | 
Average bunch charge (nC) | 1.25 |  |  | 
Synchrotron Tune @ VRF = 3 MV | 0.00871 | 0.00862 | 0.00856 | 0.0085
RMS Bunch Length @ VRF = 3 MV (mm) | 2.7 | 4.34 | 4.27 | 5.02
NSLS-II Ring Parameters (as of Aug. 24)
3IDs for
NEXT-II
~5-7 IDs for
NEXT-III

## Slide 6: NSLS-II Insertion Devices Current Installation
2 x 3.0m-In Vacuum Undulators (IVU20)
1 x 3.0m-IVU22 (LS)
3 x 1.5m-IVU21s (two for canted configuration)
2 x 2.8m-IVU23s (canted : LS)
1 x 2.8m-IVU23 (LS)
1 x 1.0m-IVU18 (canted)
7 x 1.13T-3PW
3.4m Damping Wigglers in tandem configuration
3m-IVU20 for HXN beamline
6 x 3.4m-Damping Wigglers W100s (LS)
2 x 2.0m-Elliptically Polarizing Undulators (EPU49)
1 x 2.8m-Quasi-period EPU105 and 1 x 1.4m-EPU57 (in-line configuration)
1 x 3.5m-EPU57 (LS)
1x1.6m-U42 and 1x 1.0m-EPU60 (canted)
1 x 3.5m-U68 (LS)
1 x 1.2m-Superconducting Wiggler (SCW70)
15 Different types of Insertion Devices to maintain.
LS: Long Straight

## Slide 7: ID Magnetic Measurement Facility (ID-MMF)
Current Measurement Systems
Upgrade of Flip Coil Bench
Upgrade of Pulsed Wire Bench

## Slide 8: Hall Probe Bench
Senis 3D Hall Probe
NI CompactRIO

## Slide 9: Current Flip Coil Bench
ADC Linear Stages and Yasukawa rotary drive
Achieve 1st Integral Repeatability: ~ 2 G.cm for 4 m long ID

## Slide 10: New Flip Coil Bench
Newport XPS-D Controller

## Slide 11: New Pulsed Wire Bench
Old bench at NSLS
New bench

## Slide 12: Old Pulsed Wire Bench at the NSLS
Trajectory at 64 MeV
VISA Undulator
Before
After

## Slide 13: New Pulsed Wire Bench
Courtesy of A. Khan and P. N’gotta
N’gotta, P., Ebbeni, M., Thiel, A., & Tarawneh, H. (2019, June 1). First Results of a Pulse Wire Measurement System for ID Characterization at MAX IV .
Photodiode (DET10A2) + Amplifier (PDA200C)
Load Cell to Measure Wire Tension
Agilent 33220A & linear amplifier (AE Techron)
Raw Data
After Processing
Hall Probe Data
Global Laser (Beta TX)
1st Integral
2nd Integral

## Slide 14: HEX Superconducting Wiggler
In-Vacuum Flip Coil Measurement for Integrated Multipoles & SCW Specs
In-Vacuum Hall probe bench

## Slide 15
HEX-SCW Mag. Meas. by In-Vacuum Flip Coil
Using COTS in-vacuum XY stages (Kurt J. Lester, XY31-31065-001) and rotary feed-throughs (UHV Design, MD40-31065-001)

## Slide 16: HEX-SCW Mag. Meas. by In-Vacuum Hall Probe Bench
T. Tanabe, et. al.,”Development of the high energy engineering X-ray (HEX) superconducting wiggler, magnetic measurement, installation, and commissioning”, Review of Scientific Instruments 94, (2023): https://doi.org/10.1063/5.0146964

## Slide 17: New Flip Coil Bench
Newport based design with continuous rotation

## Slide 18: New Flip Coil Bench
Integration with Newport Stages
DAQ with Ni CompactRIO with FPGA
Continuous rotation possible for the use of a lock-in amplifier
Iy
Ix

## Slide 19: SC Adaptive Gap Undulator
Concept &Magnetic Design
Measurement Plan

## Slide 20: Segmented Adaptive Gap Undulator (SAGU)
Normal
CREU
SAGU
Constant Resonant Energy Undulator
(S. Gottschalk, 2000)
Assembled PM-SAGU segment by
Insertion Devices group at BNL
SC-SAGU vacuum chamber analysis

## Slide 21: SC-AGU Magnetic Design
 | Segment 1 | Segment 2&3
Period length (mm) | 14.0 | 15.5
Number of periods | 30 | 26
Coil crosssection (mm2) | 38.4 | 38.4
Engineering current densiy (A/mm2) | ~1700 | ~1700
Pole width in Z (mm) | 2.2 | 2.95
Pole height (mm) | 8.0 | 8.0
Length of SC wire (m) | ~1940 | ~1675
Max effective K | 2.2 | 2.05

## Slide 22
SC-AGU : Magnetic Measurement Option
Plan A: Use vertical measurement system with Liquid Helium
  New small Hall probe (Senis ???) is planned to be used.
Plan B: Develop conduction cooled measurement bench using In-Vacuum Magnetic Measurement System (IVMMS).
Insulating Vacuum
Chamber Appendage
(by CS)
Core Support Girder
(by CS)
Core Stand
(from B832 granite pillars)
IVMM Chamber
(Toyama IVMM)
Isolate Granite Block
(Toyama IVMM)
Sumitomo 418CH
(from HEX spares)
Kinematic Base
(Toyama IVMM)
Mechanical
Feed-Throughs
(commercial)
Vertical Hall Probe
(from B832, SMD?)
IVMM 1.75m Z Stage
(Toyama IVMM)

## Slide 23: NSLS-II Upgrade R&D
Complex Bends Lattice
Small Aperture Rotating Coil Bench
Gradient Permanent Magnet Quadrupole

## Slide 24: NSLS-IIU Complex Bend Lattice
History of Complex Bend development
Complex Bend concept
(Interleaved dipoles and quadrupoles)
G. Wang et al., PRAB 21,(2018)
Superconducting magnet design (B=1.05T, G=500T/m)
Decoupled Dipole-Quadrupole magnets (B=0.25-0.5 T, G=±250T/m)
G. Wang et al., PRAB 22,(2019)
Combined Function Dipole-Quadrupole PMQs (B=0.25-0.5T, G=±130T/m)
Halbach type
Hybrid type
S. Brooks et al., PRAB,(2020)
P. N’Gotta et al., PRAB,(2016)
T. Shaftan et al., Complex Bend II, BNL-211223-2019-TECH, Oct 2018
T. Shaftan, Methodology for designing Complex Bend lattice, BNL-223858-2023-TECH, Jan 2022

## Slide 25: Rotating Coil Bench
12 mm diameter rotating coil with 1.8 mm thick printed circuit board, wiring, and ceramic bearings.
Small Permanent Magnet
Quadrupole for complex bend

## Slide 26: Halbach Magnet Development- Prototypes, Test
CB concept successfully tested at NSLS-II linac
diagnostic beamline 100-200 MeV electron beam energy
S. Sharma et al.
Vacuumscmelze magnet prototype
In-house magnet prototype
In-house PMQ prototype measurement
1 defocusing magnet assembly successful
1 focusing assembly foreseen
9 defocusing magnets assembly procured
6 focusing magnets assembly procured
Normalized
Absolute
High sextupole component (b3)
Assembly error (800 um error for vgap)
Modification of the aperture spacer

## Slide 27: Summary
  The NSLS-II ring currently has 29 beamlines and running with 660 pm.rad emittance. Plan to construct 8-12 new beamlines over the next decade.
  Magnetic measurement systems for SCWs (with less than 2 m) have been developed.
  SC-AGU prototype is under construction. The minimum gap at the center is 3 mm.
  A new flip coil bench with continuous rotation capability has been developed.
  The measurement system for a 4.4 m long CPMU is planned.
  Research and developments for complex bend lattices for future NSLS-II ring upgrade are in progress.
20