## Slide 1: Update muX meeting 12/01
Marie Deseyn

## Slide 2: Fit with proper lineshape

## Slide 3: Fit with proper lineshape
Realized that Roofit somehow is extremely slow on (only) my laptop  do it now on the KU Leuven cluster

## Slide 4: Fit with proper lineshape
Fit two peaks in the silver spectrum with sigma = a*E+b where a and b are simultaneously fitted for the two peaks

## Slide 5: Fit with proper lineshape
Fit two peaks in the silver spectrum with sigma = a*E+b where a and b are simultaneously fitted for the two peaks
BUT background of two peaks is the same
(since we fit the total function, gaussian goes to zero far from centroid but constant background does not)

## Slide 6: Fit with proper lineshape
Use TSpectrum to estimate full background: Background(spectrum, numberIterations,"Compton");
numberIterations = 40
numberIterations = 20

## Slide 7: Fit with proper lineshape
And fit background subtracted spectrum (only using 3 runs):
numberIterations = 40
numberIterations = 20

## Slide 8: Fit with proper lineshape
And fit background subtracted spectrum (only using 3 runs):
numberIterations = 40
numberIterations = 20

## Slide 9: Fit with proper lineshape
And fit background subtracted spectrum (only using 3 runs):
numberIterations = 40
numberIterations = 20

## Slide 10: Fit with proper lineshape
And fit background subtracted spectrum (only using 3 runs):
numberIterations = 40
numberIterations = 20

## Slide 12: Simultaneous fit
Shared A, b and f_v
Fit over whole range instead of two peaks seperately

## Slide 13: Simultaneous fit over separate ranges
Made it work in simple case of 2 gaussians near each other sharing the sigma

## Slide 14: Simultaneous fit over separate ranges

## Slide 15: Simultaneous fit over separate ranges for silver data – PROBLEMS
Takes very long time (even if I fit one peak where the range I put is equal to the range of the E param or thus the range of the ‘normal’ fit)

## Slide 16: Simultaneous fit over separate ranges for silver data
Fit with two gaussians and Chebyshev polynomial background in 2 ranges:
Takes about 1.5 min

## Slide 17: Simultaneous fit over separate ranges for silver data
Add with t(E):
Very slow > 30 min

## Slide 18: Simultaneous fit over separate ranges for silver data
Fit with two gaussians where sigma = a*E+b with a and b = for both peaks

## Slide 19: Simultaneous fit over separate ranges for silver data
Fit with two gaussians where sigma = a*E+b with a and b = for both peaks
This is without clipping, so in fact the constant backgrounds add up  Investigate clipping  Clipping increases the calculation time drastically  (without clipping, the algorithm is done in <1min)
Sig[ii] = new RooGenericPdf (sig_name.str().c_str(),"(exp(-((@0 - @1)/(@2)) * ((@0 - @1)/@2)/2) /(@2*2.5) + (@0 > @4)*(@0 < @5) * @3)",RooArgList(E,*mx[ii],sig, *constback[ii], *Roodown[ii], *Rooup[ii]));

## Slide 20: Simultaneous fit over separate ranges for silver data
Fit with two gaussians where sigma = a*E+b with a and b = for both peaks
This is without clipping, so in fact the constant backgrounds add up  Investigate clipping  Clipping increases the calculation time drastically  (without clipping, the algorithm is done in <5sec)
Sig[ii] = new RooGenericPdf (sig_name.str().c_str(),"(exp(-((@0 - @1)/(@2)) * ((@0 - @1)/@2)/2) /(@2*2.5) + (@0 > @4)*(@0 < @5) * @3)",RooArgList(E,*mx[ii],sig, *constback[ii], *Roodown[ii], *Rooup[ii]));

## Slide 21: Simultaneous fit over separate ranges for silver data
After ~1h
Seems like the clipping did not work…

## Slide 22: Effect of anti-coincidence window size
Saw some interesting things, but I first want to doublecheck my ELET optimization

## Slide 23: Effect of anti-coincidence window size
t
muon
tLow
tHigh

## Slide 24: Effect of anti-coincidence window size
899keV (muonic gold x ray(nf-3d))

## Slide 25: Effect of anti-coincidence window size
899keV (muonic gold x ray(nf-3d))
Effect of tLow and tHigh is rather similar  expected since muonic gold x ray is ‘continuous’ and thus just cutting more events

## Slide 26: Effect of anti-coincidence window size
899keV (muonic gold x ray(nf-3d))
Effect of tLow and tHigh is rather similar
There seem to be two peaks not sure what the rightmost peak corresponds to??

## Slide 27: Effect of anti-coincidence window size
899keV (muonic gold x ray(nf-3d))
Effect of tLow and tHigh is rather similar
There seem to be two peaks not sure what the rightmost peak corresponds to??

## Slide 28: Double peak near 899keV
899keV (muonic gold x ray(nf-3d))
Effect of tLow and tHigh is rather similar
There seem to be two peaks not sure what the rightmost peak corresponds to??  very clear in Ge03

## Slide 29: Double peak near 899keV
Rightmost peak looks partially dependent on muon

## Slide 30: Double peak near 899keV
Rightmost peak looks partially dependent on muon
Could it be the 900.7keV Ag muonic x ray?
Compare to other Ag muonic x rays (870keV one also overlaps with Au, 1171keV overlaps with Co calibration source)

## Slide 31: Double peak near 899keV
304keV and 308keV (Ag muonic x ray) peak are completely gone for larger anticoincidence windows  completely muon related, while at 899keV the rightmost peak does not completely disappears???
Only partly Ag peak that is leaking in

## Slide 32: Double peak near 899keV
Is it hyperfine splitting of Au?
Check by taking events in muoncoinc spectrum that have GeTime>10000ns or GeTime<-5000ns and compare to spectrum that is also in coincidence with Au 3d3/2  2p1/2 or 3d5/2  2p3/2
At 305keV and 308keV it gives strong suppression

## Slide 33: Double peak near 899keV
Fit with [0]*exp(-0.5*((x-[1])/[2])**2) + [3]*exp(-0.5*((x-[4])/[2])**2) + [5]
I want to test this for multiple timecuts to see if the p3/p0 ratio without the coincidence with Au 3d3/2  2p1/2 or 3d5/2  2p3/2 decreases when the coincidence is required

## Slide 35: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
tLow has more impact (for all of the detectors separately too)  time window after muon dominates

## Slide 36: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
tLow has more impact (for all of the detectors separately too)  time window after muon dominates

## Slide 37: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
tLow has more impact (for all of the detectors separately too)  time window after muon dominates

## Slide 38: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
tLow has more impact (for all of the detectors separately too)  time window after muon dominates  Go to negative tHigh to investigate possible shift

## Slide 39: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
It looks like the peak is shifted in time wrt muon:

## Slide 40: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
It looks like the peak is shifted in time wrt muon:

## Slide 41: Effect of anti-coincidence window size
74.4keV, 88.4keV, 93.4keV, 95.8keV = C muonic x rays (np-1s)
It looks like the peak is shifted in time wrt muon
BUT in fact it is because of the jump in the ELET algorithm when the threshold is no longer reached

## Slide 43: Effect of anti-coincidence window size
305 keV and 308.5keV (Ag muonic x rays, nf-3d)
tHigh has stronger effect  time before muon ???

## Slide 44: Effect of anti-coincidence window size
305 keV and 308.5keV (Ag muonic x rays , nf-3d)
tHigh has stronger effect  time before muon ???
tLow also has reasonable impact

## Slide 45: Effect of anti-coincidence window size
305 keV and 308.5keV (Ag muonic x rays , nf-3d)
tHigh has stronger effect  time before muon ???
tLow also has reasonable impact
For tLow = -500 ns or tHigh = 500 ns, the muonic silver x rays are almost completely gone

## Slide 46: Effect of anti-coincidence window size
305 keV and 308.5keV (Ag muonic x rays , nf-3d)
tHigh has stronger effect  time before muon ???
tLow also has reasonable impact
 per det

## Slide 47: Effect of anti-coincidence window size – 305keV peak

## Slide 48: Effect of anti-coincidence window size – 305keV peak
Only one run  not always enough statistics

## Slide 49: Effect of anti-coincidence window size – 305keV peak
Not enough statistics | tHigh increase gives strongest decrease | ¦tLow¦ increase gives strongest decrease
Ge05, Ge06A, Ge06B, Ge06C, Ge06D, Ge08, Ge09, Ge11, Ge12, Ge13 | Ge02, Ge04, Ge10, Ge14 | Ge01, Ge03
Both BEGe
Ge01
Ge02

## Slide 50: Effect of anti-coincidence window size – 305keV peak
Not because of bad timing at low E, since same behavior is also seen for higher E muonic Ag x rays
Ge02
Revisit my ELET params

## Slide 51: Effect of anti-coincidence window size – 305keV peak
Not enough statistics | tHigh increase gives strongest decrease | ¦tLow¦ increase gives strongest decrease
Ge05, Ge06A, Ge06B, Ge06C, Ge06D, Ge08, Ge09, Ge11, Ge12, Ge13 | Ge02, Ge04, Ge10, Ge14 | Ge01, Ge03
|tLow| increase is a bit stronger decrease
tHigh increase is a bit stronger decrease
Both BEGe

## Slide 53: Effect of anti-coincidence window size
434keV (Ag muonic capture)

## Slide 54: Effect of anti-coincidence window size
434keV (Ag muonic capture)
tLow (time after muon) has stronger effect (expected since delayed peak)

## Slide 55: Effect of anti-coincidence window size
434keV (Ag muonic capture)
tLow (time after muon) has stronger effect (expected since delayed peak)

## Slide 56: Effect of anti-coincidence window size
434keV (Ag muonic capture)
tLow (time after muon) has stronger effect (expected since delayed peak)

## Slide 57: Blocking the gammas from 108mAg with layer of lead??

## Slide 58: Blocking the gammas from 108mAg with layer of lead??
Gamma rays emitted from 108mAg
What if the rates become too large?  target with ~MBq of 108mAg
4p3/2  1s
4p1/2  1s
3p3/2  1s
3p1/2  1s
2p3/2  1s
2p1/2  1s
4s  2p1/2
4d3/2  2p1/2
4s  2p3/2
2p3/2  4d5/2
4d3/2  2p3/2
4p3/2  2s
4p1/2  2s
3s  2s
3s  2p3/2
3d3/2  2p1/2
3d5/2  2p3/2
3d3/2  2p3/2
3p3/2 2s
3p1/2  3p1/2
2s  2p1/2
2s  2p3/2

## Slide 59: Blocking the gammas from 108mAg with layer of lead??
depends on energy:

## Slide 60: Blocking the gammas from 108mAg with layer of lead??

## Slide 61: Blocking the gammas from 108mAg with layer of lead??

## Slide 62: Blocking the gammas from 108mAg with layer of lead??

## Slide 63: Blocking the gammas from 108mAg with layer of lead??
Effect of rho

## Slide 64: Blocking the gammas from 108mAg with layer of lead??
Effect of rho

## Slide 65: Recoil-sputtering for Ra implantation

## Slide 66: Recoil-sputtering: principle

## Slide 67: Recoil-sputtering: 1) implantation
TRIDYN simulation for 180kBq (1.31*1016 particles) of 226Ra at 30keV (1cmx1cm implantation spot)
NOTE: surface binding energy of Ra is by default taken to be 0 in TRIDYN

## Slide 68: Recoil-sputtering: 1) implantation
TRIDYN simulation for 180kBq (1.31*1016 particles) of 226Ra at 30keV (1cmx1cm implantation spot)
NOTE: surface binding energy of Ra is by default taken to be 0 in TRIDYN

## Slide 69: Recoil-sputtering: 2) Recoil-sputter simulation
Generated target from depth profile (discrete: 23 layers of 21A (Ra+C), backing of 1500A (C))
Generate recoiling 222Rn particles based on the Q-value by simulating ~90000 recoiling particles with position according to the depth profile

## Slide 70: Recoil-sputtering: 2) Recoil-sputter simulation
Sputtering yield per simulation layer
Ra

## Slide 71: Recoil-sputtering: 3) Activity lost after 1 year

## Slide 72: Recoil-sputtering: 3) Activity lost after 1 year
Note that this is only for the first alpha decay, there are 4 subsequent alpha decays  rough estimate: < 1Bq lost after one year
5.67*1012 particles lost due to decay
Ra
Ra

## Slide 73: Recoil-sputtering: 3) Activity lost after 1 year

## Slide 74: Ag collection analysis

## Slide 75: Plan for next collection
Contacted Maria and BR2
Contacted Lino and Andre to test the self-sputtering simulations for Ag