## Slide 1: Progress on the Ultrahigh Gradient, Short-pulse X-band Photogun at the Argonne Wakefield Accelerator
Bern switzerland
JOHN POWER
On behalf of
GONGXIAOHUI CHEN
and the AWA facility at Argonne National Laboratory
Sept 17, 2024

## Slide 2: outline
I am assuming (practically) no one here has heard of the AWA or SWFA.
Argonne Wakefield Accelerator (AWA) Facility
Structure Wakefield Acceleration at the AWA Facility
High Gradient X-band Photogun

## Slide 3
The awa facility

## Slide 4: What is the Advanced acceleration concepts (AAC) program
AAC ~ Wakefield Acceleration: Laser Wakefield Acceleration, Plasma Wakefield Acceleration, and Structure Wakefield Acceleration (SWFA).
Beam Test Facilities: Demonstrating the viability of emerging accelerator science ultimately relies on experimental validation.
U.S. advanced and novel accelerator beam test facilities
[C. Clarke et al 2022 JINST 17 T05009, https://iopscience.iop.org/article/10.1088/1748-0221/17/05/T05009 ]
National Laboratories
Universities
BELLA
ELL
UT3
Laser Beam
FAST/IOTA
AWA
FACET-II
Particle Beam
ATF
https://lasernetus.org/
https://www.beamnetus.org/

## Slide 5: Argonne wakefield accelerator (AWA)
Argonne Campus: 15 minutes west of Chicago
AWA: HEP test facility
APS: BES national user facility
ATLAS: NP national user facility
300 AREA
400 AREA
200 AREA
Notes: Accelerators at Argonne

## Slide 6: The Argonne Wakefield Accelerator (AWA) Facility
A Beam Test Facility to enable the development of novel acceleration technology
Drive RF Photoinjector (65 MeV)
  single bunch: 100nC
  bunch train: 600 nC
Argonne Cathode Test Stand (2-4 MeV)
Cathode research and diagnostics
Physics of high-gradient breakdown
Witness RF photoinjector (15 MeV)
Provides two-beam capability
Bright beams for low-energy experiments
Experimental Switchyard
Highly reconfigurable
6D phase space manipulation
Laser
100 mJ (IR), 10 mJ (UV),
300 fs – 6 ps (UV)
temporal shaping
https://www.anl.gov/awa

## Slide 7: The Argonne Wakefield accelerator
The AWA Facility
Witness
Drive
AWA Bunker
AWA Vacuum and Experimental Zones
ACT
EXPERIMENTAL AREA
Zones 2-5 are experimental areas
Zones 2, 4, and 5 have ~ 1 m experimental area
Zones 3A & 3B are fully re-configurable
5 Zones
7/36
https://www.anl.gov/awa

## Slide 8
The three awa research themes
To
support swfa

## Slide 9: AWA Research themes
Timeless research themes
9
Beam Production
Electron sources
  High-brightness
  High-intensity
e.g. RF Photoinjector
Beam Manipulation
Beam shaping & control.
Beam Diagnostics.
e.g. Double Emittance Exchange
Advanced Accelerator
SWFA & PWFA
  High-Gradient
  High-Efficiency
e.g. SWFA
Linear Collider
  Compact XFEL
UED
not exhaustive
Applications

## Slide 10
Research Theme:
Advanced Accelerator
Advanced Accelerator

## Slide 11: high-gradient normal conducting RF research
Rapid progress with short-pulse TBA since 2015 upgrade (started 2008)
AWA-II will enable demonstration of SWFA critical technologies in GeV range
AWA upgrade
AWA upgrade

## Slide 12: e-beam Driven Structure Wakefield Acceleration (SFWA)
Collinear Wakefield Acceleration
(CWA)
DB
MB
PWFA-like
A. Zholents, et al, NIMA 829, 190-193 (2016)​
A. Zholents, et al, Proceedings of IPAC2018​
main beam
drive beam
Klystron-like
CLIC CDR​: https://project-clic-cdr.web.cern.ch/CDR_Volume1.pdf​
W. Gai, C. Jing, J.G. Power, JPP 78, 339-345 (2012)​
drive beam
main beam
Power Extraction and Transfer Structure (PETS)
Accelerator
Two Beam Acceleration (TBA)
SWFA XFEL
IP
e-
e+
3TeV
1
10
1
10
SWFA 3 TeV linear collider
Advanced Accelerator

## Slide 13: short pulse rf generation
TBA drive beam PETS
…
ZONE1
ZONE3a
…
magnets & diagnostics
Drive bunch train
-5 GW beam power
-100A, 6 nsec
1.3 GHz Drive gun (Cs2Te photocathode)
  High charge bunch train (up to 600 nC)
  Final beam energy: ~65 MeV
……..
(Drive RF photoinjector)
(PETS)
Short RF pulse
(2 Hz)
  disk-loaded waveguide: 400 MW
  Metamaterial: 565 MW
Dielectric PETS: 80 MW
11.7 GHz
26 GHz
Advanced Accelerator
Notes: X-band test has become a general capability of AWA (work underway for 26 GHz to THz)

## Slide 14: PETS results at AWA
Dielectric X-band PETS (200 MW)
DOI: 10.1103/PhysRevAccelBeams.23.011301
2000 2005 2010 2015 2020 2025
1000 MW
900 MW
800 MW
700 MW
600 MW
500 MW
400 MW
300 MW
200 MW
100 MW
0 MW
C-band
dielectric
(2000)
C-band
dielectric
(2008)
X-band dielectric (2018)
X-band metallic (2018)
X-band metallic (2020)
X-band MTM (2019)
X-band MTM (2021)
AWA energy upgrade
15 MeV  65 MeV
K-band dielectric (2010)
J. Picard et al., PRAB 25, 051301 (2022)
MTM X-band PETS (565 MW)
  Highest peak power as 565 MW from a train of eight bunches with a total charge of 355 nC
Metallic X-band PETS (400 MW)
J. Shao et. al., https://accelconf.web.cern.ch/ipac2019/papers/MOPRB069.pdf
Advanced Accelerator

## Slide 15: High gradient structure test stand
Beam on YAG1
…
…
ZONE1
(Drive RF photoinjector)
ZONE3a
(PETS)
Example:
X-band gun beamline
high gradient test stand
Advanced Accelerator

## Slide 16: HIGH GRADIENT ACCELERATING STRUCTURES
Advanced Accelerator
Dielectric Loaded Accelerator (DLA)
2000 2005 2010 2015 2020 2025
400 MV/m
350 MV/m
300 MV/m
250 MV/m
200 MV/m
150 MV/m
100 MV/m
50 MV/m
0 MV/m
C-band TBA
DLA (2000)
K-band TBA DLA (2018)
X-band metallic (2018)
X-band metallic (2021)
AWA energy upgrade
15 MeV  65 MeV
X-band TBA DDA (2022)
X-band PC Gun (2021)
W-band CWA metallic (2015)
C-band TBA
DLA (2008)
C-band CWA
PBG (2009)
X-band MTM (2023)
Single-cell Dielectric
Disk Accelerator (DDA)
3-cell Disk Loaded Waveguide
1.5 cell X-band Photocathode Gun
Single-cell Disk Loaded Waveguide
Metamaterial Accelerator

## Slide 17
Research theme:
Beam Manipulation
Beam Manipulation

## Slide 18: Shaped electron bunches
  Deflecting cavity based long bunch shaping
longitudinal bunch shaping
Beam Manipulation
Experimental demonstration of enhanced transformer ratio (TR=4.9) Q. Gao et al., PRL 124, 114801 (2018)
Experimental demonstration planned for 2025. G. Ha, et al. PRAB (2020)
  Emittance EXchange (EEX) beamline to produce a longitudinally triangular beam profile
TDC
Mask
Quad
TDC
Notes: Either DEEX or
Multileaf collimator: https://journals.aps.org/prab/pdf/10.1103/PhysRevAccelBeams.26.022801
Bunch trains suitable for CWA (collinear wakefield accelerator) applications
->microbunch separation is ~10 ps

## Slide 19: NOVEL DIAGNOSTICS
Generative Phase Space Reconstruction (GPSR), 6-dimensional phase space reconstruction of a beam distribution from 20 measurements / ~15 minutes analysis time. Roussel, Ryan, et al. PRAB 27.9 (2024): 094601.
Beam Manipulation
Ha, Gwanghui, et al. "Single-shot measurement of transverse second moments using the projection method." PRAB 24.1 (2021): 012802.
ML diagnostics
Single-shot trans. phase space diagnostics

## Slide 20
Research theme:
beam Production
Beam Production

## Slide 21: Bright Beam generation
Main beam: needed for direct applications (linear colliders and light sources)
Beams for acceleration and diagnostics
Witness beam: As a probe to investigate phase-space degradation in CWA and TBA
Gao et al., PRL 124, 114801 (2018)
Beam Production

## Slide 22: Intense bunches and bunch train generation
Produce single drive bunch for CWA
Charge level:
  100-nC/Xband
  10-nC/sub THz
pre-shaped bunch for efficient acceleration
Drive beams are needed for TBA and CWA
laser
final drive bunch
[W. H. Tan, et al. PRAB (2021)]
Shaped laser w/ nonlinear e-beam manipulation
Beam Production
Produce drive bunch for TBA
bunch trains w/ ~600 nC (total)]

## Slide 23
High Gradient X-band Photogun

## Slide 24: two Paths to high brightness e- sources
short-pulse and TBA
Cathode
R&D
High Gradient
R&D
4D beam brightness
field experienced at emission (controlled by applied accelerating field)
1<a<2 depends on ab-initio long-transverse ratio of the beam
Mean-Transverse Energy [a property of the emitting surface (photocathode) and exciting laser]
I. V. Bazarov et. al., PRL. 102, 104801 (2009). https://doi.org/10.1103/PhysRevLett.102.104801
P. Musumeci, et al., NIMA 907 (2018) 209–220. https://doi.org/10.1016/j.nima.2018.03.019
Notes: motivation

## Slide 25: Xgun: 1.5 cell RF photocathode gun
RF Design
RF
beam
COAXIAL RF-INPUT COUPLER
1.5-CELL
XGUN
IRIS DISK
Overcoupled (b~20) -mode @11.7 GHz
RF
S. Kuzikov et al., (IPAC21)
An X-band Ultra-high Gradient Photoinjector
https://accelconf.web.cern.ch/ipac2021/papers/wepab163.pdf
S11 simulation (CST)
S11 measurement (N.A.)
Cathode is the Cu backwall
Parameter | Value
Frequency | 11.7 GHz
Mode | p
t_fill | 5.4 nsec
RF pulse length | 9ns (3 ns rise, 3 ns flat, 3 ns, fall)
Power | 250
Cathode Field | 470
25/36

## Slide 26: AWA drive and Xgun beamlines
Drive
beam
Beam on YAG1
…
…
Drive beam
Drive beam
PETS
ZONE 5
(diagnostics)
ZONE 3A + Xgun beamline
ZONE 1
L-band drive gun
Cs2Te cathode
High charge bunch train (up to 600 nC)
Final beam energy: ~65 MeV
High-power, short-pulse rf generation
      Metallic Power Extraction and Transfer Structure (PETS) installed
    PETS (our short pulse “Klystron”)

## Slide 27: Xgun beamline
drive bunch train
Power Extraction &
Transfer Structure (PETS)
power splitter
Xgun
Xgun beam
imaging
solenoid
ICT
spectrometer
dipole
YAG &
Pepper pot
Quad
BPM
laser injects from the 1st viewport
main solenoid
(w/ iron plate)
YAG
(energy meas.)
rf load
2023 config. (will upgrade this Fall)
Spectrometer
Quad
RF
ICT
trim
magnet

## Slide 28: Xgun test history
See “EXTRA” slides for details
Achieved 350 MV/m within 70k pulses.
A dark current loading region observed.
No observable dark current after conditioning.
Initial Xgun RF conditioning [1]
pre-2020
High gradient (388 MV/m) verified through beam energy measurement.
Beam energy characterized (~2.7 MeV)
Low breakdown rate confirmed (>500,000 shots, BDR<10−5).
1st beam test [1]
2021
X-band power splitter and phase shifter conditioned.
A LINAC added to the Xgun beamline. Beam energy characterized.
Performed another rf conditioning, very few BD noticed. Good robustness.
2nd beam test
& re-conditioning
2022
2023
Study the fundamentals of photoemission (Copper cathode):
Schottky studies at different gradients.
QE measurements at different gradients.
3rd beam test
(most recent)
RF conditioning test
stand
Xgun
Beam on YAG1
Next
section
[1] W.H.Tan et. al., Phys. Rev. Accel. Beams 25, 083402, August 2022 (2022)
LINAC

## Slide 29: Xgun progress
Fundamental photoemission studies
Schottky scans @ different gradients (60 MV/m to 320 MV/m)
  Simulation benchmarking
  Exploring the potential for other emission mechanisms
Exploring the potential for multipacting

## Slide 30: Schottky studies
Benchmarking Exp. Data to ASTRA simulations
Simulation setup
Possible field () contributions acting on the cathode:
Both included in ASTRA
Modeled separately using a sinusoidal surface [1-2]
where,
: applied rf field
: space charge shielding field
: modeled 3D EM field introduced by surface roughness.
In ASTRA, bunch charge is evaluated as follows,
where,
: Schottky strength coefficients
: field on the cathode
[1] D. J. Bradley, et al., J. Phys. D: Appl. Phys., Vol. 10, (1977).
[2] G. S. Gevorkyan, et al., Phys. Rev. Accel. Beams 21, 093401 (2018).
[3] G. Chen et al., https://accelconf.web.cern.ch/ipac2024/pdf/MOPR76.pdf

## Slide 31: Schottky studies
Simulation benchmarking of exp. data
@ 60, 100, 180, 250, 320 MV/m
Peak charge discrepancy only at high gradient.
Other emission mechanism involved (i.e. photo-assisted field emission)?
?
Modified Folwer-Nordheim:
Ref data for simulation param (, , ) optimization
At all gradients, simulations include the shows a better agreement with the measurements.
Revealed a beam clipping issue at the Xgun exit.
Photo-assisted field emission might happen at high gradient.
In ASTRA, bunch charge is evaluated as follows,

## Slide 32: Multipacting simulation
@ different gradients
Half cell
Full cell
Iris
Coupler
Simulation setup
In the simulation:
3D Xgun field map + solenoid field map included.
Tracking to the downstream ICT.
Primary particles for MP simulation assigned to an 8 deg slice.
Cu SEY applied.
Solenoid
ICT
Zoom-in
Total number of primary macro-particles: ~3000.
Total generated secondary electrons: ~200.
NONE of the secondary e- made to the downstream ICT.
An example of MP
simulation result

## Slide 33: Multipacting simulation
@ different gradients
①
③
②
④
Tracking the MP in different regions separately:
① Half cell
② Iris
③ Full cell
④ Coupler (no MP from simulation)
Half cell
Iris
Full cell
MP scanning param. | 
Xgun E | 10 to 350 MV/m
Phase | 0 to 360 deg
Sol. B* | 0.05 to 0.22 T
* Solenoid B for each scan was predicted based on the recorded experimental values | 
Get an insight on the MP issue which is sensitive to the gradient, rf phase and solenoid strength.
Nearly NO secondary electrons can reach to the downstream ICT.

## Slide 34: conclusion
AWA themes
Short-pulse TBA (NCRF): High-gradient demonstrated.
  ~300 MV/m X-band TW accelerating metallic accelerator
  ~400 MV/m X-band photocathode gun
Bunch manipulation
  6d phase space manipulation
  Longitudinal bunch shaping and associated diagnostics
X-band Photogun
Characterized parameters of Xgun, include:
  High gradient ~400 MV/m
  Beam energy 2.7 MeV
  Good robustness. No noticeable BDs after fully conditioning.
Fundamental cathode studies have been done:
  Schottky studies at different gradients have been performed.
  Benchmarking of experimental data to ASTRA simualtions.
  Studies on FE and MP issues through simulations underway.
Future work:
  New beam test in Fall 2024
  New designs of the Xgun have been proposed in parallel
E-field
Cathode
Half cell
Full cell
Iris
beam
WR90 port

## Slide 35
Big Thanks to our team!
Gongxiaohui Chen (AWA) Scott Doran (AWA) Alex Ody (AWA) Wanming Liu (AWA) John Power (AWA) Charles Whiteford (AWA) Eric Wisniewski (AWA) Gwanghui Ha (was at AWA, now at NIU) Jiahang Shao (was at AWA, now at IASF) Maomao Peng (was at AWA) | Chunguang Jing (Euclid Techlabs / AWA) Ernie Knight (Euclid Techlabs) Sergey Kuzikov (Euclid Techlabs) Ben Freemire (Euclid Techlabs) Sergey Antipov (Euclid Techlabs, now at PALM Scientific) Xueying Lu (NIU / AWA) Philippe Piot (NIU / AWA) Emily Frame (NIU) Wei Hou Tan (NIU, now at SLAC) Sarah Weatherly (IIT)
We also thank funding agencies: DoE HEP and SBIR programs and ANL LDRD.

## Slide 36
extras

## Slide 37: The AWA facility
65 MeV L-band photoinjector linac, 40 m long bunker, Support areas
https://www.anl.gov/awa

## Slide 38: Experiment #1: high-power rf conditioning
Experimental setup at AWA (Dec, 2020: 1 week run)
Xgun only
PETS [1]
Xgun [2]
drive beam
INSTALLED
DIAGNOSTICS
Bi-directional coupler
YAG screen + Faraday cup
[1] M. Peng, et al., (IPAC 19)
Generation of high power short rf pulses using an X-band metallic power extractor driven by high charge multi-bunch train
https://accelconf.web.cern.ch/ipac2019/papers/MOPRB069.pdf
[2] J. Shao, et al., (IPAC 21)
High-power test of a highly over-coupled X-band rf Gun driven by short rf pulses
https://accelconf.web.cern.ch/ipac2021/papers/thpab331.pdf
Short rf pulse
(9 ns)
38/36
Notes: Milestone: 350 MV/m achieved

## Slide 39: experiment #1: high-power rf conditioning
Experimental results (Dec, 2020: 1 week run)
J. Shao, et al., (IPAC 21)
High-power test of a highly over-coupled X-band rf Gun driven by short rf pulses
https://accelconf.web.cern.ch/ipac2021/papers/thpab331.pdf
RF conditioning history of the Xgun
Strong beam loading from dark current was observed during RF conditioning
Xgun only
I think we are onto something
Ecathode 350 MV/m (inferred from measured P=250MW)
Low Breakdown Rate
RF conditioned fast (~70k pulse)
No detectable dark current (<1pC)
39/36
Notes: Milestone: 350 MV/m achieved
No breakdowns after fully conditioned, BUT not too many pulses so no stats for BDR

## Slide 40: Experiment #2: first beam measurements
Experimental setup at AWA (Nov 2021: 3 week run)
W.H.Tan et. al., PRAB 2022
Demonstration of sub-GV=m accelerating field in a photoemission electron gun powered by nanosecond X-band radio-frequency pulses
Phys. Rev. Accel. Beams 25, 083402, August 2022 (2022)
RF
Xgun only
Additions to Exp’t #1
Installed a complete beamline w/ spectrometer installed for energy measurements
Added UV laser injection for e- beam generation
PETS
40/36
Notes: Milestone 1: 350 MV/m confirmed with beam measurement
Milestone 2: Stable beam was produced, Jitter correlated with drive-beam jitter

## Slide 41: experiment #2: first beam measurements
Xgun phase scan @340 MV/m
Evidence of strong Schottky effect
Results 1: first electron beam from Xgun (Nov 2021: 3 week run)
100 pC photoelectron beam on YAG1 screen
Xgun only
Phase Scan
41/36
No detectable dark current (<1pC)

## Slide 42: experiment #2: first beam measurements
Results 2: energy and gradient (Nov 2021: 3 week run)
Xgun only
Gradient confirmed
Gradient inferred from FR power was beam energy measurement
Max achieved gradient = 388 MV/m from the beam energy measurement
Stable beam produced
Jitter due to drive beam charge jitter due to laser energy jitter
Energy fluctuation ~3%, likely due to the drive charge instability due to laser instability
Low breakdown rate confirmed
∼500,000 shots gives a conservative upper limit for the BDR <10−5
Low dark current
No detectable dark current (<1pC)
42/36
Notes: GC: note there is a mystery. When drive Q was high, main beam was low energy. Weird!!!

## Slide 43: Experiment #3:Power splitter and phase shifter test
Setup & design (2-day run, April 2022)
Phase shifter
chokes
Power Splitter
PETS
High-power test of Broadband power splitter and phase shifter
(necessary for ultrashort pulse regime)
notch
trombones
S. Kuzikov et. al., IPAC22
Toward emittance measurements at 11.7 ghz short-pulse high-gradient rf gun
https://accelconf.web.cern.ch/ipac2022/papers/MOPOMS013.pdf
43/36
Notes: prep for experiment #4

## Slide 44: Experiment #3: Power splitter and phase shifter test
PETS = 400 MW
Both components conditioned to >200 MW
Power splitter (power level): 0-100% power variation
Phase shifter: >180 deg phase shift
Xgun
linac
between the linac and Xgun
Results (2-day run, April 2022)
Power splitter
Phase shifter
Phase Shifter
Power Splitter
44/36
Notes: We tested both compoents under high power. ->the power splitter can provide us a tunable from ..
Then, the phase difference between the linac and the xgun is plotted -> As we move the controller, the phase shift is pretty linear

## Slide 45: Experiment #4: second beam measurements
Setup: add a linac and extended the beamline (3-weeks, June 2022)
“LINAC” [1]
G. Chen et. al., NAPACC22
Emittance measurements and simulations from an x-band short-pulse ultra-high gradient photoinjector
https://epaper.kek.jp/napac2022/papers/moze3.pdf
Xgun, linac,
waveguide
45/36

## Slide 46: Experiment #4: second beam measurements
Results: Energy gain with linac demonstrated (i.e. staging!)
First attempted emittance measurement (beamline not optimized)
  (due to geometry asymmetry of the linac)
  Kinetic energy: 5.9 MeV
Breakdowns observed
~1.2 m
quad
spectrometer
~1.13 m
G. Chen et. al., NAPACC22
Emittance measurements and simulations from an x-band short-pulse ultra-high gradient photoinjector
https://epaper.kek.jp/napac2022/papers/moze3.pdf
Xgun, linac,
waveguide
46/36

## Slide 47: Experiment #4: second beam measurements
Results: Why is measured high? And what next?
Non-ideal LINAC geometry
  New LINAC design is proposed
Non-ideal solenoid
  New solenoid design is under review
Unknown BDs happened randomly and prevent us reaching to a higher optimized gradient
  Has Xgun has been damaged? (We suspect bad vacuum due to clamped linac.)
Issues in the 1st measurement:
Conclusion: pause program to understand breakdown
Vent the beamline and inspection Xgun
Reinstall Xgun without linac and with RF components
Add pumping
Xgun, linac,
waveguide
47/36

## Slide 48: experiment #5: Second high-power rf conditioning
Setup at AWA (Oct 2022: 2-day run)
PETS
RF
Xgun
bunch train
Xgun RF test-stand
YAG +
Faraday cup
Xgun alone
without linac
without phase shifter
without power splitter
48/36

## Slide 49: experiment #5: Second high-power rf conditioning
Result: Xgun has no damage, immediately back to ~350MV/m
Conditioning process is quick.
A dark current loading region observed (~40,000)
1st Xgun conditioning (Dec. 2020)
2nd Xgun conditioning (Oct. 2022)
The Xgun fully conditioned very smoothly. No damage
Did not observe dark-current
49/36
Notes: GC: Shao left gaps, but GC removed gaps from data

## Slide 50: New Xgun design
1.5 cell gun with removeable cathode
New Xgun is designed by Sergey Kuzikov and Ernie Knight at Euclid TechLabs.
E-field
H-field
Cathode
Half cell
Full cell
Iris
beam
beam
WR90 port
Ez
S11