## Slide 1: Reconstruction in a Segmented Calorimeter
Omar Beesley

## Slide 2: Current Calorimeter Reconstruction
t1
t2
|t1-t2| < 10 ns → Pileup
|t1-t2| > 10 ns → Not Pileup
P. Schwendimann (2022)
Move templates closer together until fitter can’t find two pulses
Pileup
Within 10 ns
LYSO measured to have <200 ps resolution
Segmented should do much better!

## Slide 3: Implementation of LYSO Detector Response
Truth energies/times
Waveforms
Fitted waveforms (reconstructed energies/times)
Calorimeter clusters

## Slide 4: A Waveform Generator from LYSO Waveforms
Templates built from testbeam waveforms across PIONEER energy scale
2. Waveforms are fit with templates and residuals are recorded as a function of voltage
3. Residual distributions at each voltage are fit to quantify voltage dependent fluctuations
4. Fluctuation size is fit as a function of voltage to obtain a two parameter waveform model
Pedestal noise

## Slide 5: Outline of LYSO Clustering Algorithm
Crystal hits within 2.5 RM that are within 3.5 standard deviations of time resolution – combined to form “bunches”
Bunches within 5 RM that are within 2 standard deviations of time – combined to form “proto clusters”

## Slide 6: Calorimeter and Beam Setup
Nominal LYSO inner radius is now 15 cm
Beam of pions with 3e5 rate – forced to decay to muons

## Slide 7: Event Displays
511 keV gamma from albedo
Look 5 RM to capture 511s
3 separate e+ events in the calo

## Slide 8: Proto cluster performance
High energy proto cluster angles are typically within 5 degrees of the true position angles
Highest energy proto cluster misses energy
Uncertainty in reconstructed energy from fitter
Additional energy from a 2nd hit is misidentified as being part of the cluster

## Slide 9: Reconstruction from proto clusters to clusters
Simulation outputs proto clusters – user able to do additional reconstruction/merging
To classify events using only calo information, energy dependent criterion for timing difference used to combine proto clusters into clusters
  Proto clusters above 5 MeV need to be almost exactly time coincident to be merged – rarely merged
bunches → proto clusters → clusters
Time Difference | Overall Efficiency | More clusters than e+ | More e+ than clusters | Reasons for inaccuracy
0-2 ns | 86% | 0.3% | 13.7% | 1. Timing limitations 2. Fitter bug 3. Delayed energy deposits
2-10 ns | 98% | 0.5% | 1.5% | 1. Delayed energy deposits 2. Fitter bug 3. Timing limitations
Overall <10 ns | 95.4% | 0.5% | 4.1% | 

## Slide 10: Effect of clustering on calorimeter energy resolution
Add uncertainty in cluster energies to intrinsic calorimeter resolution via quadrature
Reconstruction smears 1.8% resolution to 2%
Uncertainty of reconstructed energy from fit - especially at low energies
Inaccurate clustering of 511s

## Slide 11: Next Steps
Improve fitter stability and introduce correlated waveform fits
Implement LYSO intrinsic radioactivity at a Geant4 level
Optimize clustering for PiBeta
Train a neural network to classify and cluster events in the calorimeter