## Slide 1: Quench analysis: 0D estimate
Conductor layout:
Strand diameter | 0.7 mm
Copper-noncopper ratio | 1
RRR | 150
Number of strands | 24*7 = 168
Total width | 24.34 mm
Total height | 3.88 mm
Insulation thickness | 0.2 mm
Operating current | 18 kA
J eng | 182 A/mm2
J cu | 533 A/mm2
Inductance | 0.13 H
Stored energy | 21.1 MJ
Discharge voltage (max) | 1 kV
Time constant | 2.34 s
Delay time | 16 ms
Operating current | 18 kA
J eng | 182 A/mm2
J cu | 533 A/mm2
Inductance | 0.13 H
Stored energy | 21.1 MJ
Discharge voltage (max) | 1 kV
 | 2.34 s
 | 16 ms
Conductor cross-section | 94.4 mm2
Cable | 64.7 mm2 (68.5%)
Copper | 32.3 mm2 (34.2%)
Noncopper | 32.3 mm2 (34.2%)
Impregnation | 18.7 mm2 (11.8%)
Insulation | 11.1 mm2 (19.8%)
13 / 02 / 23

## Slide 2: Quench analysis: 0D estimate
Adiabatic analysis:
[W/m]
Conductor cross-section isothermal
Current flow in copper
Size of normal zone to reach 100 mV at 18 kA: 1.7 m (0 T), 0.2 m (15 T)
8 K: 397 K at B = 0 T constant 1090 K at B = 15 T constant 1060 K for B = k x I
I = 17 kA, V = 1.5 kV, tau = 1.47 s: 100 K at B = 0 T constant 262 K at B = 15 T constant 243 K for B = k x I
B = 15 T
B = 0 T
Cable + insulation + impregnation

## Slide 3: Quench analysis: 0D estimate
Constant B:
Quench integral: = 384 kA2.s at 18 kA, 1.0 kV = 218 kA2.s at 17 kA, 1.5 kV
B = 0 T
B = 15 T
Cross-check the actual effect of magnetoresistance?
3-D model to be prepared to quantify impact of thermal conductivity in transverse and longitudinal directions, though strong impact on Tmax is not expected
RRR ~ 20

## Slide 4: Quench analysis: 0D estimate
Rd, mΩ | 100 | 94
, s | 1.3 | 1.4
I, kA | 18.0 | 17.0
E, MJ | 21.1 | 18.8
V, kV | 1.8 | 1.7
Tmax*, K | 258 | 212
Rd, mΩ | 100 | 94
 | 1.3 | 1.4
I, kA | 18.0 | 17.0
E, MJ | 21.1 | 18.8
V, kV | 1.8 | 1.7
Tmax*, K | 258 | 212
* @ B = 15 T constant
15 / 04 / 23

## Slide 5: Quench analysis: 0D estimate
10 m/s
B=15 T: solid lines
B=k x I: dashed lines
Q ~ 330 kJ
(~1.6% stored energy)

## Slide 6: Quench analysis: 0D estimate
Neglected terms so far:
Thermal conductivity in longitudinal and transverse direction  lower Tmax
AC loss heating due to Bdot, thus faster current decay  lower Tmax
Higher resistance due to Rcoil, thus faster current decay  lower Tmax
Impact of iron on coil inductance during quench? ~20% higher L at low B?

## Slide 7: Quench analysis: Copper RRR
OD 0.7 mm, cnc ~1.2, Scu 0.21 mm2, RRR
Resistance estimate for RRR = 50: ~80 mΩ/m at 293 K  ~1.5 mΩ/m at 4 – 20 K  ~4.3 mΩ/m at 4 K, 15 T
Measurements on non-reacted 0.5 m-long sample
Impact of heat-treatment…
https://iopscience.iop.org/article/10.1088/1361-6668/aa67ab

## Slide 8: Quench analysis: towards 3D model
Coil splicing layout?
Cooling interface?

## Slide 9: EDIPO1 QD parameters
+ few ms to open circuit breakers
25 / 06 /24

## Slide 10
Setting up 3-D quench model:
Geometry import
Matrix of mutual inductances
Magnetic field incl. iron (by Xabier)
Current sharing, Tcs distribution
Heat equation

## Slide 11
Geometry:
20 pancakes (4 per vertical, 6 per side coils)
560 turns (46 per vert. pancake, 16 per side pancake)
100 nodes per turn
 56’000 nodes to evaluate heat equation

## Slide 12
Inductance:
Magnet: 137 mH
Coil: 4 x 4 matrix
Pancake: 20 x 20 matrix
Turn: 560 x 560 matrix (Average value = 0.44 µH, max value = 9.93 µH, min value = -0.21 µH)

## Slide 13
Magnetic field within the coil winding (over 56’000 nodes)

## Slide 14
Current sharing at 18 kA operation
Tcs distribution along conductor length
Intra-strand resistance neglected
Tcs<11 K
Tcs<9 K
Tcs<7 K
min Tcs = 6.97 K

## Slide 15
Heat equation:
[W/m3]
Conductor face and conductor side cooled by helium
(through 0.2 mm G10)
Current discharge once ‘quench is detected’ (td = 0.1 s):
(mutual inductance used to calculate distribution of voltage to ground)
Connectivity matrices for nodes in the same cross-section

## Slide 16
External energy of 1.7 J deposited over 12 cm (3 nodes) within 0.1 s (power ~140 W/m)

## Slide 17
~98% stored energy released in Rdump, ~660 kJ in the coil winding, i.e. losing ~250 liters of helium (latent heat 2.6 kJ/liter)
Heat removal rate by helium up to ~30 kW
NZPV strongly depends on temperature threshold, up to ~100 m/s for the 10 K front
tdetect
tdetect+td