## Slide 1: Superconducting magnet String test for the SIS100 accelerator of FAIR
Patricia Aguar Bartolome et al.
GSI Helmholtzzentrum für Schwerionenforschung GmbH
5th SMTF Workshop, 31 March 2025
Bad Zurzach, Switzerland

## Slide 2
FAIR / SIS100
Introduction
Installation
Documentation
Performance
Setup
Measurements
Summary
Outline

## Slide 3
SIS100
SIS18
UNILAC
p-LINAC
Existing GSI facility
FAIR facility
FAIR / SIS100
The SIS100 heavy ion synchrotron is the main accelerator of the FAIR complex
SIS100
beam rigidity 100 [Tm]
circumference 1083.6 m
fast ramped machine 4 Ts-1 → 27.5 kAs-1 (1Hz)
417 sc-magnets assembled in
over 190 cryo-magnetic modules
over 60 local cryo components

## Slide 4
DM with CAP
DM
QDM type 2.5
End Box (EBx)
End Cap (EC)
with CWT
RT
pumping
chamber
Bypass line (BPL)
Feed box
LHe supply
establishing installation sequence and procedures
verification of design and interfaces
preparation of work procedures and quality assurance
validation of the cryogenic system
quench and protection study
powering behavior of the system
functionality of the beam and insulation vacuum system
accelerator relevant operation
Introduction
SIS100 String test serves as a crucial preparatory phase for the installation, commissioning and operation of the SIS100 accelerator
Scope
Objectives
SIS100 arc segment

## Slide 5
Assembly of the String test components mainly carried out by IFJ PAN Cracow team except the welding of the hydraulic interconnections (KRIOSYSTEM Wrocław)
Installation
Installation of telescopic bellows
UHV interconnections
Hydraulic connections
Electrical connections
Closing of telescopic bellows
Dipole-Dipole connection
End cap connection
Quadrupole-Dipole connection
Stabilizer supports
  Challenges during installation:
    restricted space between components
    large number of interconnections within a limited volume, especially in the end cap
    proximity between critical components (sc-bus bars to welded connections)
    design and production of special tooling
Quality control processes:
  leak test of all the UHV interconnections
  visual inspection of all the hydraulic interconnections
  radiographic test of all the hydraulic interconnections
  leak test of all the hydraulic interconnections
  pressure test up to 16 bar of the He-process line system
  Integral leak test of the entire system

## Slide 6
Documentation
Work preparation & test planning
Work plan → contains the relevant assembly and test steps
Work instructions → procedures for the installation and assembly
  13 documents created
Test instructions → procedures for quality control
  5 documents created
Acceptance protocols
  7 documents created
Non conformity reports
Risk assessment for work to be carried out
Lessons learned → compilation of findings and recommendations
String test documentation uploaded to EDMS and currently used in the SIS100 tunnel installation

## Slide 7
Cool down
Assembly work completed in October 2023
  The cool down process is divided into two phases with different pressure:
  Phase 1: Since the cold masses are smaller in the 2 parallel lines of the quadrupole module, the doublet cools down faster than the dipoles.
  Phase 2: The QDM cools down faster than the dipoles → the mass flow rates start to unbalanced due to the different flow impedance caused by the difference in the temperature.
Phase 1 | Phase 2
300 K to ~80 K | ~80 K to 4.5 K
Balancing of the mass flows of the modules by a combination of capillaries and heaters
EBx
EC
BPL
QDM
DM1
DM2
QDM
DM1
DM2
pInsVac ~ 6E-6 mbar
No problems observed during the cold phase
in the insulation vacuum of the String cryostat
Performance – Cool down

## Slide 8
Performance – Beam vacuum / Temperatures
CWT
dipole
chamber
dipole
chamber
Cryogenic beam
vacuum system (~14m)
quadrupole
chamber
quadrupole
chamber
cryo-
collimator
cryosorption
pump
Warm beam vacuum system
BPM
R-CWT
+PSC
Temperature
sensor
(T = 293K)
Magnet chambers reached ultimate temperatures of around 5K
Cryo-collimator temperature around 6K
Temperatures in the interconnection areas significantly higher → not actively cooled
  The filaments of the extractor gauges directly flanged into the cold beam pipe caused a high heat load

## Slide 9
Performance – Beam vacuum / Pressures
CWT
dipole
chamber
dipole
chamber
Cryogenic beam
vacuum system (~14m)
quadrupole
chamber
quadrupole
chamber
cryo-
collimator
cryosorption
pump
Warm beam vacuum system
BPM
R-CWT
+PSC
T = 293K)
pwarm_1
pwarm_2
low UHV pressures in warm beam vacuum system
XHV pressures in cryogenic beam vacuum system
pcryo_3
pcryo_1
gas type and temperature-corrected real pressure
pcryo≈ 5E-13 mbar or lower
pcryo_2
Pressure measurement along the cryogenic beam line with 3 extractor gauges flanged directly to the cold beam pipe at the interconnection areas
T ≈ 5K

## Slide 10
Performance – Beam vacuum
 | Required | Verified @ String | 
H2 pressure in cryogenic beam vacuum (< 10K) | < 1E-12 mbar | 5E-13 mbar | 
H2 pressure in RT vacuum system | < 3E-11 mbar | < 1E-11 mbar | 
ultimate temperature of cryogenic beam vacuum system (steady state) | < 5 K | ~ 5 K | 
Dominant residual gas component | H2 | H2 | 
sc magnets and the beam vacuum system reached their planned ultimate temperatures within the expected time period
ultimate pressures and residual gas composition in the two short RT sections were achieved
generated residual gas densities in the cold beam vacuum system corresponded to H2 vacuum pressures of ~ 5E-13 mbar or even less
density and temperature conditions along the string were constant over the entire duration of the cold phase
no leak-induced density increases were observed
Beam vacuum quality requirements for future beam operation are fulfilled
The String test has demonstrated that He mass flows and the magnetic and vacuum cryogenic systems operate as expected

## Slide 11
FAIR-QDS
Series quench detection electronics installed in the String
Dipole circuit monitored by 2 MCL detectors and 4 bridge detectors
Quadrupole circuit monitored by 2 MCL detectors and 3 bridge detectors
Both main circuits in an overlapping structure similar to SIS100 with quench conditioning boxes
Bridge cabling asymmetry was introduced on purpose Corrector circuits (2 x ST + 1 x CS) monitored by MID detectors
Setup – FAIR quench detection system
FAIR quench dection system is reliable and safe to operate
Open topics
Scaling and synchronization of the Dipole and Quadrupole circuits DCCTs (actually not a part of the F-QDS)
Synchronisation of signals acquired by different electronic boards:
  initially ±70 ms, currently ± 6 ms - still not enough
  search for optimal parameters for data frames (work in progress)
  consequence: difficulties with quench data interpretation for Dipole
  and Quadrupole circuits

## Slide 12
Construction (front) of PC and SCADA
Construction (back) of PLC and cabling
  Objectives:
    Test IOs
    find configuration to heat SIS100 magnets
  Sensors and actors tested:
    CERNOX
    TVO
    PT100
    Thermocouple
    Current measurement
    PWM heater
Accelerator Control System developed
for FAIR/GSI
Successful completion of the commissioning of the SIS100 cryo-controls at the String test
Key control functions tested to provide information on the control of the SIS100 cryogenics system
Setup – SIS100 cryo-control system

## Slide 13
Applications provided by APP cover all standard operation software used in the central and local control rooms of FAIR
Physics parameters are typically modifyable by the user
the String circuits perform correctly
    no quenches
    no major issues
    powering tests continue...
Setup – SIS100 accelerator control system
SIS100 String test serves as a platform for the ACC control system
Four SIS100 Patterns have been created for the String

## Slide 14
Measurements – Alignment
1
Laser tracker
2
Photogrammetry
3
Absolute Multiline System
Change of outer geometry
  relative to each other (cryostat vs. cryostat)
  absolute to external references (cryostats vs. sorrounding area)
Change of outer geometry
  relative to each other (e.g. cryostat vs. support frame vs. adjustment feet)
Change of inner geometry (cold mass vs. cryostat)

## Slide 15
Measurements – Alignment
1
Laser tracker
Measurements @ room temperature - vacuum - 4K
The results refer exclusively to the String cryostats, NOT to the behaviour of the cold mass
String @vacuum – comparison between measurement at room temperature and at 4.5K

## Slide 16
Measurements – Alignment
2
Photogrammetry
Verification of laser tracker results
Visualization of more details
Measurements @ RT – vacuum – 4K → measurement after cold cycle pending
Deformation after evacuation:
  dipole adjustment feet vs. cryostat ~ 1.2 mm
  cryostat vs. surrounding area ~ 1.5 mm
Deformation after evacuation:
  dipole adjustment feet vs. cryostat → negligible
  cryostat vs. surrounding area ~ 0.15 mm
QDM
DM
DM

## Slide 17
X
Y
DM 26
X
Y
DM16
X
Y
QDM
Measurements – Alignment
3
Absolute Multiline System
Monitoring lateral movement of the cold masses vs. cryostats @ RT and 4.5 K
AMS is a 1D interferometric system with 0.5 µm/m accuracy
Line of sight (LOS) created to detect translation and rotation around the beam axis
magnets cross sections

## Slide 18
Measurements – Cross talk
MDP-Q = LDP • VQ / VDP
Measured inductance matrix for the String:
Mutual inductance values:
  MDP-Q ≈ 10 nH between DP and Q
  MQ-DP ≈ 3 nH between Q and DP
Method: powering one of the main circuits and check if there is any induced signal in the other circuit
 | L_ DP (mH) | L_ Q (mH)
L_ DP (mH) | 1.6E+03 | 9.00E-03
L_ Q (mH) | 3.00E-03 | 8.11E+02
No significant cross talk between the dipole and quadrupole circuits
Scaling to the SIS100 (x100) → M ≈ 1.0 μH
Cross-talk between main circuits
LBB = 0.25 μH/m
M
LDP
LQ
{
}

## Slide 19
Procedure
Principle of a cryogenic bake-out
Tests – Beam vacuum / “Cryogenic bake-out”
pumping capacity of cold beam line surfaces limited for H2 and He → pressure in the cold beam vacuum sections increases with operating time
residual gases (mainly H2) from the room temperature areas enter the cryogenic areas and increase surface coverage (adsorption isotherm)
cryogenic beam vacuum system of SIS100 designed to warm up independently on the sc magnets to allow for “regeneration” of the cold surfaces
cryogenic beam tubes warmed up to approximately thermal shield temperatures → desorption of previously cryo-pumped gases (mainly H2) from the cold surfaces
desorbing gases are pumped by the NEG-IGP pumps installed at the room temperature side
when the pressures in the cold system are ~1E-10 mbar, re-cooling is initiated to LHe temperatures
low XHV initial conditions in the cryogenic beam vacuum system are restored
Concept
Successful experimental test of the functionality of a “cryogenic bake-out” in the SIS100 String

## Slide 20
Summary
Objectives | 
establishing installation sequence and procedures | 
verification of design and interfaces | 
preparation of work procedures and quality assurance | 
validation of the cryogenic system | 
quench and protection study | 
powering behavior of the system | 
functionality of the beam and insulation vacuum system | 
accelerator relevant operation | 
SIS100 String test serves as a test site for the installation processes, commissioning and operation of the SIS100 accelerator
String INSTALLATION succesfully completed in October 2023 important MILESTONE for the SIS100 achieved!!
Constant pressure and temperature conditions along the String over the entire duration of the cold phase
No thermomechanical damage to the cold mass even after repeated cold cycles
First energization of the String test electrical circuits with real current ramps of the SIS100 successfully carried out
No significant cross talk between the dipole and quadrupole circuits have been observed
Numerous precision measurements on the movement of cold masses and cryostats with different methods @ vacuum and 4.5K carried out
Experimental proof of the functionality of a „cryogenic bake-out“ at String was successful
Successful transfer of work instructions and QA documents from String test to the SIS100 installation
The team responsible for the installation of the String test is currently carrying out the installation in the SIS100
Sector 3