## Slide 1: MEG 2011 Run

## Slide 2: MEG 2011 Overview
VERY Successful Physics Run : Doubled 2009+2010 Statistics!!!
BTS major repair &
safety modifications
(end 2010 + Spring 2011)
– proved to be successful
Ran contiuously for 212 D
Beam-rate Optimization
low, Normal, High &
Intermediate intensities
for 2011 detector intensity
tests
New DC HV-system successfully
introduced to reduce noise –
though effect on resolutions was
counter-balanced by gain-
degradation suspected to be due
to aging effects  talk Malte
New DC alignment system laser-
tracker + prismatic corner-cube
reflectors  talk Malte
Gas + beam intensity studies undertaken
Shows may be also possible to
work at ‘’Intermediate intensity’’
 talk Malte
BGO array replaces NaI array
in CEX
- finer granularity,
- 30% improved E/E at 55 MeV,
- improved position resolution,
- 30% increase in LT to 97%
- factor 2.1 > in efficiency
REDUCES 0 calibration time by 2
 talk Toshiyuki
Beam
DCs
BGO

## Slide 3: MEG 2011 Overview Cont.
Stable operation of calorimeter
- slow 4% LY-loss (well
monitored & compensated)
- PMT gain-loss at 2010 level
0.1%/D
- improved energy resolution
- beam intensity studies show
pile-up rejection works well
even at Rμ ~ 1108 Hz
Shows could work at
increased beam rate 2012!
Mott scattering e+ Beam
- study of cloud muon
contamination 50 & 53 MeV/c
- RF introduced 1st time
- Mott & MEG target data taken
RF-selection gives good
monochromatic line
σE ~ 450 keV (8‰ σE /E)
Neutron generator with
9 MeV Ni gamma-line used as
standard calibration tool
Dedicated Cosmic Alignment
data runs taken throughout run
period
Calorimeter
Calibrations
TCs
TC bar performance
- stable operation
- performance comparable 2010
 talk Matteo
TC Fibre performance
- US-side 10% noisy channels
excluded (influence on DC)
- performance not sufficient for
online trigger inclusion
- used for ‘’offline’’ analysis
 talk Matteo

## Slide 4: MEG 2011 Overview Cont.
Trigger+DAQ
Trigger/DAQ Performance
- Multi-buffering used as standard
- LT increases to > 99%
- MEG trigger rate 511 Hz
- direction-match LUT relaxed
without loss of efficiency
- UCN spill compensation for
LXe PMT-gain change
(<1% effect)
in trigger BUT! available
UCN-signal needs optimizing
Organization
Remote Shift Scheme introduced
- during Physics Run Part-II
- full set of ‘’remote tools’’ to run
experiment over Internet
- added monitoring & surveillance tools
- added electronic control room aids
Power
Outage
Power Outage
- kills Cryo-plant 4 down
till next year
- setup for BTS dewar operation
once another source LHe ready
- 10D beam loss to MEG
- successful dewar operations
all tests could be finished
Cryostat filling

## Slide 5: 2011- the Start
January
BTS Re-mounting
outside 𝛑E5 after
Repair/modifications
Beg. February
Cool-down Test
In 𝛑E5
March:
DCs de-cabled
EC + IS removed
US/DS TC out
End May:
DC-installation (5W delay
replacement DC construction
proved technically more difficult)
+ 1W minor delays
Back to “Square One”
TOTAL Spectrometer
DISMANTLED + part of
Beam Line
Before Run 2011

## Slide 6: Schedule 2011
Split beam optimization & calibration time + positron beam test to minimize
influence from DC construction & installation as well as survey preparations

## Slide 7: Physics Run
shifts started on schedule 24th June
due to the extensive detector testing + trigger setup “week” (24th-28th June)
MEG data-taking was also started on schedule & very efficiently
CEX calibration run flexible, in September
power-outage mid. Nov. Kills cryo-plant 4 (loss 10 D) MEG recovery using BTS Dewar-operation

## Slide 8: 2011 in Numbers
Statistical – MEG’s most
Significant Physics Run
  2011 Double the Statistics of 2009 + 2010
  (based on Normalization)
  2011 1.91014 µ-stops compared with
  2009+2010 1.751014 µ-stops
  113 Physics Days/81.3 DAQ Days
  62.4 M Triggers (MEG) – 30998 Runs @ 2k events
  Total of 1213 shifts & remote shifts
2011
µ-stops on Target
CEX
Acc
SD
Cryo-
Plant
Down
Dewar
10 Day Beam-loss
due to unexpected
power-outage & loss
of cryo-plant 4

## Slide 9: 2011 Run Conditions
- target
inclination
angle
Muon Target Parameters:
Inclination Angle  =(20.00.3)º
Thickness 205 µm CH2/Polyester Sandwich
Density 0.895 g/cm3
Beam Intensity: -
Mode | Beam Rate measured COBRA Centre at 2.2 mA 300m Degrader, He/Air 95%/5%
‘’Low’’ (slits 75) | 1.2107 +s-1
“Normal” (slits 105) | 3.6107 +s-1
“Intermediate” (slits 115) | 4.2107 +s-1
‘’High’’ (slits 250/280) | 9.2107 +s-1
Degrader:
Stopping Rate for physics Run (300m degrader) at 2.2 mA ~ 3·107+s-1

Degrader
Thickness 300 µm Mylar
Density 1.395 g/cm3
He/Air 95%/5%
Notes: 9

## Slide 10: 2011 Preliminary Data Quality c.f. 2010
DCs
Calorimeter
TCs
E/E (w> 2cm) ~ 11% better
better uniformity than 2010
energy-scale linear at 0.2‰
level (50% statistics)
- 9% high ‘’core’’ contribution
10% better -resolution
slightly improved -resolution
5% improved z-vertex res.
9% improved y-vertex resolution
5% improved te-resolution
noise suppression FFT-technique
gives resolution improvement
BUT
lower chamber gain – (aging?)
counteracts improvement
- Michel-edge asymmetry under study
- most resolutions consistent
with 2010 level
some problems with NIM
timing signals – solved
with ‘’offline’’ template fit

## Slide 11: New Spectrometer Alignment System
REASON: Improve previous theodolite-based DC-survey measurements - Why?
Previously theodolite method dependent on TC N2-Bag being extracted  survey NOT
performed under final detector conditions
Large uncertainty on z-measurements due to theodolite "forward intersection method"
Can One Improve...YES using Laser-tracker which combines
 laser interferometry distance measurement
+ absolute distance meter
Need implementation solution for light reflector on DCs
 "Corner-cube" Reflectors

## Slide 12: Alignment Cont.
Ideal: mirror corner-cube retro-reflectors
– PROBLEM dimension too large for mounting on system
Studied several possibilities – corner-cube ‘tapes’, ‘foils’, ‘plastic arrays’, prismatic retro-reflectors
only ‘prismatic’ type proved useable
at 630 nm
Principle of corner-cubes:
- reflected beam parallel to incident beam
irrespective of prism orientation
- optical path-length OPL=  n(l) dl is constant
inside the corner-cube if n=constant
- OPL  apex length
- high qulity BK7 borosilicate crown glass n=1.51519 (630 nm)
Corner-cubes individually catalogued:
- 70 corner-cubes (need 66 for DC-system) individually assessed

## Slide 13: Alignment Cont.
However prismatic corner-cubes need extra calibration
due to ‘refraction effects’ which vary with incident angle at the surface of the prism
Angular calibration Measurements
Area Implementation
Solution found so that both theodolite &
laser-tracker measurements could be done
X-check
X & Y both methods consistent
Z laser tracker estimated ~10 x more precise
Implementation on DC-system  talk Malte

## Slide 14: e+ Mott Scattered Beam
Coherent Mott-scattered
monochromatic Positron Beam
as a calibration-tool for our
spectrometer
After an initial feasibility test in 2010
2011 – first "full test" with introduction of accelerator RF for
Cloud Muon background suppression
Data at 50 MeV/c & "Signal momentum" 53 MeV/c
Mott target (1mm thick) & MEG target (0.205mm thick) used
RF-signal from accelerator used + slits 65 & 70
Michel Trigger #16 + prescaled #18, 22 (DC+ TC alone)
TOF separation COBRA Centre
vs beam Momentum
at our momenta ~53 MeV/c have
beam e+, cloud µ+, beam +, Michel e+
Separator doesn’t really help much at these momenta
TOF separation wrt RF COBRA Centre only possible at 53 MeV/c
No separation at 50 MeV/c
P(MeV/c)
t()
t(µ)
t(e)

## Slide 15: Monochromatic e+-Beam Cont.
53 MeV/c Mott Target 1mm
TOF-Spectrum
53 MeV/c MEG Target 205 µm
Prob. Energy-loss tail - investigating
Preliminary
Monochromatic

## Slide 16: e+- Beam Possibilities
Polarization Study of Michel e+ compared to Mott e+ X-section-form known
Preliminary
-Distribution of Mott-events compared to
MC theoretical X-section
& detector "accepted" X-section
Detector Alignment Study
For
Polarization=0
MC Data
Scattered e+ well known F()
from binned -Distribution of Mott-events vs. P
can see misalignment effects – most sensitive for z!
Vertex resolution Possibility
Shows sensitive to plastic screws on MEG-target
Could add small mettalic pins to dedicated MOTT Tg
With varying distances apart in x & y so measuring the
vertex resolution at the target for "signal" momentum

## Slide 17: Remote Shifts
Electronic Control Room
‘’White Board’’ on Web
moveable
moveable
Webcam
Area Surveillance
Shift-crew communications via video SKYPE link
Web-based tools for remote full control of Expt.
Remote web-based ‘’analysis tools’’ available
Full accounting + Rules integrated into MEG
shift Scheme

## Slide 18: Spin-off Physics
1.)
LFV-transition mediated by a very-light,
long-lived pseudo-scalar boson 
 talk Physics Results Wataru
2.)
2-body muon-decay decay into massless Majoran
 talk Physics Results Wataru
M. Hirsch and A. Vicente, PRD 79,(2009) 055023
Phys. Rev. D 72, 117701 (2005)
Radiative Muon Decay
3.)
RMD measurement using polarized muons
normalization for MEG + internal check
non-SM Michel parameter measurement possible
 talk Yusuke

## Slide 19: Next
This gave a brief overview of the relevant
aspects of our 2011 Run
Detailed information will follow
in the remaining talks....