## Slide 1: 70 years of muon radiography: a biased historical overview
Chris Morris
Los Alamos National Laboratory, Los Alamos, NM 87545
4 November 2024
Abstract The history and status of muon tomography and radiography will be presented.
Managed by Triad National Security, LLC, for the U.S. Department of Energy’s NNSA.
Physics of fundamental Symmetries and Interactions - PSI2025

## Slide 2: Cosmic-ray muons
• As cosmic rays (mostly protons) strike the upper atmosphere, they interact with atomic nuclei and produce particle cascades. Muons (leptons) can survive and make it to the surface.
• Muons have a large penetrating ability, being able to go through tens of meters of rock with low absorption.
• Muons arrive at a rate of 10,000 per square meter per minute (at sea level).
15-20 km
1936 Carl D. Anderson and Seth Neddermeyer identified but mislabeled muons as mesons

## Slide 3: Muon Interaction with Matter
Kinematics
Coulomb Interaction
Ernest Rutherford

## Slide 4
,
 | dx/dE | x
 | cm/GeV | cm
Reactor Core | 731.9 | 8.7
Concrete | 254.1 | 15.8
Fe | 88.4 | 9.5
water | 502.5 | 36.0
Energy Loss (Bethe)
Multiple Scattering (Moleère, Bethe, Fermi)
Chart: Momentum [GeV/c]
| 1.1200000000000001 | 1.41 | 1.7600000000000049 | 2.29 | 2.8499999999999988 | 3.57 | 4.49 | 5.6599999999999975 | 7.1199999999999966 | 8.9500000000000028 | 11.26 | 14.17 | 17.829999999999988 | 22.439999999999987 | 28.23 | 35.520000000000003 | 44.7 | 56.25 | 70.790000000000006 | 89.09 | 112.13 | 141.12 | 177.62 | 223.56 | 281.39 | 354.18 | 445.81 | 625.45999999999947 | 990.22
0 m | 3.2668e-05 | 3.3529e-05 | 3.4648e-05 | 3.3176e-05 | 3.1839e-05 | 2.9336e-05 | 2.6681e-05 | 2.376e-05 | 2.0512e-05 | 1.7253e-05 | 1.3859e-05 | 1.078e-05 | 8.0767e-06 | 5.7349e-06 | 3.9789e-06 | 2.6449e-06 | 1.7161e-06 | 1.066e-06 | 6.4887e-07 | 3.7555e-07 | 2.2101e-07 | 1.2349e-07 | 6.6359e-08 | 3.7368e-08 | 1.8697e-08 | 9.6919e-09 | 5.4373e-09 | 1.7703e-09 | 3.9824e-10
 | 4.59e-05 | 4.16e-05 | 3.67e-05 | 3.33e-05 | 2.97e-05 | 2.76e-05 | 2.43e-05 | 1.98e-05 | 1.09e-05 | 7.14e-06 | 4.82e-06 | 2.51e-06 | 1.5e-06 | 7.19e-07 | 4.77e-07 | 2.79e-07 | 2.43e-07 | 2.26e-07 | 8.89e-08 | 1.27e-08 | 4.43e-08

## Slide 5: The first use of Muography (1955)
E. George, Commonwealth Engineer 455 (1955).
School of Physics, (1952 to 1966), [REF-00003167]. University of Sydney Archives

## Slide 6: Muon mapping of Chephren’s Pyramid Science, 167, 832 (1970)
left: actual image
right: simulated image,
with hidden chamber
as in Cheops
There are no hidden chambers of the size of the Kings chamber

## Slide 7: Muon mapping of Chephren’s Pyramid Science, 167, 832 (1970)
left: actual image
right: simulated image,
with hidden chamber
as in Cheops
There are no hidden chambers of the size of the Kings chamber
Provided by: Roy Schwitters (Our new age 1957-1973)
through John McGill)

## Slide 8: Cosmic radiography of a volcano (Nagamini 1994)
Method of probing inner-structure of geophysical substance
with the horizontal cosmic-ray muons and possible application
to volcanic eruption prediction
K. Nagamine a,bj * , M. Iwasaki a, K. Shimomura a, K. Ishida b
a Meson Science Laboratory, Faculty of Science, Uniniuersiloyf Tokyo (UT-ML), Hongo, Bunkyo-ku, Tokyo, Japan
b Muon Science Laboratory, The Institute of Physical and Chemical Research (RIKEN), Wake, Saitama, Japan
Received 4 July 1994; revised form received 12 September 1994

## Slide 9: Cosmic radiography of a volcano (Nagamini 1994)
Method of probing inner-structure of geophysical substance
with the horizontal cosmic-ray muons and possible application
to volcanic eruption prediction
K. Nagamine a,bj * , M. Iwasaki a, K. Shimomura a, K. Ishida b
a Meson Science Laboratory, Faculty of Science, Uniniuersiloyf Tokyo (UT-ML), Hongo, Bunkyo-ku, Tokyo, Japan
b Muon Science Laboratory, The Institute of Physical and Chemical Research (RIKEN), Wake, Saitama, Japan
Received 4 July 1994; revised form received 12 September 1994

## Slide 10: Cosmic ray muon tomography
Cosmic ray muon generator / multiple scattering simulation.
Good agreement with experiment.
Allows for extrapolation to larger, more complex scenes.
Experiment
Simulation
X
D1
Y
C2
X
D2
Y
C3
X
D3
Y
C4
X
D4
Y
B
W
B
L
27 cm spacing, all detectors
X
D1
Y
X
X
D1
D1
Y
Y
C2
X
D2
Y
C2
X
X
D2
D2
Y
Y
C3
X
D3
Y
C3
C3
X
D3
Y
X
X
D3
D3
Y
Y
C4
X
D4
Y
C4
C4
X
D4
Y
X
X
D4
D4
Y
Y
B
W
B
L
B
B
W
W
B
B
L
L
L
D3
D3
D4
D4
C2
D2
C2
D2
D2
D1
D1
B
B
W
W
B
B
L
L
K. N. Borozdin, G. E. Hogan, C. Morris, W. C. Priedhorsky, A. Saunders, L. J. Schultz, and M. E. Teasdale, Nature 422, 277 (2003).

## Slide 11: It really works! (Funded by Decision Sciences)
Uranium

## Slide 12: Four different kinds of radiography
out
in
out
in
out
in
Scattering
Transmission/Stopped
Tagged

## Slide 13: Four different kinds of radiography
Scattering
Ln(N/N0)
Stopped (hr-1)
Tagged(hr-1)
LEU (20 kg)
2 5x12 cm EJ301
20x20x40 cm
concrete
Chart: time (ms)

## Slide 14
Z=-160 cm
Z=-150 cm
Z=-140 cm
Z=-130 cm
Z=-120 cm
Z=-110 cm
Z=-100 cm
Z=-90cm
Z=-80 cm
Z=-70 cm
Z=-60 cm
Z=-50cm
Z=-40 cm
Z=-30 cm
Z=-20 cm
Z=-10cm
200 cm
U cubes
3-d single sided tagged muon laminography image
U cubes
Neutron detectors were on the floor-same average distance as the front of the tracker from the cubes
2.5 cm steel
-160 cm

## Slide 15: Fuel cask imaging for NA-22
Muon trackers in weatherproof enclosures. One side elevated to increase muon flux through both detectors (falls off as ~cos2Ɵ).
Westinghouse MC-10 cask

## Slide 16: Fuel Cask Verification-GEANT model of diversion scenarios
Application of muon tomography to fuel cask monitoring, Volume: 377, Issue: 2137, DOI: (10.1098/rsta.2018.0052)
Fresh
Missing
Lead
Steel
14 day
2 weeks of exposure
Fresh
Missing
Lead
Steel
0.01
1.00
0.10
Fractiona change

## Slide 17: Human radiography
896 channels
Drift gas: 60% Ar/ 40% Isobutane
~100 Hz trigger rate at current geometry
1.5 m tall sample area
Lead
1.8 kg
Lead

## Slide 18: Cosmic ray radiography of a human phantom
Simple model
Power law source
Decay + stopping for transport
Cos2(q)
0 rl
2.2 rl
0
1
2
4
Perfect
Momentum determination
Exposure 24 hours in MMT
Combine weight multiple scattering and stopping to assess body composition.
Imagine what you can do with an artificial source

## Slide 19: Conclusions
Cosmic ray radiography/tomography
The work of George, Alvarez, Nagamine, and Borozdin has led to a vital and growing field.
Many new areas of application in a growing field.
Detectors and analysis continue to advance.
There are exciting prospects for affordable artificial sources.
Decision sciences scanner