## Slide 1: LYSO calorimeter related topics
Erik Swanson UW
PIONEER collaboration meeting
TRIUMF, Vancouver BC, Canada 2025

## Slide 2: Outline - LYSO Related Topics
Laser calibration/monitoring system
  Concept recap
  Leveraging on-going studies from muon g-2
Covering crystal polygon shapes
  Coatings or wraps?

## Slide 3
355 nm
Ce3+ energy levels in LYSO crystal
Concept recap
Monitoring LYSO light output with UV Laser
Ionizing radiation puts electrons in conduction band – excites Ce3+ ion
Directly excite Ce3+ ion with 355 nm UV laser light
De-excites with wavelength shifted blue light
Emission spectrum shape matches that of ionizing radiation
UV light absorption profile

## Slide 4
diffuser
100 Fiber bundles
To LYSO crystals
Fiber
launcher
Fiber
launcher
Fiber
launcher
Fiber
launcher
UV Laser head A
UV Laser head B
Filter wheel
Filter wheel
Non-polarizing beam splitter (3)
Double pulsing with two independent lasers
The slope of the variance/mean plot is the proportionality constant or gain of the PMT
Concept implementation features
Two independent laser pulsing systems illuminate each crystal in the calorimeter
UV LED based system was demonstrated in Test Beam calorimeter, cost prohibits UV laser based prototyping at this time
Outline

## Slide 5
L1
L2
FW 1
FW 2
laser breadboard for all 24 g-2 calorimeter units
Subset of laser breadboard components needed to study SiPM responses in a single g-2 calorimeter unit
Optical components were borrowed from the breadboard and sent to CENPA to build the double pulser shown below
On-going systematic studies of g-2 calorimeter response to lasers
One of the calorimeter units was disassembled, sent to CENPA and reassembled for the studies

## Slide 6
Dual laser pulser assembled from the optical components
While the laser wavelength is 403, not 355 nm, other optical components are equivalent, and we now have experience assembling and aligning a prototype calibration system

## Slide 8: Covering crystal polygon shapes coatings
PiBETA Tapered CsI crystals (305 nm). Coated with wavelength shifting lacquer with chemical composition POP+POPOP+COUM.1
POP (305nm -> 385nm), POPOP (-> 410nm), COUM.1 ( -> 460nm)
L3 BGO calorimeter crystals (truncated pyramid shapes). Coated with reflective white paint (40 – 70 um thick)

## Slide 9: Covering crystal polygon shapes Wraps
BABAR - slightly tapered CsI(Tl) crystals(5x6, 6x6, 36 cm long) wrapped with Dupont Tyvek (porous chalk loaded polyethylene fleece)
BELLE - CsI truncated pyramid crystals wrapped with 200 um Goretex and 50 um aluminized polyethylene
PIONEER – previous rectangular LYSO crystals were wrapped with precut ESR (silvered polyethylene (76 um thick)) strips stacked between crystals
Not so easy with tapered LYSO polygon crystals. ESR is too stiff to bend around edges and adhesives may affect light uniformity (LU)

## Slide 10
3D printed model of pentagon crystal shape
CAD drawing provides external surface of polygon unfolded as well as individual facet lines
Cutting the external shape out of ESR sheets takes 10 passes of the laser cutter
Using fewer passes, the laser cutter can scribe fold lines
Laser cut pentagon wrap with 6 pass fold scribe lines
3D pentagon model wrapped with ESR