## Slide 1
ReCap and KPPs
Progress and Tasks
  G4BL tuning
  see previous talks this session
  AI and machine learning*)
  Major beam design (Stefan)
Plans
  Beam request 2025
piE5 Beam
Beam specs and impact on key performance parameters
piE5 beamtest: Goals, sensitivity and plan
*) limited progress since last CM not covered, but news in previous talks
Anna Soter and
Peter Kammel

## Slide 2: KPPs and achieved results from test run
KPP |  | test run results and future work | impact
Rate 300k π/s stopped in ATAR Momentum lowest p preferred 55-70 MeV/c | 😁 | ok at 65 MeV/c | but 55 MeV/c better, get rid of DTAR, better range width
Momentum bite ∆p/p <2% | 🙂 | Probably not, requires more data analysis/beam modeling | pi-mu range based separation
Spot size smaller than ATAR | 🙄 | only 50% stopped, difficult, requires beam design, modeling and hardware, experimental design, active veto | halo rate and pile-up
Particle contamination µ/e less than 10% | 🙂 | Not yet, requires additional magnets, beam modeling and design | background

## Slide 3: G4BL modelling
History
  original piE5 model from PSI and Zach
  Urs and Peter established derived models
  results
    strong non-linear behavior in phase space (PS) observed
    additional effort required
      - grand solution:
      AI/ML surrogate model, first steps with Paul’s semester thesis
      but not follow up last year
      - full beam request for systematic AI based optimization not justified
Recent progress
  Peter
    included beam model from Giovanni’s thesis
    significantly developed my machinery towards real tuning
    together with ETH/PSI/StonyBrook effort that should be sufficient for beam request

## Slide 4: G4BL model updates: Procedure
USBL+DSBL
endUSBL+DSBL
DSBL

## Slide 5: G4BL model updates: 3 tunes to compare
Downstream needs tuning
G4BL
TRANSPORT 1st order

## Slide 6: G4BL model updates: Focus after triplet
“near” focus 22 cm to cQSK43 exercise only
“far” focus
53 cm to cQSK43
z (m)
z (m)
Giovanni USBL tune
MEG USBL tune
focus not elliptical per se (even if the x-PS is larger)
    depends on the tune
but the tune likely generates asymmetries
needs real beam design
First time reasonable tune of full PIONEER beamline

## Slide 7: G4BL model updates: Focus after triplet
near focus
far focus
Giovanni UBL tune
MEG UBL tune
far focus not worse than near focus
Liouville’s theorem?

## Slide 8: G4BL model updates: Focus after triplet
near focus
Giovanni USBL tune
far focus
Caution: Beam optics design must allow full benefit of phase space Non-Gaussian tails might affect conclusion

## Slide 9: Summary and plans
Developments
  G4BL tuning infrastructure developed
  Applied to existing piE5 beam line
  “Realistic” (in MC sense) predictions possible
Results
  (At first sight) upstream tunes gives similar focus
  Focus properties can and need to be studied carefully
  Sufficient progress to support beam request
Plans
  Develop automatic G4BL optimizer, cpu cluster
  compare with simple TRANSPORT
  Tune DSBL for realistic scenarios
    CALO position
    explore collimator options
    explore large final focus magnets
  I can do that, but only after a few months Help very welcome
Extended Plans
  Full extended beamline design
  Attack USBL issues

## Slide 10: Beam request: Justification and Goals
Justification
  Characterizing (and optimizing) the piE5 beam is critical to inform the overall piE5 detector setup and
  to design the required extension of this beam line with additional magnets to spatially separate the PID separation and target focus, and to achieve a smaller beam spot with large aperture final quadrupoles.
Goals
  Baseline
    Measure phase space with two thin x-y tracker planes for nominal settings with “required” precision
    Small variations in phases space and geometry as consistency checks
  Stretch
    Explore effect of bends and QSBs
    Extract phase space in separator
    Change USBL slits
    (Study USBL later)

## Slide 11: Beamtest: Phase Space, Geometry and Tasks
Phase space
Optimize measurement
  size and dependence of measurement uncertainties, subject to
  beam properties
  x,y resolution both planes
  multiple scattering first plane
Eliminate overwhelming e+ rate (collimator at 0.5 m after QSK43
Trigger with scintillator for PID
Prepare tracking detectors
Prepare beam tunes
Pepperpot as backup, but orders of magnitude less efficient

## Slide 12: BVR Preparation
1 page beam request
Convincing presentation at BVR
  Requirements and KPPs, impact on PIONEER
  Beam dynamics studies
  Measurement hardware
    thin 2 plane tracker system with scintillator trigger
  Measurement plan and expected results

## Slide 13: Holzer

## Slide 15: G4BL Model shows Strong Non-linear Effects
Peter - Urs
  Not directly comparable, but non-linear behavior confirmed
  Compare magnet current/field conversion
More work
  Understand main non-linear matrix elements
  Rough beam tuning, currently it does not represent measured reality
All pions
Peter 2023
Urs June 2024

## Slide 16: Far Focus: Tune Comparison

## Slide 17: Paul’s AI/ML Work
Design variables
  18 currents of the quadrupole and sextupole magnets
Final phase space
  Function of initial phase space and design variables
Optimize for m objectives functions
Use G4BL as “virtual” reality
5. Fast surrogate model
    ~
Results - Proof of Principle
    Analyzed upstream 6 magnets
    Varied current 20 A for training set in G4BL
    Optimized surrogate model for 2-D pictures
Advisors: Andy A. and Sebastian H.
x-y phase space
G4BL
surrogate model
~ 104 faster
    =
    =

## Slide 18: AI/ML Strategy
Method Developments
  Unified surrogate model for simultaneous 5-6d phase space description
  Include (selected) virtual plane in surrogate model definition, slits.
Full Beamline
  Extend the surrogate model to the full beam line. Particles making it to ATAR will exhibit very distinct features compared to initial flux.
  Does Urs confirm Peter’s non-linear effects? partially done.
Optimization Method
  Fit to optimize objective functions
    rate on ATAR,
Anna: What does that have to do with reality? Answer: 2 steps
  Step 1:
    Use G4BL as “virtual” reality to develop and establish method
    Importantly, study required input data set for robust prediction
  Step 2:
    Replace input-output relation with measured phase space (chamber tracker at ExB location)
    Re-optimize based on data
AI/ML Tuning strategy
  Full BL or DBL (downstream) only (Black box approach) DBL only probably not enough
  Step-by-Step optimization ?
UBL
DBL
    G4BL world
    =
    =
    Real world
    =
    =

## Slide 19: Major Design Upgrades
Two separate foci required so that background is rejected outside of detector
    1st focus separates particles after ExB velocity filter and reject μ and e on collimator
    2nd focus is a double x/y focus aimed at ATAR
  First attempt with singlet triplet promising
    but using only linear beam dynamics
  Large custom final quad?
Smaller momentum bite
  Retune upstream beam line to let dispersion grow
Degrader in dispersive section?
  Requires dispersive double focus
beam envelope in V-H planes
p+
20 cm
20 cm
V
H

## Slide 20: Major upgrade: Extend Beam with Two Vertical Foci
For particle separation and target focus two separate foci required, so that background is rejected outside of detector
  1st focus separates particles after ExB velocity filter and reject μ and e on collimator
  2nd focus is a double x/y focus aimed at ATAR
First attempt with s-t promising
  large final magnet
  phase space
    initial x: 2.40 π mm r y: 0.09 π mm r
    promising final focus
200
!

## Slide 21: Kinematics
Si

## Slide 22: piE5 @ PSI - World’s Brightest Stopped Pion Beam
PIONEER
MEG
Mu3e
experimenters have full control over beam line (after first bend)
        carefully studied for fundamental muon experiments
still surprises for pions, unique PIONEER requirements

## Slide 23: Simple Transport Model
Compare Δp/p= 3/0 %
1st order only
  2nd order diverges
  other discrepancies to PIONEER Run ‘22
upstream part in shielding
    indirect diagnostics with slits
beam envelope in V-H planes
V
H
extraction, momentum selection and achromat
particle separation, focus on target
MEG tune adjusted to PIONEER geometry, P-R Kettle
BxE
D
20 cm
20 cm
p+
dipoles
separator

## Slide 24: Puzzles from beam test
Explore/explain most striking puzzles, problems
strong
dispersion
beam meandering
significant dispersion
insufficient focus
cannot achieve PID separation and target focus simultaneously

## Slide 25: Summary of findings
Final focus
PID
Dispersion? at target
Δp/p two methods
  TOF
    16m beamline
    1% Δp/p ~ 1 ns (65 MeV/c)
  Direct stopping measurement with range curve
    pion signal amplitudes with different degraders
    use π→ μ sequence to identity stops
  analysis needed

## Slide 26: Particle Separation Good Enough?
In area restricted to ATAR
(optimistic accounting)
e: 25.0%
μ: 32.1%
π: 42.9%
amplitude in scint.
TOF (ns)
No location of collimator !
Separator HV can be increased
π
μ
e
Patrick
Josh

## Slide 27: Dispersion at Target Location?
TOF changes when when detector moves 5 cm to the left
X=X(P), significant dispersion D at target location, deteriorates focus.
Patrick

## Slide 28: Dispersion at Target Location?
D~1 cm/%
similar to dispersive section??

## Slide 29: Beam: piE5 @ PSI - World’s Brightest Stopped Pion Beam
Progress 2023
  PIONEER requirements and test beam 2022 results
    Rate: 300k π/s stopped in ATAR: ok at 65 MeV/c
    Momentum bite: ∆p/p <2%: marginal
    Spot size: <2 cm FWHM: not achieved
    µ,e less than 10% π: needs second focus extension
  improved understanding and optimization
    non-linear effects due to large phase space
    beamline model with G4BL
    novel promising machine learning approach (Adelmann et al)
Plans 2024
  machine learning
    extend machine learning to full beam line
    optimization of beam properties
    prepare experimental verification
  beam design
    2nd focus extension
    better focus
    retune for smaller ∆p/p <2%
x-y phase space
request PSI support in design
Physics
oncept
Components
Summary

## Slide 30: People and Timeline
People
  Andy Adelmann
    No progress this year, needs student
    Kolja interested candidate
  David Tarazona
    1st rate beam physicist
    Currently work with Lawrence
    Applied for Cornell AI in Science Postdoctoral Fellowship
    Plans to model pE5 with BMAD
  Kolja also analyzing first beam test
  Remark concerning simulation
    Prediction won’t be ready on CDR timescale
    Include beam as parametrized input
  Hope that activity can resume in fall
  Other help more than welcome
Timeline
Fall 2026 | Beam test
Fall 2025 | AI/ML studies with G4BL finalized to justify πE5 2026 beam request. Extend the surrogate model to the full beam line running Optimization demonstrated Measurement strategy developed At the same time we should have tracker system available.
Fall 2025 | Beam design with extension ready To justify extension measurements
CDR | What do we need for that?