## Slide 1
Industrial Application of OPM:
Flow Metering
  —
    08.08.2025 Peter Koss and Leonhard Schmieder, Fraunhofer IPM
    Fraunhofer Model and Showcase Development
    Flow Metering with OPM
    Summary and Outlook
Logobereich

## Slide 2: Fraunhofer Model and Showcase Development
Fraunhofer IPM in 2023
  Fraunhofer Institute for Physical Measurement Techniques (IPM)
  Operating budget: 26 Mio. €
        Industrial revenue share: 40 %
        Acquired projects: 40 %
        Basic Funding: 20 %
  Investments: 2 Mio. €
  Employees: 270

## Slide 3: Fraunhofer Model and Showcase Development
Business units
Production Control
Inline microscopy
Gas and Process Technology
Trace gas analysis
Object and Shape Detection
Capture underwater infrastructure
Photonic Systems
Laser light sources

## Slide 4
Photonic Systems: Laser frequency converters
Fraunhofer Model and Showcase Development
      Color change
      MIR-to-NIR conversion
      Tunable colors
      Use of non-linear optics in volume resonators or waveguides for frequency conversion
      High efficiency!!

## Slide 5
State-of-the-art in industrial flow metering
Flow Metering with OPM
Inertial Flowmeters: Very accurate
Ultrasound Flowmeters: clamp-on
Magnetic Flowmeters: large pipes
Mechanical Flowmeters: cheap
      State-of-the-art
      Many different flowmetering technologies
      Wide range of application cases covered
      Current technologies are very robust and work in harsh environments
       Still some cases are not covered (requires a new solution)

## Slide 6
State-of-the-art in industrial flow metering
Flow Metering with OPM
Jankees Hogendoorn et al., Practical Experiences Obtained with the Magnetic Resonance Multiphase Flowmeter, KROHNE Messtechnik GmbH, 2015
Flow direction
RF-coil
1 m
      Krohne M-Phase 5000
      NMR based flow meter  Multiphase measurement
      Skin effect  Cannot measure through metallic pipes

## Slide 7
Basic Idea
Flow Metering with OPM
Strong magnet
Hydrogen (1H)
1 Tesla
Voltage
„classical“ NMR
IPM-approach
Time
Magnetic field
Time

## Slide 8
Basic Idea
Flow Metering with OPM

## Slide 9
Basic Idea
Flow Metering with OPM
      Key advantages
      Contactless (no direct contact with fluid)
      Can measure through steel pipes
      Hydrogen nuclei are the magnetic marker  wide range of fluids are measurable

## Slide 10
Experimental Setup
Flow Metering with OPM
1T-Halbach magnet
coil
OPM
½‘‘ steel pipe
5 cm
magnetic shields

## Slide 11
Measuring the flow velocity
Flow Metering with OPM

## Slide 12
Sensitivity to the flow profile
Flow Metering with OPM
100x100px-mask
Pipe diameter (px)
Pipe diameter (px)
      Origin of the signal and signal shape:
      Include the contributions of the flow profile, field distribution
      OPM signal is an average over all two

## Slide 13
Sensitivity to the flow profile
Flow Metering with OPM
Inner wall of the shield
RF-coil
OPM

## Slide 14
Sensitivity to the flow profile
Flow Metering with OPM
Inner wall of the shield
RF-coil
OPM
Pipe diameter (px)
Pipe diameter (px)

## Slide 15
Sensitivity to the flow profile
Flow Metering with OPM
Inner wall of the shield
RF-coil
OPM
Pipe diameter (px)
Pipe diameter (px)

## Slide 16
Sensitivity to the flow profile
Flow Metering with OPM
Inner wall of the shield
RF-coil
OPM
Pipe diameter (px)
Pipe diameter (px)
Pipe diameter (px)
Pipe diameter (px)

## Slide 17
Sensitivity to the flow profile
Flow Metering with OPM
Relative amplitude
Voltage applied to coil (mV)

## Slide 18
Sensitivity to the flow profile
Flow Metering with OPM
Pipe diameter (px)
Pipe diameter (px)
Pipe diameter (px)
Pipe diameter (px)
Pipe diameter (px)
Relative amplitude
Voltage applied to coil (mV)

## Slide 19
A clamp-on magnetic flow meter: The Halbach magnet
Flow Metering with OPM
Under the right angle a Halbach magnet can be opened without force.
42 cm
C. W. Windt et al., „A portable Halbach magnet that can be opened and closed without force: The NMR-CUFF,“ Journal of Magnetic Resonance, Bd. 208, pp. 27-33, 2011.

## Slide 20
A clamp-on magnetic flow meter: The Halbach magnet
Flow Metering with OPM
42 cm
Half shell segment
Hinge cylinder
      Magnets are housed in half shells
      Whole magnet can be longer by adding segments

## Slide 21
A clamp-on magnetic flow meter: The shield
Flow Metering with OPM
© Sekels GmbH
28 cm
      Clamp on design with inlet diameter of 1“
      Two layer shield with shielding factor approx 103
      System of coils will be added

## Slide 22
Current status and future opportunities
Summary
      Current status:
      Proof-of-principle of OPM based flow metering
      Has specific advantages compared to other flow metering technologies
      Next steps:
      Build a clamp-on demonstrator
      Make it usable in the field
      Far future ? (10+ years):
      Commercial OPM based flow meter

## Slide 23
Contact
  —
    Peter Koss
    Gas and Process Technology
    Caloric Systems
    Fraunhofer Institute for Physical Measurement Techniques IPM
    Phone +49 761 8857 243 peter.koss@ipm.fraunhofer.de http://www.ipm.fraunhofer.de/en | LinkedIn | YouTube
Logobereich