## Slide 1
Quantum noise in a squeezed-light-enhanced
multiparameter quantum sensor
Aleksandra Sierant
ICFO – Institute of Photonic Sciences
Atomic Quantum Optics Group (M. W. Mitchell)
Wokrshop on Optically Pumped Magnetometers
8th August 2025, Paul Scherrer Institute, Villigen, Switzerland

## Slide 2
Braginsky or Helstrom?
Source: https://www.ligo.caltech.edu/news/ligo20160426

## Slide 3
Braginsky or Helstrom?
Source: https://www.ligo.caltech.edu/news/ligo20160426
Vladimir Braginsky

## Slide 4
quantum sensing – Braginsky approach
Vladimir Braginsky
Source: https://www.ligo.caltech.edu/news/ligo20160426
measuring x, perturbs p

## Slide 5
quantum sensing – Braginsky approach
Vladimir Braginsky
Source: https://www.ligo.caltech.edu/news/ligo20160426
  perturbing p affects x
  measurement back-action (MBA)
measuring x, perturbs p

## Slide 6
quantum sensing – Braginsky approach
Vladimir Braginsky
Source: https://www.ligo.caltech.edu/news/ligo20160426
  Standard Quantum Limit (SQL)
  perturbing p affects x
  measurement back-action (MBA)
measuring x, perturbs p

## Slide 7
quantum sensing – Braginsky approach
Vladimir Braginsky
Source: https://www.ligo.caltech.edu/news/ligo20160426
  quantum enhancement to improve sensor’s performance
  Standard Quantum Limit (SQL)
  perturbing p affects x
  measurement back-action (MBA)
measuring x, perturbs p

## Slide 8
Multiparameter sensor
balanced
detector
probe
87Rb
-
Stokes parameter
HWP
Wollaston
prism

## Slide 9
Multiparameter sensor
balanced
detector
probe
87Rb
-
Stokes parameter
HWP
Wollaston
prism
spin projection noise measurements

## Slide 10
Multiparameter sensor
balanced
detector
Wollaston
prism
pump
87Rb
-
probe
Stokes parameter
HWP

## Slide 11
Multiparameter sensor
balanced
detector
Wollaston
prism
pump
87Rb
-
probe
Stokes parameter
HWP
A.Fabricant, I. Novikova, and G. Bison. New Journal of Physics 25.2 (2023): 025001.

## Slide 12
Multiparameter sensor
balanced
detector
Wollaston
prism
pump
87Rb
-
probe
Stokes parameter
HWP
z
y
x

## Slide 13
Multiparameter sensor
Stokes parameter
balanced
detector
Wollaston
prism
87Rb
-
probe
pump
time domain
HWP

## Slide 14
Multiparameter sensor
Stokes parameter
balanced
detector
Wollaston
prism
87Rb
-
probe
pump
Fourier transform
time domain
frequency domain
HWP

## Slide 15
Multiparameter sensor
Stokes parameter
balanced
detector
Wollaston
prism
87Rb
-
probe
pump
Fourier transform
time domain
frequency domain
HWP
frequency domain
demodulation

## Slide 16
in phase quadrature
out of phase
quadrature
Multiparameter sensor
Stokes parameter
balanced
detector
Wollaston
prism
87Rb
-
demodulation
probe
pump
HWP

## Slide 17
Stochastic spin dynamics
collective
spin
light shift
relaxation
optical
pumping
spin noise
Larmor
precession
B
pump

## Slide 18
Stochastic spin dynamics
collective
spin
light shift
relaxation
optical
pumping
spin noise
Larmor
precession
spin projection noise (SPN)
B
pump

## Slide 19
Stochastic spin dynamics
collective
spin
light shift
relaxation
optical
pumping
spin noise
Larmor
precession
spin projection noise (SPN)
measurement backaction (MBA)
quantum noise
atoms
B
pump

## Slide 20
Stochastic spin dynamics
collective
spin
light shift
relaxation
optical
pumping
spin noise
Larmor
precession
spin projection noise (SPN)
measurement backaction (MBA)
quantum noise
atoms
random rotation around z
x
y
z
B

## Slide 21
Stochastic spin dynamics
collective
spin
light shift
relaxation
optical
pumping
spin noise
Larmor
precession
photon shot noise (PSN)
Stokes parameters
spin projection noise (SPN)
measurement backaction (MBA)
quantum noise
atoms
B
pump
readout: Faraday rotation
described by Stokes parameter

## Slide 22
Stochastic spin dynamics
collective
spin
light shift
relaxation
optical
pumping
spin noise
Larmor
precession
photon shot noise (PSN)
Stokes parameters
spin projection noise (SPN)
measurement backaction (MBA)
quantum noise
atoms
light
readout: Faraday rotation
described by Stokes parameter
pump

## Slide 23
Stochastic spin dynamics
photon shot noise (PSN)
Stokes parameters
spin projection noise (SPN)
measurement backaction (MBA)
quantum noise
atoms
light
detected spectrum:
readout: Faraday rotation
described by Stokes parameter
pump

## Slide 24
Stochastic spin dynamics
photon shot noise (PSN)
Stokes parameters
spin projection noise (SPN)
measurement backaction (MBA)
quantum noise
atoms
light
detected spectrum:
instantaneous
accumulative
readout: Faraday rotation
described by Stokes parameter
pump

## Slide 25
Multiparameter sensor: quantum noise
unpumped atoms
detected spectrum:

## Slide 26
Multiparameter sensor: quantum noise
detected spectrum:
unpumped atoms

## Slide 27
Multiparameter sensor: quantum noise
PSN
detected spectrum:
unpumped atoms

## Slide 28
Multiparameter sensor: quantum noise
SPN
PSN
detected spectrum:
unpumped atoms

## Slide 29
Multiparameter sensor: quantum noise
unpumped atoms
pumped atoms
SPN
PSN
detected spectrum:
pumped atoms

## Slide 30
Multiparameter sensor: quantum noise
unpumped atoms
pumped atoms
MBA
SPN
PSN
detected spectrum:
pumped atoms

## Slide 31
Multiparameter sensor: quantum noise
unpumped atoms
pumped atoms
detected spectrum:
SPN dominated
PSN dominated

## Slide 32
Multiparameter sensor: sensitivity
polarisation noise PSD

## Slide 33
Multiparameter sensor: sensitivity
polarisation noise PSD
magnetic sensitivity

## Slide 34
Multiparameter sensor: sensitivity
polarisation noise PSD
magnetic sensitivity
+ responsivity
10-6
10-7
10-8
10-9
10-10
102
103
test field frequency [Hz]
rf
dc
Peak spectral density [V2]
104

## Slide 35
Multiparameter sensor: sensitivity
polarisation noise PSD
magnetic sensitivity
+ responsivity
10-6
10-7
10-8
10-9
10-10
102
103
test field frequency [Hz]
102
104
103
Frequency [Hz]
Sensitivity [pT/√Hz]
102
101
rf
dc
rf
dc
Peak spectral density [V2]
104

## Slide 36
Photon shot noise (PSN)
measurement backaction (MBA)
photon shot noise (PSN)
y
z
B
x
detected spectrum:
squeezing parameter
antisqueezing parameter

## Slide 37
Multiparameter sensor: quantum noise
x
detected spectrum:
squeezing parameter
antisqueezing parameter

## Slide 38
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 39
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 40
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 41
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
squeezed
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 42
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
squeezed
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 43
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
squeezed
antisqueezed
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 44
Multiparameter sensor: quantum noise
coherent
unpumped atoms
pumped atoms
squeezed
antisqueezed
dc detection
x
detected spectrum:
antisqueezing parameter
squeezing parameter

## Slide 45
Multiparameter sensor: quantum noise
unpumped atoms
pumped atoms
squeezed
antisqueezed
dc detection
rf detection
antisqueezed
coherent
coherent
squeezed

## Slide 46
Multiparameter sensor: quantum noise
unpumped atoms
pumped atoms
squeezed
antisqueezed
dc detection
rf detection
antisqueezed
coherent
coherent
squeezed
squeezed light probing improves shot noise for both fields

## Slide 47
Multiparameter sensor: quantum-enhanced sensitivity
quantum enhancement of magnetic sensitivity with squeezed light for both fields
measurement bandwidth enhancement for both fields

## Slide 48
Single parameter sensor: quantum noise
unpumped (spin noise spectroscopy)
coherent light
pumped (Bell-Bloom magnetometer)
squeezed light
coherent light
C. Troullinou et al. Phys. Rev. Lett. 127, 193601 (2021)
response
spin noise + photon shot noise
photon shot noise

## Slide 49
Single parameter sensor: quantum-enhanced sensitivity
unpumped (spin noise spectroscopy)
coherent light
pumped (Bell-Bloom magnetometer)
squeezed light
coherent light
C. Troullinou et al. Phys. Rev. Lett. 127, 193601 (2021)
response
spin noise + photon shot noise
photon shot noise

## Slide 50
What about measurement backaction?
multi-parameter sensor
single-parameter sensor

## Slide 51
What about measurement backaction?
multi-parameter sensor
single-parameter sensor
measurement backaction shunted into the unmeasured spin component

## Slide 52
quantum-enhanced sensitivity
squeezed light
coherent light
300 fT/√Hz
1.6 dB quantum enhancement of magnetic sensitivity with 1.9 dB squeezed light
measurement bandwidth enhancement from 275 Hz to 320 Hz
C. Troullinou et al. Phys. Rev. Lett. 131, 133602 (2023)

## Slide 53
Conclusions
demonstrated practical, multiparameter sensor based on OPM
  simultaneous detection of rf and dc magnetic fields
  quantum noise limited sensitivity
implemented quantum enhanced protocols
squeezed-light probing
improved sensitivity and measurement bandwidth
studied interplay between different quantum noise sources

## Slide 54
Conclusions
demonstrated practical, multiparameter sensor based on OPM
  simultaneous detection of rf and dc magnetic fields
  quantum noise limited sensitivity
implemented quantum enhanced protocols
squeezed-light probing
improved sensitivity and measurement bandwidth
studied interplay between different quantum noise sources
outlook
miniaturisation

## Slide 55
Outlook: miniaturisation
quantum-enhanced multi-parameter sensor
miniaturisation: QUANTIFY project
photonic integrated squeezer
https://www.lionix-international.com/
macroscopic cell
table top squeezer
MEMS cell (csem.ch)

## Slide 56
OPM sensor - cd
Diana Méndez Avalos
  Earth’s field operation
  QE via spin squeezing
  miniaturised OPM
  find Diana during poster session!

## Slide 57
Atomic Quantum Optics group at ICFO

## Slide 58
Atomic Quantum Optics group at ICFO
  Morgan
  Diana
  Santiago

## Slide 59
Atomic Quantum Optics group at ICFO
  Morgan
  Diana
  Santiago
  Thank you!

## Slide 60
quantum sensing – Braginsky approach
measuring x, perturbs p
  Standard Quantum Limit (SQL)
  quantum enhancement
  perturbing p affects x
  measurement back-action (MBA)

## Slide 61
B
Outlook 2: stroboscopic probing
measurement backaction evasion in a multiparameter sensor

## Slide 62
Who should care?
  Quantum noise affects high precision sensing
  optical interferometers
  atomic clocks
  atomic gravimeters and gyroscopes
Nat .Phys. 2011
www.macqsimal.eu/
igfae.usc.es/igfae/es/experimento/ligo/
www.iqo.uni-hannover.de

## Slide 63
quantum sensing – Braginsky approach
spin squeezing
back-action evasion
[1] Vasilakis, G., et al. "Generation of a squeezed state of an oscillator by stroboscopic back-action-evading measurement." Nature Physics 11.5 (2015): 389-392.
[2] Vasilakis, G., V. et al. "Stroboscopic backaction evasion in a dense alkali-metal vapor." Physical review letters 106.14 (2011): 143601.
[3] Ciurana, M., et al. "Entanglement-enhanced radio-frequency field detection and waveform sensing." Physical review letters 119.4 (2017): 043603.
[1] Colangelo, G., et al. "Simultaneous tracking of spin angle and amplitude beyond classical limits." Nature 543.7646 (2017): 525-528.
[2] Troullinou, C., et al. "Squeezed-light enhancement and backaction evasion in a high sensitivity optically pumped magnetometer." Physical Review Letters 127.19 (2021): 193601.
[3] Troullinou, C., et al. "Quantum-enhanced magnetometry at optimal number density." Physical Review Letters 131.13 (2023): 133602.
spin has three components
➔ different strategy for MBA evasion

## Slide 64
spin dynamics
resonant dc
no rf
strong dc
no rf
weak dc
no rf
resonant dc
positive rf
resonant dc
negative rf
B
B
B
B

## Slide 65
multiparameter sensor: I and Q quadratures
collective
spin
Larmor
light shift
relaxation
optical
pumping
spin noise

## Slide 66
Bell-Bloom optical pumping
resonant field
weaker field
B
B
B
stronger field

## Slide 67
Bell-Bloom optical pumping
resonant field
weaker field
B
B
B
stronger field
Q quadrature (90° out of phase) carries the signal

## Slide 68
optimal number density
squeezed light
coherent light
300 fT/√Hz
C. Troullinou et al. Phys. Rev. Lett. 131, 133602 (2023)

## Slide 69
Squeezer

## Slide 70
quantum sensing – Braginsky approach
measuring x, perturbs p
  Standard Quantum Limit (SQL)
  quantum enhancement
  perturbing p affects x
  measurement back-action (MBA)

## Slide 71
Multiparameter sensor
Stokes parameter
balanced
detector
Wollaston
prism
87Rb
-
probe
pump
time domain
HWP

## Slide 72
Photon shot noise (PSN)
detected spectrum:
time
A
t
t
1
0
d
B
*
*
U
N
C
A
L
1
A
P
C
L
R
W
R
A
3
D
B
R
B
W
3
0
k
H
z
V
B
W
1
0
H
z
S
W
T
1
.
4
5
s
R
e
f
-
6
5
.
7
d
B
m
C
e
n
t
e
r
1
M
H
z
1
4
5
m
s
/
-
7
5
-
7
4
-
7
3
-
7
2
-
7
1
-
7
0
-
6
9
-
6
8
-
6
7
-
6
6
1
M
a
r
k
e
r
1
[
T
1
]
-
6
9
.
6
2
d
B
m
1
.
4
5
0
0
0
0
s
Date: 16.APR.2003 00:10:26
coherent
antisqueezed
squeezed
noise (dB)
time (s)
2 dB
4 dB

## Slide 73
Photon shot noise (PSN)
squeezing parameter
detected spectrum:
time
A
t
t
1
0
d
B
*
*
U
N
C
A
L
1
A
P
C
L
R
W
R
A
3
D
B
R
B
W
3
0
k
H
z
V
B
W
1
0
H
z
S
W
T
1
.
4
5
s
R
e
f
-
6
5
.
7
d
B
m
C
e
n
t
e
r
1
M
H
z
1
4
5
m
s
/
-
7
5
-
7
4
-
7
3
-
7
2
-
7
1
-
7
0
-
6
9
-
6
8
-
6
7
-
6
6
1
M
a
r
k
e
r
1
[
T
1
]
-
6
9
.
6
2
d
B
m
1
.
4
5
0
0
0
0
s
Date: 16.APR.2003 00:10:26
coherent
antisqueezed
squeezed
noise (dB)
time (s)
2 dB
4 dB

## Slide 74
references for this talk
Michał Lipka
Morgan W. Mitchell
in preparation
Santiago
Tabares Giraldo
Diana
Méndez Avalos
Charikleia Troullinou