## Slide 1: Magnetic Field Optimisation and Design Procedures for Quantum Sensing Applications
Dr Chris Morley

## Slide 2: Contents
Stream function methods
  Mumetal coupling
Discrete coil optimisation
  Loops, Saddle and Ellipse coil optimisation
Permanent magnet optimisation
Hand wound initial tests
  Gravimeter and Inertial Navigator
GA4 Benchtop Magnetic Shield
  First steps towards PCBs
RF Optically Pumped Magnetometer Bias Coils
  Flex PCB wrapper coils
Our Methods
Testing, applications and projects

## Slide 3: Our Methods: Streamfunction Method
Analytical Stream function Method
Green’s function method determines current density required to generate field, can couple to mumetal if required
Analytical method determines current density, contours of this are then wire paths
Resolution not tied to mesh
Rapid code execution allows for fast iteration
Pseudo-current density on shield
Boundary conditions to constrain field
Packer, M., et al. Physical Review Applied 14.5 (2020): 054004.

## Slide 4: Our Methods: CreateCoil
Building Block Optimisation
Optimises discrete coil loops/saddles/ellipses, more applicable to high magnitude magnetic field requirements
Express field as spherical harmonics, and null error harmonics by removing harmonic coefficients.
Weighting of magnetic field harmonic, fn,m
Antisymmetric current flow
Optimal volume where the field deviates by <1% is ~3 times greater
P. J. Hobson et al., IEEE TIM
Vol 72 doi:10.1109/TIM.2023.3284138.
CreateCoil Paclet:
Substitute in for Helmholtz loop

## Slide 5: Our Methods: Permanent Magnets
Expanding Green’s Function Methods
Applying similar methods to determine permanent magnet arrangements, by utilizing the scalar potential
Suitable for cases where the field is constantly required
Expand using cylindrical Green’s function
Surface magnetisation
Hobson, P. J., Morley, C. et al. Physical Review Applied 22.3 (2024): 034015
Morley C. et al. – In Progress

## Slide 6: Initial Applications
Gravimeter
First application of stream function methods
Utilising 3D printed former with hand wound coil traces
Less than 1% error over target region
Estimated reduction of the systematic shift from the quadratic Zeeman effect from 90mrad to 9.9rad
Hybrid coil systems for atom interferometry:
Reduce quadratic Zeeman effect induced error
Control atoms during preparation
Reduce sensor size, weight, and bulk
Without Passive Shielding:
Dark blue dash – Theory
Triangles - Experiment
With Passive Shielding:
Cyan/black line – Theory
Circles - Experiment
Hobson, P. J., et al. Scientific Reports 12.1 (2022): 1-12.

## Slide 7: Initial Applications
Navigator
Larger planar coils retrofitted to existing quantum navigator experimental apparatus
Navigator required magnetic field stabilization
Less than 1.3% deviation over the target region
3x improvement over previous coil system
Measurements of uniform and gradient fields
Black dash – Theory
Red dots - experiment
Davis, A., et al. Physics Open 20 (2024): 100227.

## Slide 8: Moving to PCBs
GA4 – Magnet Shielding
Collaboration to build a product with Magnetic Shields Limited for OPM sensor development
Required a level of robustness prior projects had not
Began to develop PCB manufacturing knowledge and develop our pipeline
System nulled from 1.68nT to 230pT over 40% of shields length.
Johnson noise <15 fT/√Hz – hitting the noise floor of the magnetometer
Uniform and Gradient fields.
Hobson, P.J., et al. IEEE Transactions on Instrumentation and Measurement 72 (2023): 1-9.

## Slide 9: RF Optically Pumped Magnetometer
Bias Coil Wrapper
Bx, By and Bz bias field generation around a vapour cell
cylindrical geometry with flex PCB with end caps to aid field uniformity
Optical Access
PCB endcap on 3D printed test former
Theory (solid lines) vs experiment (black dots)

## Slide 10: RF Optically Pumped Magnetometer 2.0
Bias Coil Wrapper
Moved to cuboidal geometry for vapour cell – 5 x 5 x 5 volume
Development of flex PCB net to include all three required bias fields with minimized alignment requirements
Required 100 with less than 600mA current and max deviation of 2%
Simulated percentage error of:
(red)
(blue)
(black)

## Slide 11: RF Magnetometer MK2

## Slide 12: RF Magnetometer MK2

## Slide 13: Conclusion
Rapid iteration capabilities due to analytic nature of methods
Variety of methods for various different applications
Developed robust methods for designing magnetic field shaping systems
Variety of applications and form factors
Can incorporate mumetal coupling
Co-optimisation of for example, wrapper and end caps
Established a reliable and efficient PCB pipeline
Retrofitting or incorporated design capabilities

## Slide 14: Acknowledgements
Additional Thanks:
Michael Packer
Peter Hobson
Noah Hardwicke
Sionnach Devlin
Dom Simms
Our Project Partners
David Woolger
Bartel van der Veek
Curtis Manley
Philip Marsden
Prashant Patel
Steve Lenham
CreateCoil Paclet:
Our Group:
Mark Fromhold
Alister Davis
Niall Holmes
Nandhakishore Perarulalan
Kosit Wongcharoenbhorn
Thomas Smith
Adam Taylor
Monty Clark
Julen Eccleston Etxeberria
Madeleine Sonnenberg
Alice Ray
Christopher.Morley2@nottingham.ac.uk