## Slide 1: Evaluating interference suppression algorithms for OPM-MEG
Christoph Pfeiffer
Assistant Professor and Head of the Swedish National Facility for MEG (NatMEG)
Deptartment of Clinical Neuroscience

## Slide 2: (OPM-)MEG at KI
Primarily used for clincial and cognitive neuroscience
SQUID-MEG interference suppression: IAS + MaxFilter
Since 2024: Whole-head OPM-MEG with 136 sensors (Fieldline HEDSCAN) & smart helmet
IAS + MaxFilter does not work for OPM-MEG

## Slide 3: Algorithms
Homogenous Field Correction (HFC) Tierney et al., NeuroImage, 2021
Signal Space Separation (SSS) and iterative implementation Taulu and Kajola, J. Appl. Phys., 2005; Holmes et al., Sensors, 2023
Adaptive Multipole Model (AMM) Tierney et al., Hum. Brain Mapp., 2024
Signal Space Projection (SSP) Uusitalo and Ilmoniemi, Med. Biol. Eng. Comput., 1996
Hum Brain Mapp. 2024 Mar 4;45(4):e26596

## Slide 4: Simulated data

## Slide 5: Simulation
Implemented in Fieldtrip/MATLAB
Sensor array (130 sensors, single-axis mode), head and sourcemodel from a real recording
Signals= sensor noise + brain signal + noise signals
  Sensor noise (white + pink) with amplitudes matched to recorded data
  Brain signal: 10 highly coupled current dipole sources (±10 pT, single-shell headmodel)
  Noise signals: magnetic dipoles (±141 pT)
    Dental noise source @0.14 m
    Chest noise source @0.3 m
    Close environmental noise sources @1 and 2 m
    Far environmental noise sources @3 and 5 m
Empty room without brain, dental and chest sources
dental
chest
1 m
brain
2 m
3 m
5 m
PSD (T2)
Notes: .

## Slide 6: Homogenous Field Correction (HFC)
Noise suppression (dB)
Signal change (%)

## Slide 7: Signal Space Separation (SSS)
Unstable!
Noise floor ratio
order

## Slide 8: Iterative Signal Space Separation (SSSit)
Unstable!

## Slide 9: Adaptive Multipole Models (AMM)

## Slide 10: Signal Space Projection (SSP)

## Slide 11: (OPM-)MEG at KI
Primarily used for clincial and cognitive neuroscience
SQUID-MEG interference suppression: IAS + MaxFilter
Since 2024: Whole-head OPM-MEG with 136 sensors (Fieldline HEDSCAN) & smart helmet
IAS + MaxFilter does not work for OPM-MEG

## Slide 12: Signal Space Projection (SSP)

## Slide 13: Recorded data
Notes: Alright. Now let’s look at some real data.

## Slide 14: Recording
Single participant (left-handed, no dental wire)
130 single-axis sensors
Paradigms:
  Auditory task
  Tapper (index finger)
Empty room before (sensors flush with helmet)
Empty room after (minimal sensor move)
Recording
Empty room before
Empty room after

## Slide 15: Results
Iterative SSS:
  Temporal: unstable
  Spatial: problems with source reconstruction
ItSSS-temporal: Peak channel

## Slide 16: Results
HFC:
Peak channel vs order
AMM:
Peak channel vs Lout
Iterative SSS:
  Temporal: unstable
  Spatial: problems with source reconstruction
HFC+AMM:
  Signal drop at high order/Lout

## Slide 17: Results
Iterative SSS:
  Temporal: unstable
  Spatial: problems with source reconstruction
HFC+AMM:
  Signal drop at high order/Lout
  Oscillatory spatial patterns appear at higher order/Lout

## Slide 18: Results
Iterative SSS:
  Temporal: unstable
  Spatial: problems with source reconstruction
HFC+AMM:
  Signal drop at high order/Lout
  Oscillatory spatial patterns appear at higher order/Lout
AMM (temporal):
  Minor SNR increase at lower thresholds
Signal-to-Noise Ratio
tAMM: Peak channel vs thr

## Slide 19: Results
SSP:
  Good signal integrity
  Minor differences between empty room before and after
08/08/2025
19
SSPbefore:
Peak channel vs ncomp
SSPafter:
Peak channel vs ncomp

## Slide 20: Conclusions/Recommendations

## Slide 21: Conclusions/Recommendations
HFC, AMM and SSP perform well but parameter choice important
Avoid SSS/tSSS (for now)
If signal amplitudes or topography are important, less is more:
  1st order HFC, AMM with Lout = 1, or SSP (≤4 components)
When using AMM: Lin≥10
For high participant noise, e.g., dental wire: tAMM (i.e., thr < 1)
For strong noise sources:
  SSP if interference is present in reference data
  Otherwise: AMM with high Lout, but: beware of spatial filtering artifacts and amplitude changes

## Slide 22: Conclusions/Recommendations
Record empty room after (moving sensors as little as possible)
Limitation: Tested only for Fieldline Hedscan
Next:
  Real data with dental noise
  Dual and triaxial data

## Slide 23: Thank you!