## Slide 1
Fast total field OPM for muscle measurements: first in vivo recordings in MyoQuant project
Victor Lebedev (PTB, Berlin)
13th Workshop on optically-pumped magnetometers
2025-08-08

## Slide 2: MyoQuant – Myography with OPMs
Exploration of EMG & MMG
Commercial sensor characterization
MMG in demonstrator
Shield design & feasibility validation of mobile magnetomyography (MMG)
Lab-based setups and evaluation
Miniaturization of the probing unit
8 cm
1 cm
This talk: high-density MMG & EMG
Nordenström et al. 2024, https://www.nature.com/articles/s41598-024-69829-y
Nordenström et al. 2025,
https://doi.org/10.1117/12.3043675
SQUID-MMG: Poster by Stefan Hartwig
Earlier works:
Kruse et al. 2025 https://dx.doi.org/10.1088/2057-1976/adaec5
Noury et al. 2025 http://iopscience.iop.org/article/10.1088/1741-2552/adeaeb
System integration MyoQuant demonstrator

## Slide 3: Magnetic sensor requirements
Kilohertz-scale bandwidth demanded
  Sub-millisecond muscle response observed in needle EMG
  400+ Hz signals detected with broadband SQUID magnetometers
  400+ Hz spectral components observed with SERF OPMs in voluntary contraction
Muscle flux density with amplitude from 1 pT to 100 pT signals were observed in various experiments, depending on signal origin, mode of stimulation, actual distance to sensor, and sensor type
  Signals feature about 1 pT/ spectral energy (20 pT amlitude in 400 Hz bandwidth)
  <100 fT/ sensitivity is demanded for reliable detection
Flux strength scales as 1/R to 1/R3 as a function of the source-to-sensor distance
  10 pT amplitudes at a distance to muscle of about 15 mm
  Substantial variation observed in HD-sEMG and synthetized MMG over 5 mm along the muscle, good sensing point localisation needed
Compact sensors allowing for short (<10 mm) lateral field sampling pitch are needed
Unshielded or weakly shielded environment is anticipated by physicians
poster by S.Hartwig

## Slide 4: OPM in moderately optically dense vapor
Bandwidth expansion via laser power broadening
Degree of spin polarization is maintained/improved
Cramer-Rao phase noise limit is yet nonlinear
Pumping rate in optically dense medium
Experimental and
photon-shot-noise limited senitivities
Theoretical phase noise limited sensitivity

## Slide 5: OPM with miniature probe
≈ 300 fT/√Hz
Bandwidth ≈ 1000 Hz
Quadratic fit
Gradient robustness
Frequency response
Sensitivity
Test signal (≈ 60 averages)

## Slide 6: MyoQuant MMG OPM demonstrator
MyoQuant shield
Controller laptop
Lock-in amplifier
Waveform generator
Laser stabilization unit
Laser and optics box
Laser controller
OPM prototype
OPM mount
Power amp for heating
Decoupled arm rest

## Slide 7: Commercial vs MyoQuant OPM
Test signals applied (Rosenfalck functions, blue) to built-in coils of shield
Slow
Intermediate
Fast
QuSpin
SERF
OPM
MyoQuant
OPM
MyoQuant prototype: much higher fidelity in measuring intermediate and fast signals

## Slide 8: Proof-of-principle MMG in demonstrator
axial
azimuthal
radial
abductor
digiti minimi
muscle
(ADM)
electrical stimulation
Myomagnetic fields successfully measured in vivo with MyoQuant OPM prototype and shield!
≈ 60 averages
≈ 60 averages
≈ 100 averages
Sensitivity:
>0,3 pT/√Hz
at Tint = 70 °C,
Tsensor = 30 °C
Bandwidth:
1060 Hz
Stimulated ADM muscle,
60/100 Epochs
B (pT)
B (pT)
B (pT)
time (ms)
time (ms)
time (ms)

## Slide 9
Summary
Functional OPM prototype with 1000+ Hz 3 dB bandwidth und sub-pT/√Hz practical noise
OPM integrated in custom shield for the MMG measurement of the hand muscles
Demonstrated improved linearity in recording the phantom magnetic flux
First in vivo recording confirms the applicability and performance in practice
Outlook
further micro-integration of OPM
Systematic case studies with developed sensor
Transfer to medical partner for preclinical tests
High reliability towards space-borne platform
Outlook:

## Slide 10: Thanks!
Victor Lebedev
Simon Nordenström
Stefan Hartwig
Marlen Kruse
Thomas Middelmann
Peter Krüger
Philip Broser
Justus Marquetand
Nima Noury
Christoph Braun
Markus Siegel
Sascha Neinert
Kirti Vardhan
Marc Christ
Markus Krutzik