## Slide 1: B1 to Athos - recent progress and status
Improvements to feedbacks, ICTs, and gas detectors
Pavle Juranić, Gian Luca Orlandi, Florian Löhl, Philipp Dijkstal
PSI, 03.12.2024

## Slide 2: Motivation for Bunch 1 to Athos
There is no technical reason to have B1 to Aramis and B2 to Athos. In particular, the resonant kicker can be configured to act only on the first bunch without any difficulty.
Possible reasons for using the B1 to Athos mode:
  You can/want to have only 1 bunch in the machine, but it should go to Athos.
    Photocathode shaping project
    Horn cutting at maximized repetition rate
  You want to have more physical rf readings, but for the bunch that goes to Athos.
  Possibly: a mode with 200 pC in Athos and 10 pC in Aramis.

## Slide 3: Status before last MD week
We successfully used B1 to Athos for two photocathode shaping shifts, but for this project we never have a second bunch, the two lasers are always at the same repetition rate, and we do not use compression feedbacks.
Gian Luca had to manually change the ICT configuration, otherwise the MPS would turn off the machine after a certain time.
We noticed problems with the gas detector and the compression feedbacks. Although this was not critical for the photocathode shaping project, it prevented the B1 to Athos mode from being used for the EEHG, mode-locked FEL, and mode-coupled FEL projects and related efforts.
Minor problem for MDs: many display panels are incompatible with B1 to Athos.
Therefore, we scheduled a few hours of MD time for Florian to look at the feedbacks, for Gian Luca and Waldemar to look at the ICT, and for Pavle and Scott to look at the gas detector.
Summary:
Feedback issues were resolved. Many thanks to Florian.
ICT isuses were resolved. Many thanks to Gian Luca and Waldemar.
Gas detector issues were resolved apart from the more general problem of the timing signals.

## Slide 4: The Problem with the gas detector
Bunch switching confuses the gas detector
The gas detectors were coded to look at bunch 1 on Aramis, and bunch 2 on Athos. Various alarms and features depend on seeing a charge or frequency.
If you switch the bunches, Aramis is getting information from Athos and vice versa for this, causing possible issues.
Bunch 1 Freq and charge
Bunch 2 Freq and charge
Aramis Freq and charge
Athos Freq and charge
Normal mode:
Bunch 1 Freq and charge
Bunch 2 Freq and charge
Aramis Freq and charge
Athos Freq and charge
Bunch Switch mode:
Gas detector view:
Athos sees Athos freq and charge
Aramis sees Aramis freq and charge
Athos sees Aramis freq and charge
Athos sees Athos freq and charge

## Slide 5: The solution for gas detectors … or so we thought
We create PVs that can be looked at by devices that we put in the bunch 1 or bunch 2 properties in.
We tried it, and it looked OK! When the beam goes off, gas detector goes off on the right beamline.
However, an issue pops up when we have different rep rates in different beamlines.
Bunch 1 Freq and charge
Bunch 2 Freq and charge
Aramis Freq and charge
Athos Freq and charge
Athos sees Athos freq and charge
Aramis sees Aramis freq and charge
Bunch 1 Freq and charge
Bunch 2 Freq and charge
Aramis Freq and charge
Athos Freq and charge
Athos sees Athos freq and charge
Aramis sees Aramis freq and charge

## Slide 6: The solution for gas detectors … or so we thought
We create PVs that can be looked at by devices that we put in the bunch 1 or bunch 2 properties in.
We tried it, and it looked OK! When the beam goes off, gas detector goes off on the right beamline.
However, an issue pops up when we have different rep rates in different beamlines.
Bunch 1 Freq and charge
Bunch 2 Freq and charge
Aramis Freq and charge
Athos Freq and charge
Athos sees Athos freq and charge
Aramis sees Aramis freq and charge
Bunch 1 Freq and charge
Bunch 2 Freq and charge
Aramis Freq and charge
Athos Freq and charge
Athos sees Athos freq and charge
Aramis sees Aramis freq and charge
Many thanks to Didier Voulot for creating the PV’s, and Scott Stubbs for adapting the IOC’s. Thanks to Philipp Dijkstal for the bunch switching and overall coordination.

## Slide 7: Event triggers are hard-coded
All EVRs are looking at the events for their timing. Cameras, ADC, etc. The two events looked at are Generic B1 Follow (13) and Generic B2 Follow (52).
To change the EVRs, you need to change all of them one by one for the bunch switching. This is a pain.
So, if the rep rates are different, the fast signals get very confused at all diagnostics devices. You can make them work on a case-by-case basis.

## Slide 8: Conclusion and current status
B1 to Athos should be completely usable for the following scenarios
  There is no B2.
  B2 always has the same repetition rate as B1.
Otherwise there are problems with some of the diagnosics because they are hardcoded to certain triggers.
Many display panels are still broken -> Not yet suitable for standard / user operation.
Didier created new channels: SF-AR:Freq, SF-AR:Q, SF-AT:Freq, SF-AT:Q
Detailed wiki entry: https://acceleratorwiki.psi.ch/wiki/SwissFEL_Bunch_destination