## Slide 1
Status of the n2EDM experiment (2024)
Towards a new measurement of
the neutron Electric Dipole Moment
Thomas Lefort on behalf of the nEDM collaboration
Notes: Very low pressure to prevent Hg depolarization due to the presence of residual gases (H20 for instance)

## Slide 2
Storage chambers where neutron frequency measurement is performed
From the measurement of two frequencies (parallel and antiparallel fields configurations)
Two main challenges
neutron statistic & magnetic field uniformity and stability
→ Ramsey’s method: required polarized neutrons
The n2EDM experiment design

## Slide 3
UCN statistic: 10,000 per chamber (factor 6 below design goal)
Missing crucial subsystems:
- Magnetometry (Hg, Cs): still under development
- HV: bipolar power supply failed (no electric field) !
2023: short reminder
Switch box
Internal coils system
- First UCN in the fully assembled apparatus
- Neutron frequency measured (Ramsey’s method)
2024 goal: first nEDM measurement
Precession chambers in the vacuum tank
UCN detectors and spin analyzers

## Slide 4
2024 achievements: Hg co-magnetometer
Hg co-magnetomer operational over weeks:
T2 (TOP) = 50 s ; T2 (BOT) = 80 s
Performance still be improved but nearly at the design goal sensitivity (factor ~ 4 missing)
Operational for nEDM measurement (but sensitivity to improve)
Online monitoring of the magnetic field drift in the chambers: mandatory for nEDM measurement (R = fn/fHg)
Hg polarization chamber)

## Slide 5
Performance:
Stable (sparkless) operation at 150 kV (E= 12.5 kV/cm) : ready for data taking !
Up to 180 kV (design goal) but sparkling (conditioning procedure to improve)
2024 achievements: high voltage
Bipolar power supply replaced by two unipolar supplies (300 kV)
Full setup tested for the first time in 2024
Commissioning during 2025 shutdown
Electric field generation: mandatory for nEDM measurement
Polarity switcher needed: development started in 2024
Goal: remote control of polarity changes (switcher) ready before restart of data taking

## Slide 6
Two Cs units installed in 2024: steady operation over weeks
2024 achievements: Cs magnetometers
Cs magnetometry planning:
2025: half of Cs setup installed (56 cells) before data taking
2026: full Cs setup installed (112 cells)
One Cs unit (4 cells)
Online monitoring of field non uniformities (G30): systematic assessment

## Slide 7
Average magnetic field sampled by neutron, Hg and Cs over a run (~ 1 day):
- high stability observed by the three magnetometers
- neutron in agreement with Hg
- Cs offset due to incomplete array (under investigations)
First test-EDM run
Four systems (UCN + Hg + Cs + HV) simultaneously operating: → test-EDM run can be performed (~1 day)
Vertical gradient (GTB): < 0.6 pT/cm (within specifications)
- similar field in both chambers: common RF pulse can be applied

## Slide 8
Test of a new UCN storage chamber:
- new insulator rings (quartz instead of Rexolite)
- test electrodes: higher surface quality (polishing) + DLC
UCN statistic (2024)
Lot of efforts to improve our storage capability:
- Two culprits (2023): coatings of electrodes (DLC) & insulator ring (DPS)
New insulator ring (quartz)
Mirror polished test electrode
Test electrode DLC coated
Test chamber
Test chamber
UCN transport: + 40% with new UCN guides
Uncoated quartz ring + test electrodes + new guides
42,000 in the test chamber (x4 / 2023)

## Slide 9
UCN statistic in 2025-2026
Manufacturing of new electrodes: (improved) design done
- goal: ready for summer
Manufacturing (x2) in 2025
Uncoated quartz ring + new DLC coated electrodes
84,000 for two chambers (66 % of design goal)
Test chamber
Still room for improvements in 2025:
- Insulator ring: coating with deuterated paraffin (VF = 90 neV → 160 neV)
ongoing development (ready in 2025 ?)
- A few new UCN guides towards detectors
New UCN guides

## Slide 10
Main actions in 2025
Field mapping during winter: field reproducibility (offline corrections of systematic effects)
Implementation of the blinding procedure: directly in the DAQ system
Installation of half of the Cs array (56 cells): online assessment of higher order gradients
Improvements of the Hg co-magnetometer sensitivity: ongoing study
Substantial effort to get a magnetically clean environment:
Small pieces scanned with PSI gradiometer (cleaned or replaced)
Large pieces (i.e. electrodes): scanned at PTB (cleaned)
and many others tasks …
Mapping robot
Still a lot of work …. before restart of data taking
Gradiometer

## Slide 11
Current n2EDM sensitivity
Experiment sensitivity (dn)
Components | nEDM (2016) | n2EDM (2024) | Design goal
Precession time (T) | 180 s | 180 s | 180 s
Neutrons statistic (N) | 15,000 | 64,000 * | 120,000
High Voltage (E) | ± 11 KV/cm | ± 12.5 KV/cm | ± 15 KV/cm
Polarisation () | 0.75 | 0.82 - 0.85 | 0.80
Daily sensitivity () | 11. 10-26 ecm | 4.5 10-26 ecm | 2.6 10-26 ecm
Current sensitivity: improved by a factor 2.4 / nEDM experiment
~ 30 days required to reach previous experiment sensitivity
Room for improvement: UCN statistic (ring coating) + High Voltage (conditioning)
→ towards the design goal sensitivity
2025: first measurement in the 10-27 e cm range ?
Uncoated quartz rings
* Former electrodes

## Slide 12
Thank you

## Slide 13
n2EDM sensitivity
Current sensitivity (dn)
Components | nEDM (2016) | n2EDM (2024) | Design goal
Precession time (T) | 180 s | 180 s | 180 s
Neutrons statistic (N) | 15,000 | 60,000 | 120,000
High Voltage (E) | ± 11 KV/cm | ± 12.5 KV/cm | ± 15 KV/cm
Polarisation () | 0.75 | 0.82 - 0.85 | 0.80
Daily sensitivity () | 11. 10-26 ecm | 5. 10-26 ecm | 2.6 10-26 ecm
[1] “Generating a highly uniform magnetic field inside the magnetically shielded room of the n2EDM experiment” accepted in EPJC (2025)
Current sensitivity:
- improved by a factor 2 / nEDM experiment
- missing a factor 2 / design goal
Components | 2024 | Design goal
Hg Comagnetometer | T2 = 50 - 70 s | T2 = 100 s
Cs magnetometers | 8 cells | 112 cells
Magnetic field [1] |  | 
Components | 2024 | Design goal
Hg Comagnetometer | T2 = 50 - 70 s | T2 = 100 s
Cs magnetometers | 8 cells | 112 cells
Magnetic field [1] |  | 
Magnetometry:
Room for improvement: UCN statistic (ring coating) + High Voltage (conditioning)
With current sensitivity:
15 to 30 days required to reach previous experiment sensitivity

## Slide 14
The n2EDM experiment in the coming years
10-27 e cm
2027
2030
2025
2026
2028
2029
UCN
UCN
UCN
UCN
UCN
PSI shut
down
UCN Source repair (x1.3)
~ 5 10-27 e cm
n2EDM
n2EDMagic

## Slide 15
Measuring the energy spectrum of stored UCN
Super Conducting Magnet (SCM) scan:
UCN polarized up to a given energy Emax (a given SCM field strength)
- Polarized UCN: E < Emax ; unpolarized UCN: E > Emax
UCN polarization measured at the end of the storage period
- low polarization → high energy (unpolarized) UCN are stored
- large polarization → high energy (unpolarized) UCN are lost during storage
Emax is a measurement of the lowest Fermi potential in the chambers
UCN polarization
Magnetic field strength (T)
Magnetic field gradient scan:
Depolarization rate depends on:
- UCN energy spectrum & field non uniformities
Method:
apply different field gradients and measure UCN polarization
Depolarization give access to UCN energy spectrum
Results confirm that coating of electrodes and rings were not performant

## Slide 16
Magnetic field commissioning
Magnetic field characterization (2021-2022): close collaboration between LPC and LPSC
- internal coils system simulated, built and installed by LPC
- field characterization performed by LPSC
T. Bouillaud, P. Flaux, “An exceptionally uniform magnetic field for the n2EDM experiment” (LPC-LPSC); internal review.
Performances are excellent
Part of the systematics already below requirements