## Slide 1
Diamond Anvil Measurement of Muon-Catalyzed
Fusion Kinetics
The MuFusE Collaboration
PSI BVR 56 Progress Report
February 11, 2025
Ara Knaian

## Slide 2: Fusion is a safe, abundant source of clean energy
Introduction
Fusion of the deuterium in a stream of tap water could power a city.

## Slide 3: Plasma fusion requires stable 100,000,000 ⁰C plasma
Introduction
The deuterium-tritium fusion reaction has the highest cross section.
A cutaway view of the ITER tokamak, scheduled to burn DT in 2039.

## Slide 4: Muons can catalyze nuclear fusion reactions at lower temperature
Introduction
d
t
t
µ
µ
Muon comes into orbit
Muon forms chemical bond between Deuterium atom and Tritium atom
Nuclear fusion
µ
Muon Reactivation
µ
Energetic alpha
Energetic neutron
Muon Recycling
Negatively-charged muon enters
99%
Sometimes muon sticks to the alpha particle product of the fusion
1%
Squeezes nuclei together and fusion occurs

## Slide 5: Cost of electricity versus physics parameters
Motivation
Cost of baseload power
by source, $/kWh (1)
Coal $0.089
Biomass $0.077
Nuclear fission $0.071
Gas: $0.043
Target operating point:
Fusion (?): $0.025
(1) Levelized Costs of New Generation Resources in the Annual Energy Outlook 2023, US Energy Information Administration, Document #AEO2023
Target operating point for a reactor
Engineering breakeven
(Using a superconducting accelerator, Brayton cycle balance of plant, and revenue from heat sales.)

## Slide 6: Fusion rate increases with temperature and density
Background
Experimental Data from JINR measurements on DT
Ref: V.R. Bom et. al, JETP, 2005

## Slide 7: Sticking may decrease with density
Background
Ref: K. Nagamine, 2008
1000
200
500
250
100
H. Rafelski theory
170
330
Both experiment and theory predict that sticking decreases with density.
Data from four experimental groups is shown.
At high density, the measured sticking is uniformly lower (better) than predicted by theory
Density is stated as a fraction of liquid hydrogen atomic number density.
Sticking limit on the number of fusions per muon

## Slide 8: Goals of our collaboration:
MuFusE — Muon-Catalyzed Fusion Experiment
2.Create open-source physics process models for GEANT4
1. Measure DT cycling rate and sticking fraction at high density and temperature
Design range of our anvil cell target
Range measured historically

## Slide 9
Design overview
Optics System
Muon Beam
Neutron detectors
Diamonds
DT
Muon Beam
Diamond
Anvil
Cell

## Slide 10: End-to-end simulation: sticking fraction vs cell size

## Slide 12
Muon beamline
VAC-SEC
Tritium Monitor
Fume Hood
Elena and George
Digitizers
Liquid Helium
DT Glovebox
Detectors and target
𝜋E1.2 Beam
Area

## Slide 13
Muon beamline
Neutron detector array
Optical diagnostics

## Slide 14: Measured spectra and rates align with simulation
Detector and Simulation Performance
AmBe
Neutron Source
CF-252
Neutron Source
D-D Muon Catalyzed Fusion Neutrons
+14%
-9%

## Slide 15: Neutron detection between the muon and electron
Results
Liquid Deuterium
Liquid Hydrogen
Fusion

## Slide 16: Loading the tritium into the U-beds
Materials and Methods

## Slide 17: Loading the cell with liquid DT
Materials and Methods

## Slide 18: Compression of the liquid DT to a solid
Materials and Methods

## Slide 19: Optical pressure measurement via ruby fluorescence
Results

## Slide 20: Real-time gas analysis via Raman spectroscopy
Results

## Slide 21: Pressure and temperature reached
Results
Melting curve
Range previously measured
Oct 2024 run with 60/40 DT
Area we plan to map
Diamond anvil cell

## Slide 22: Hits classified as fusion neutrons peak at 46 MeV/c muon momentum, matching simulation
Results

## Slide 23: Time spectrum of hits classified as fusion neutrons
Results
60/40 solid DT, 50K, at 2.2 LHD
Empty target

## Slide 24: Snapshot of a typical DT fusion event
Results

## Slide 25: PRELIMINARY data on DT cycling rate to 2.2 LHD (2024)
Results
*Work is ongoing to characterize and correct for systematic errors and to properly size the error bars.

## Slide 26: 2025 Timeline and Beam Request
Planning
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Setup and onsite testing at PSI
Cell improvements and test compressions
Detector and DAQ improvements
Bakeout and gas analysis procedure improvements
Thanksgiving Nov 28
Data analysis
Beam

## Slide 27
Acknowledgements