## Slide 1: Recent MIDAS developments
MIDAS Workshop
Stefan Ritt
TRIUMF, Vancouver, CA, 22 September 2025

## Slide 2: Agenda
Improvements to odbxx API
mdev device driver concept
New equipment pages
Sequencer improvements
Alarm notifications
Custom page improvements (SVG, Mplot, Example Gallery)
One more thing

## Slide 3: odbxx API improvements
odbxx API used very successful since last workshop
New switch to access ODB from files or buffers: set_odb_source(STRING, “{ … }”); set_odb_source(FILE, “odb.json”);
  Suitable to read ODB dumps from .mid files, JSON or XML files
  User code does not need to be changed
  Only read operation allowed
Optimized transfer of large ODB trees server  XML tree  Network  frontend  midas::odb object
Implemented 64-bit values
Many small bug fixes

## Slide 4: Slow control architectures
Idea: we do not want one front-end program for each device
  Some experiments have 100s of devices
  Many devices can be logically grouped (like HV boxes)
A slow control architecture should give an easy way to write a FE without specific knowledge of the underlying communication

## Slide 5: Old Slow Control Architecture

## Slide 6: mdev front-end architecture
Generic “mdev” base class
  Links to ODB /Equipment/<name> tree
  Manages Event ID, readout period etc.
  Implement read_event() for periodic event generation
  Implement odb_setup(), init(), loop() and exit() functions (pure virtual)
  Simple front-end programming std::vector<mdev *> mdev_table; auto device = new mdev_xxx(”HV"); device->add_channels(adress1, type1, …); device->add_channels(adress2, type2, …); . . . mdev_table.push_back(device); mdev::mdev_odb_setup(mdev_table); mdev::mdev_init(mdev_table); install_frontend_loop([](){ mdev::mdev_loop(mdev_table)});
Driver derived from mdev
One object per device

## Slide 7: mdev_mscb usage

## Slide 8: mdev_mscb implementation (simplified)

## Slide 9: Advantages of mdev architecture
All midas “driver” functionality encapsulated in single object instead of class, device and bus drivers (object still needs to “talk” to device)
New features: conversion function, confirmation function
Any number of attributes per channel possible
Drawback: No multi-threading framework
User can call loop in own thread because ODB is now thread safe

## Slide 10: Old Equipment Pages

## Slide 11: New Equipment Pages
Allow write access: User can change values
Display: Defined which settings and variables to display
Names: Names of “channels”
Editable: Name(s) of editable values
Unit XXX: Unit to display
Grid display: Display several values in one row

## Slide 12: Sequencer Improvements
New sequencer commands
  BREAK to exit a loop
  ODBLOOKUP “/DIR/Names”, “CH02”, index  retrieve index for an array
  ATEXIT subroutine gets called when sequencer gets stopped (automatic or manually)
New UI (many thanks to Zaher Salman)
  Load/Save scripts from server ($MIDAS_DIR/userfiles/sequencer)
  Syntax highlighting
  Variable display
  Tabs for multiple files
  “Batch queue”

## Slide 13: Sequencer limitations
MIDAS Scripting Language (MSL) is easy to learn, but limited
“Can we fit a I-V curve and save the result?”
PySequencer (many thanks to Ben Smith)
  Same GUI and functionality as MSL
  Full Python language including numpy, …
  See detailed talk later by Ben
  Already heavily used

## Slide 14: PySeqeuncer Vision
Run Sequencer
Detector optimizations e.g. (I-V) curves
IDE to develop stand-along Python programs
Slow Control (replace Labview)
Beamline Scans

## Slide 15: Alarm Improvements
Some slow control channels have “spikes”
Annoying when they trigger an alarm
Usually only 1-2 values above threshold
New setting “Trigger count required” fires trigger only after N consecutive alarm conditions
Alarm condition will be replaced by TinyExpr++ condition (planned, requires C++17): o(“/Equipment/TC/Variables/Curr[0]”)*1000 > 100 && o(“/Runinfo/State”) == 3 on(”/Equipment/TC/Variables/Curr”, “CH3”) > 100

## Slide 16: Alarm Notifications
In case an alarm happens, shift crew needs to be notified quickly
You don’t want to get notified when you’re not at the lab
Email not suitable
Shell scripts for Telegram, Mattermost, Slack
Channels can be muted 😉
https://daq00.triumf.ca/MidasWiki/index.php/Alarm_System

## Slide 17: Custom Pages

## Slide 18: mplot library
History plots are only value over time, but what about X/Y and X/Y/Z (color plots)
mplot JavaScript library https://daq00.triumf.ca/MidasWiki/index.php/Custom_plots_with_mplot
<div class="mplot" style="height: 360px;width: 700px;"
data-odb-path="/Path/To/Data"
data-x="X" data-y="Y">
</div>
Fully interactive
  Zoom and pan
  Inspect individual values
  PNG / CSV download

## Slide 19: mplot examples
Help  plot_example.html
TBD:
error bars (X & Y)
time X-axis
category X-axis

## Slide 20: mplot fit similar to JSRoot  TBD

## Slide 21: SVG graphics
Use free Inkscape to produce complicated schematics

## Slide 22: SVG graphics manipulation
<button onclick="change()"> Change color </button><br />
<object id="svgObject" type="image/svg+xml" data="valve.svg" />
<script> function change() { doc = document.getElementById('svgObject').contentDocument; const obj = doc.getElementById('Valve_1'); obj.style.fill = "#FF0000"; }
</script>

## Slide 23: Custom Page Gallery
SVG
modbthermo
modbgauge
modbhbar
modbbox
modbbutton

## Slide 24: Custom Page Gallery

## Slide 25: Custom Page Gallery
Style Guide?

## Slide 26: Custom Page Gallery
Style Guide?

## Slide 27: Custom Page Gallery
Noise Scan

## Slide 28: Custom Page Gallery
mplot data-h
mplot data-z (colormap)

## Slide 29: Custom Page Gallery
Bad example!

## Slide 30: Custom Page Gallery
<canvas> +
mjsonrpc_db_get_values()

## Slide 31: Custom Page Gallery

## Slide 34: MidasGPT
Standard ChatGPT “knows” midas since it was trained with the public documentation
New midas features are usually not in training set
GPTs allow “special” versions of ChatGPT having PDF files in its context
MidasGPT contains PDF dumps of midas Wiki  https://chatgpt.com/g/g-68b1cce155a48191bb5df1b2919bdaf4-midasgpt

## Slide 36: Links back to Midas Wiki

## Slide 37: Python Sequencer Documentation upload sequencer.py and ask for API docs

## Slide 38: Example MidasGPT generated PySequencer script

## Slide 39: Two more things: What’s new?

## Slide 40: Two more things : What’s new?