## Slide 1: The AMORE Detector
An aircraft and balloon-borne particle telescope for secondary cosmic-ray measurements
Justin Dante Tabbett, Gabriele Auriemma
Paul Scherrer Institut, LTP(izza)hD, 17 September 2025

## Slide 2
space WEATHER
“Space weather” refers to conditions on the Sun and in the solar wind, magnetosphere, ionosphere, and thermosphere that can influence the performance and reliability of space-borne and ground-based technological systems and can endanger human life or health.

## Slide 3: Space Weather: An Introduction
Effects of solar activity
Microelectronics radiation damage (e.g. SEE, TID)
Telecommunications disturbances
Global Navigation Satellite Systems (GNSS) failure
Induced currents (geomagnetic and geoelectric)
High radiation exposure for aircrews and passengers
Positive aspects: Aurora Borealis

## Slide 4: Space Weather: Monitoring
Ground-based Monitoring System
Solar Telescopes
Magmetometers (The geomagnetic Kp Index)
Radio Spectrograph (eCALLISTO)
GNSS Networks
Ionosphere Monitoring
Cosmic Rays Neutron Monitors
Space-Based Monitoring Systems
Solar and Heliosperic Observatory (SOHO)
The Vigil Mission (ESA)
DSCOVR (NASA)
Satellites Payloads (including SmallSats and CubeSats)
Mini neutron monitors
eCALLISTO
SOHO space craft
1U CubeSat

## Slide 5: Space Weather: Monitoring
Ground-based Monitoring System
Solar Telescopes
Magmetometers (The geomagnetic Kp Index)
Radio Spectrograph (eCALLISTO)
GNSS Networks
Ionosphere Monitoring
Cosmic Rays Neutron Monitors
Space-Based Monitoring Systems
Measurements of Solar Wind (Flux, Density)
Photospheric Magnetographic Imagers
Heliospheric Imagers
Plasma Analysers
Radiation Monitors, Particle Telescopes
Radiation Monitoring
Low Earth Orbit
Lagrange Points
Geostationary Orbits
400 km up to 1.5 Ml Km
Mountains Summit
Sea Level
3-4 km down to sea level
Something’s missing

## Slide 6: The Atmospheric Region
Previous Studies
Readapted from Cosmic Rays at Earth
Researcher's Reference Manual and Data Book(2001)
~30 km (Stratosphere)
Mainly simplified instrumentation (Gamma-Ray Detectors)
~10 km (Troposhere)
Mainly Dosimetric Studies (Aircrew exposure)
Gaps of Knowledge:
Energy spectrum
Particle composition
Direction of particles

## Slide 7: The AMORE Instrument
The Airspace Measurements Of Radiation Environment Instrument
Particle Telescope ΔE-E-ΔE
Planar BC-400 Scintillator surrounding Cubic NaI(Tl)
AMORE Features
Energy range up to 100s of MeV
Sensitive to neutral and charged particles
Directional sensitivity - 4π FOV
Low mass, size & power consumption
Final design illustration

## Slide 8
building AMORE

## Slide 9: AMORE ΔE (dE) Detector
First version – Luka Marjanovic’s Master’s Thesis
52x52x2 mm3 BC-400 plastic scintillator
8x SiPM 1.3x1.3 mm2 optical readout
  4 channels of 2 SiPMs
Investigating
Light output with different wrappings (paper, Aluminium, Vikuiti, none)
Position sensitivity
1.3x1.3 mm2
Single channel

## Slide 10: AMORE ΔE (dE) Detector
Current version
52x52x2 mm3 BC-400 plastic scintillator
16x SiPM 1.3x1.3 mm2 optical readout
  Single channel
Changes made for the Demonstration Model (DM)
Simplify the design  Future version will combine both iterations
10x10 cm2
dE scint.
1x SiPM

## Slide 11: AMORE E Detector
Current version
50x50x50 mm3 BC-400 plastic scintillator
8x SiPM 3x3 mm2 optical readout
  2 channels of 4 SiPMs
  One channel at top of E volume
  One channel at bottom of E volume
dE scint.
E scint.
SiPMs

## Slide 12: AMORE Demo Model: Full Assembly
Detector Head
Top Case
Head + WaveDream,

## Slide 13: Data Acquisition System
WaveDREAM Board (WDB)
DRS4 based readout module
Developed for the MEG II Experiment
For our use
HV supply to SiPMs
Variable gain multiplication
Temperature corrections
Waveform measurements
Credit: Stefan Ritt, PSI
Channel inputs
Power socket
Ethernet

## Slide 14: Proton Measurements
Beam Setup :
Low flux: 3E3 p/cm2/s
5x5 mm square collimator
Energy Scans: 200, 150, 100, 70, 50, 30 MeV
Tests:
X,Y scans
Angle scans: -90° to 90°
Background
0°
90°
X,Y Table

## Slide 15: Proton Spectra
Example of Energy scan
Perpendicular and centered beam
Fixed Acquisition Parameters (Gain, HV, Trigger threshold, Trigger patterns)
OR Trigger Logic

## Slide 16
flying AMORE

## Slide 17: Primary Objectives for Commercial Aircraft Flights
Determine in-situ AMORE performance
Aircraft vibrations
Environmental effects
Operational aspects
Use flight measurements to iterate upon AMORE performance
Tuning & optimisation
Preparation for autonomous operation
Radiation Response
Initial Performance
Instrument Tuning
Measure secondary cosmic radiation onboard
Study instrument characteristics in-situ
Initial observations of particles and rates
Measurements as a function of altitude and latitude

## Slide 18: AMORE Operation
Equipment setup
Laptop charger connected to power socket
AMORE detector connected to power socket
Two cables between AMORE detector and laptop
  USB and ethernet
Laptop
Power socket
Power socket
Ethernet cable
USB cable
<22 W power
Cable < 1 m length
100 W power
Cable ~1.5 m length
AMORE Detector unit

## Slide 19: SWISS
Hopefully flying in the next couple of months!
Boeing 777
Airbus A330

## Slide 20: Balloon Flights
Dramatic difference in the radiation environment from 0 km  10 km  33 km
For higher than 10 km we need to use balloons
WDB is incompatible with balloon environment
It’s cold!
Ice formation on electronics due to air cooling
WDB is heavy
“High” power consumption
New front-end electronics being developed
Temperature-altitude profile for balloon flight
Charged particle concentration-altitude profile.
Adapted Y. I. Stozhkov, 2003.

## Slide 21: Balloon Schematic
Equipment setup
xyz
Batteries
USB cable for Sensor board
Amplifiers
AMORE Detector unit
DRS4 Eval. Board
Power distributor
Balloon
Max weight 1.2 kg

## Slide 22: Balloon Flights
Partnered with AGH University of Science and Technology, Kraków, Poland
Infrastructure to launch & recover payloads
Filling balloon with helium. Credit: AGH
Balloons from Sunday 10:30 pm to Monday 10:30 am. Credit SondeHub

## Slide 23: Summary
Developing a ΔE-E-ΔE particle telescope
Demonstration Model is assembled and undergoing calibrations
Flights on commercial airplanes are planned for the coming months
Balloon flights within the next year
Characterising the airspace radiation environment
Acknowledgments
Wojtek Hajdas – AMORE lead
Michael Müller – AMORE electronics
Mike Gantert – AMORE Technician
Malte Hildebrandt – Detector Group lead
Thank you for listening
Are there any questions?

## Slide 24: Additional Slides

## Slide 25: The Solar Activity
Sunspots
Images from NASA’s Solar Dynamics Observatory highlight
Associated Events:
Solar flares
Coronal mass ejections (CMEs)
Solar particle events
The solar wind
https://www.swpc.noaa.gov/products/solar-cycle-progression