## Slide 1: WLHA Electron Source Test Facility
Activities 2026 onwards
Thomas Lucas with input from Cezary and Carlo
Ort, TT. Monat JJJJ

## Slide 2: Work packages, milestones and deliverables
Injector linacs and sources
Coordination (WP0)
Collaborations
FCC-ee project
WP1
Electron and positron linacs
WP2
Electron source
WP3
Positron source and linac
WP4
Damping ring and transfer lines
WP5
Towards TDR
D1.1: Industrialization
processfor RF structues
M1.2, M1.3: RF prototypes
M1.1: working frequency
M1.4: High power test, BDR
D2: demostration charge
modulation up to 5 nC
M2.1: Concept for
electron source
e-, p- and HE-linac
D3.1: TD and integration
target and capture system
M3.1: working frequency
D3.2: P-cubed project:
positron production @SF
D4.1: Physics design
Damping ring and TLs
D5.1
Unified Global Requirement
D5.2
Physics Requirements Docs
Eng. specifications docs
TDR chapers
Involvement of technical groups from CERN and PSI
not in the CHART proposal
Functional Specifications Documents
Specifications
for CE and TI

## Slide 3: 2026-2028: Electron Source Test Facility (CHART and EPITA)
C-band
Modulator
(TW Gun or Acc 1)
S-band
Modulator for
Electron Source
Storage and
loading Area
Photocathode Laser
Water
Water
Water
Test Place
With RF Load
Chillers
Laser
Development
Area
EPITA Test Place
Water

## Slide 4: 2026-2028: Electron Source Test Facility (CHART and EPITA)
C-band
Modulator
(TW Gun or Acc 1)
S-band
Modulator for
Electron Source
Storage and
loading Area
Photocathode Laser
Water
Water
Water
Test Place
With RF Load
Chillers
Laser
Development
Area
EPITA Test Place
Water
We will build a replica of the SwissFEL electron gun.
C-band test stand to continue to run.

## Slide 5: 2026-2028: Electron Source Test Facility (CHART and EPITA)
C-band
Modulator
(TW Gun or Acc 1)
S-band
Modulator for
Electron Source
Storage and
loading Area
Photocathode Laser
Water
Water
Water
Test Place
With RF Load
Chillers
Laser
Development
Area
EPITA Test Place
Water
Photocathode Laser for S-band Gun must be synchronised to the S-band RF System.
We would like to have at least a C-band source synchronised to the S-band too. X-band would be a luxury

## Slide 6: First Concept
Synchronisation Box
Laser oscillator
Frequency comb
Fr=142.8 MHz
2.998 GHz
5.712 GHz
Switch
Switch
142.8 MHz
Feedback
Separate Oscillator
Separate Oscillator
2.9988 GHz
5.712 GHz
To Amplifier
Reference to fix drift

## Slide 7
Fcc-ee photocathode laser layout
Oscillator
@142.8 MHz
Compressor 1
Main Output
T=600 fs FWHM
E=2.5mJ @ 1040 nm
Synch Unit
Reference
Pulse Picker
Compressor 2
Aux. Output
T=600 fs FWHM
E=2.2mJ @ 1040 nm
Short Probe Output
T=600 fs FWHM
E=0.3mJ @ 1040 nm
Compressor 3
Rejected Pulse @142.8 MHz DIAGNOSTICS+FEEDBACK
Trigger single shot – 100 Hz Timing System
Laser
Amplifier
To be discussed

## Slide 8
Fcc-ee photocathode laser layout
Menhir Photonics
RR=142,8 MHz
@1040 nm
CPA amplifier
Amplitude
@ 1040 nm
RR=100 Hz
Compressor 1
Main high
energy
output
Main Output
T=600 fs FWHM
E=2.5mJ @ 1040 nm
Synch Unit
PSI Reference Clock
Pulse Picker
Optical
Switch
Compressor 2
Auxiliary high
energy output
Aux. Output
T=600 fs FWHM
E=2.2mJ @ 1040 nm
Short Probe Output
T=600 fs FWHM
E=0.3mJ @ 1040 nm
Compressor 3
Short probe
output
Rejected Pulse train @142.8 MHz
T= sub-200 fs FWHM
P=60 mW @ 1040 nm
Trigger single shot – 100 Hz Timing System

## Slide 9: Laser oscillator
Low noise femtosecond oscillator
Specification
  Wavelength 1040 nm
  Pulse duration 200 fs
  Power 150 mW
  Rep rate 140.8 MHz
  Piezos tuning range
    Fine 150 Hz
    Coarse 3 kHz (worse case scenario)
    SwissFEL has very good temperature
    and humidity stability.
Free running noise
RF spectrum

## Slide 11: T&S
Function | Name | Estimated cost | Comment
2.9988GHz reference | Rohde&Schwarz SMA100B | 36kCHF | Same for SwissFEL and SLS2: easy spare situation
Laser oscillator | Menhir 143 | 70kCHF | Frequency comb generation
Harmonic extraction | Custom build | 10kCHF | An improved version is in progress, the old one could be used for “free”
Laserlock | Custom build “SOM-DLL” | 10kCHF | Should be finished soon, for the above laser oscillator and harmonic extraction
RF distribution | LiberaSync | 40kEu-65kEU | Cost is for TX&RX combination and depends on ordering numbers
142.8MHz distribution | Custum build by Sintec | 20kEU | For one transmitter and one receiver
Function | Name | Estimated cost | Comment
8GHz reference | Rohde&Schwarz SMA100B | 36kCHF | This source is EVERYWHERE now
Laserlock | Custom build “SOM-DLL” | 10kCHF | For the gun laser
Function | Name | Estimated cost | Comment
2.9988GHz reference | Rohde&Schwarz SMA100B | 36kCHF | PSI “Standard” RF source now
Laserlock | Custom build “SOM-DLL” | 10kCHF | For the gun laser
(2.9988GHz-2.9988GHz/21)*2 | Frequency conversion (to be build!) | 10kCHF | Cost: wild guess / upper limit!

## Slide 12: Notes
IMPACT shutdown is start 2027.
Optical Master Oscillator is the laser.
Separation is the interface of the 2.998 GHz cable to the LLRF.
Require 15 dBm for all frequencies.
Responsiblilites
  Carlo: Laser (OMO)
  Cezary: photodiode, frequency generator 142 MHz, 2998 MHz, 5712 MHz and amplifcation to >20 dBm (after cable)
  Mark: S-band and C-band LLRF for S-band and C-band modulators.
  Tom to contact Romain Vallotton