## Slide 1
Development of a Synthetic Database for CORC® Cables
MAG-S.01.01-T030-D002
Fabio Freschi
Laura Savoldi
Department of Energy – Politecnico di Torino

## Slide 2
Why a synthetic database?
Design-space is large: geometry, tape count/layers, material law parameters, , external (magnitude + orientation).
CORC® physics is coupled: self-field + anisotropic → non-uniform current sharing.
Need fast “engineering outputs” for magnet design loops → train metamodels (ANN/surrogates).
What is stored per case?
Raw samples around the transition (few points).
Identified pair from log-domain regression.
Tape-wise / segment-wise current distribution (optional feature targets).
Full metadata: geometry inputs, model + parameters, description, temperature, random seed, convergence + fit diagnostics.
ML-ready outputs (what the metamodel predicts)
→ A metamodel is only as good as the dataset: Inputs must encode the same physics used by the solver: geometry, material law, and operating field.
→ trained surrogate enables rapid scans / optimization loops with uncertainty bands
Motivation & End-Product
curve features
Current sharing metrics
Notes: [Sources] - Project deliverable: MAG-S.01.01-T030-D002 v1.0 (docx), Executive Summary + Sec. 13. [/Sources]

## Slide 3
STAR2d (2‑D DC, cross-section)
Unknowns: segment currents + one shared cable voltage.
Self-field via Biot–Savart (no air mesh).
Best for: fast parameter sweeps, sensitivity studies, dataset scale-out.
STAR3d (3‑D stream-function on tape surfaces)
Captures axial/helical effects (pitch), terminations, non-uniform field along axis.
More expensive; used selectively as high-fidelity anchors.
Voltage inferred from power loss; includes automatic outlier rejection in fit.
Simulation engines used to generate the synthetic database
4 layers – 3 tapes per layer
Notes: [Sources] - Project deliverable: MAG-S.01.01-T030-D002 v1.0 (docx), Sec. 9 Results (COMSOL benchmark) and timing statement. [/Sources]

## Slide 4: Step 1 — Geometry parameterization and discretization (STAR2d)
Geometry pre-processor inputs
Tape width w, SC thickness (SC-only in DC model).
No. layers, No. tapes per layer, layer-to-layer spacing.
Inner/core radius (first layer).
Target segment size → discretization density.
Feasibility check: first-layer circumference must fit tapes
Case instantiation
Geometry params
→ fast re-use across current sweeps and parameter scans
Discretize tapes
Cache Biot-Savart kernels
Attach material law

## Slide 5: Step 2 — Material law and nonlinear solution
Numerical robustness
Continuation: reuse previous current-point solution as initial guess
Mesh adaptivity: refine until ΔV between refinements < 5% (fixed per geometry)
Cache geometry kernels (fixed layout) → cheap iterations
→ stable E–I samples over many decades of E (critical for log-fit)
Constitutive relation (per segment)
Power-law with criterion and exponent .
Nonlinear resistivity derived from the power-law.
model options: critical-state, isotropic Kim, anisotropic Kim-like, magneto-angular fits.
Nonlinear system solved
Unknowns: segment currents + cable voltage V.
Constraints: and voltage equalization .
Self-field update: Biot–Savart superposition each iteration.
Solver: MATLAB fsolve (trust-region) with variable scaling.

## Slide 6: Step 3 — Identify from a small sample set
Why log-domain fitting?
spans many decades: log-fit treats multiplicative error uniformly.
Prevents high‑ points from biasing the regression upward.
Window kept tight around so slow variation does not introduce curvature.
Database implication: few solves → reliable labels → massive coverage
Key choices for a scalable database
Use few current points near transition.
Guarantee bracket around before fitting.
Fit in log-domain to avoid dominance of high‑ points.
Identification algorithm
Provisional
Solve at currents around (continuation)
Check bracket:
Log–log linear regression near crossing
Return: (slope), from

## Slide 7: Cross-check vs COMSOL
Local J profile across tape width matches closely
and behavior consistent near transition
Faster solution time
Chart: 
| STAR2d | COMSOL
Time per solve (s) | 0.1 | 4.5
seconds
COMSOL
formulation.
Discretization of tapes and surrounding air.
Each tape is discretized with 71 elements, whereas the surrounding air is discretized with 5556 triangular elements for a total of 11305 degrees of freedom.

## Slide 8: 3-D extension: STAR3d
STAR3d
Representation of a thin-surface
No air mesh
Nodal-based unknowns
The calculation kernels for B are cached
Connections (inlet/outlet sections) effect
Computational expensive but necessary: “true results”
STAR2d:

## Slide 9: 2-D/3-D interaction and development of the database
Role of 2-D simulations
Essential environment for physics and numerics exploration
Intermediate training database (parameter sensitivity, extrapolation
2-D/3-D combination through ML-based correction model
Define configuration space
Geometry + materials + T + operating conditions
Generate candidate set X2
Large: 103-106
Run STAR2d on X2
Compute fields + Solve + E-I
Label extraction
Ic, n, QC metrics, E-I curve
QC
pass
Select 3-D anchor set X3
DoE + active learning
Run STAR3d on X3
Expensive Hi-Fi solution
Label extraction
Ic, n, QC metrics, E-I curve
QC
pass
D2: 2-D DB
Dense, Lo-Fi
D3: 3-D DB
Sparse, Hi-Fi
Build mapping correction model
Augmented multi-fidelity DB
D = {D2, D3, mapping}
Train ML metamodels
No
Adjust numerics
No
Adjust numerics
Yes
Yes

## Slide 10
Takeaways
Development of Synthetic Database
Physics‑consistent features (geometry + + material law) → metamodels that generalize configurations and operating conditions.
Robust label extraction: store raw + fitted + residuals.
Scale via Star2d; control bias via Star3d anchors (multi‑fidelity, residual correction).
Database records include provenance + QC flags → training is repeatable and defensible.