## Slide 1: PSI General Beam Profile Monitor
Kick-off Meeting Jan 30th, 2026
Stefan Ritt
Muon Physics Group, LTP

## Slide 2: Idea of this meeting
Collect requirements for a general-purpose beam profile monitor
Review existing solutions
Discussion about a path forward

## Slide 3: General Requirements
Beam profile X/Y
  Position
  Width
  Phase space
Beam intensity
  Hz to GHz (HIMB)
Particle ID
  ToF on ~ns level to distinguish e, m, p, (p)
  dE/dx

## Slide 4: Consolidation of existing solutions
Many beam profile monitor exists: “Pill”-based scanners, Scintillator-based, Pixel-based, GEM-based, …  will review them today
Each solution has its own hardware / software / documentation (?) and typically needs an expert to install and run it  waste of work-power
What about consolidating solutions for an easy-to-use, general-purpose device?
Detector A
Detector B
DAQ
“Black box”

## Slide 5: My Vision: Software
MIDAS for detector readout
  Established PSI system (MSetPoint)
  Modern web interface
  Sequencer (Optima, …)
Software should come pre-installed on the beam profile monitor
User Interface should be independent of actual detector  quick learning
How to achieve that?

## Slide 6: My Vision: Hardware
Avoid Windows & Labview
Cheap & Compact
Detector readout & Slow Control (HV, Temperature, …)
Proposal: RevolutionPi

## Slide 7: RevolutionPi https://revolutionpi.com (KUNBUS, Denkendorf, Germany)
Raspberry Pi based extendable control units
Digital, Analog (+-10V, 4-20mA, PT1000), Relais expansion units (up to 80 IOs), USB, Ethernet
Standard Linux with Real Time extension (cycle time <10 ms) “Soft Real Time”
Can run MIDAS natively, can read out WaveDREAM boards
Open-Source philosophy (schematics can be downloaded, software under github)
KUNBUS founded in 2008, 1 million devices produced, including nuclear power plants

## Slide 8: RevolutionPi Devicec
Mixed Analog / Digital IO
  0…10V In/Out
  Digital In/Out
  PWM / Frequency In/Out
Analog IO
  +-10V, +-5V, 0…20mA, PT1000
Relais 4x
Gateway
  Profinet
  EtherCAT
  Profibus
  CAN
  M-Bus
~200 CHF/device

## Slide 9: Test Setup
24V
AOUT  AIN
Controller
I/O

## Slide 10: Web access

## Slide 11: Node-RED https://nodered.org

## Slide 12: Graphical Output

## Slide 13: More complicated controls

## Slide 14: More complicated UI

## Slide 15: mdev front-end architecture
Generic “mdev” base class
  Links to ODB /Equipment/<name> tree
  Manages Event ID, readout period etc.
  Implement read_event() for periodic event generation
  Implement odb_setup(), init(), loop() and exit() functions (pure virtual)
  Simple front-end programming std::vector<mdev *> mdev_table; auto device = new mdev_xxx(”HV"); device->add_channels(adress1, type1, …); device->add_channels(adress2, type2, …); . . . mdev_table.push_back(device); mdev::mdev_odb_setup(mdev_table); mdev::mdev_init(mdev_table); install_frontend_loop([](){ mdev::mdev_loop(mdev_table)});
Driver derived from mdev
One object per device

## Slide 16: mdev_revpi MIDAS device driver
Stand-alone
MIDAS running
on RevPi
WaveDREAM readout via Ethernet
Slow Control:

## Slide 17: My vision: Detector integration through common data format
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
MIDAS event
. . .
N: Number of particles
X,Y,Z: Position in m
T: Time in s
dE/E: Energy in MeV/c2
Detector A
MIDAS
DRIVER
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
MIDAS event
. . .
UI

## Slide 18: Mapping of different detectors
Pixel
  N = 1
  X/Y = Pixel X/Y + offset
  Z = position(s)
Scanner
  N = count rate
  T = unused
  X/Y = motor
  Z = position
Sandwich
  X/Y = Pixel X/Y + offset
  T = scintillator time
  dE/E = scintillator light
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
MIDAS event
. . .

## Slide 19: Data presentation / analysis
Profile plots
  X/Y
  Cut on Particle ID
Phase Space / Divergence
  X1-X2 / X
  X1-X2 / Y1-Y2
Beam rate
  SN / normalization
Particle ID
  T: ToF
  dE/E: Energy loss
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
N
X
Y
Z
T
dE
E
MIDAS event
. . .

## Slide 20: Conclusions
Combining our efforts will benefit our community and safe double work
A general tool is only useful if easy-to-use and well documented
I’m happy to bring in my experience with MIDAS and various hardware, but rely on others for the detector parts