## Slide 1: MEG Upgrade Programme Beam & Target Considerations

## Slide 2: Current MEG Beam Line & Target
Main Characteristics:
High intensity, high transmission optics for surface muons (28 MeV/c)  maximize µ+ at target
Small emittance  minimize target size
Adustable momentum-byte < 10%  monochromatic beam with high stopping-density
Ultra-thin slanted target + minimization of material in beam (vacuum, He-environment)  minimize multipe
scattering for µ+ & Michels + minimize photon production AIF or Bremsstrahlung
Minimization & separation of beam-correlated backgrounds  e.g. e+ from 0-decay at Target E or µ+ decay-in-flight

## Slide 3: Main Components
Wien Filter+Triplett I & II
Hor. + Vert.
Correction Magnets
End-Caps
+ IS
DS
US
Degrader
System
Collimator
System
SC
BTS
Steering
Magnet
Target
Systems

## Slide 4: Beam Line Performance
Horizontal Profile
Vertical Profile
2-D Beam-spot
Separtor Scan
μ+ Momentum Spectrum
8.1σμ Separation ≈ 12 cm physical separation
at collimator
(Δp/p)MAX ~7% FWHM
(Rμ )MAX > 1⋅108 μ+s-1 at 2mA
COBRA Centre (no Degrader)
σX,Y ~ 9-10 mm

## Slide 5: MEG Beam & Target Upgrade Strategy & Possibilities
Currently MEG runs at :
~ 3⋅107 μ+-stops/s on a 205μm thick target placed at 20º to incoming beam with
a 300μm thick Mylar degrader - selected for optimal sensitivity with current detector capabilities
MEG Upgrade Sensitivity Reach: aims at approximately an order-of-magnitude improvement.
In order to achieve this with improved detector capabilities and within a reasonable running time
of 3 years - this requires a baseline detector rate capability of about 7·107µ+-stops/s
Q: What beam possibilities exist to fully exploit the upgraded detector
intensity reach & try to increase the muon stopping density?

## Slide 6: Constraints & Coinsiderations
Increase intensity: - simply open slits since we have spare intensity 
 increases Δp 
 increases range-straggling 
 need thicker target to stop all muons 
 increases multiple scattering & radiative background 
t90
t
r =<R>
r =<R>


t = target thickness
t90 = measure of e+ Multi. Scatt.
<R> = mean range of µ+
 = target angle to axis
 = angle between axis & radius r which
meets DS target face
r = <R> “umbral” region 50% stops contour
r = (<R>+ 3R) “penumbral”
region 100% stops contour
+
Target angle Considerations ( & )
if 3(rms)MS >  “Leakage”
on US face
if 3(rms)MS >  “Leakage”
on DS face
So can one increase the intensity & reduce the Range Straggling?

## Slide 7: Beam Strategies – a Quick Guide
Surface or Sub-surface Muons?
Basis – muon momentum spectrum
stopped π-decay kinematic edge 29.79 MeV/c
“Surface” muons come from a layer few hundred microns below
surface range approx. 120 mg/cm2
“Sub-surface” muons from layer shifted below the surface
Why are Sub-surface muons interesting?  Muon Range & Range straggling
Muon Range Straggling in our 30 MeV/c region– 2 components
(i) Dependent on energy-loss straggling = constant ≈ 9% of the range
(ii) Dependent on momentum-byte of channel
Muon momentum Spectrum
measured PiE5
R = a⋅P 3.5
To reduce Range-straggling more efficient to Reduce P than Reduce ΔP/P ➪ Sub-surface Beam
BUT!!! Remember Rate reduces as P3.5 towards lower momenta  Compromise
Also expect µ-e separation from Wien-filter to be improved by about 25% ➪ greater velocity difference
dn/dp ∝ P 3.5

## Slide 8: Possible Strategies
“SURFACE” Muon Beam 27.9 MeV/c
“SUB-SURFACE” Muon Beam 25 MeV/c
ACTIVE Target 250μm
Passive Thin Target 100-205 μm
Simplest Baseline configurations:
Surface muon beam “High Intensity” MEG Target
“Sub-surface” Muon Beam “High Intensity” MEG Target
Different slant-angle & target thickness configurations
Upgrade possibilities Studied:
Active Target – if dominated by multiple scattering then depending on tracking performance
extra vertex should help improve e+-resolutions But background Must be studied in detail
Thin Passive Target – multiple scattering reduced & radiative-related background reduced BUT
need REDUCED Range Straggling ➪ otherwise DS background! ➪ Sub-surface Beam

## Slide 9: 25 MeV/c Sub-surface Beam already Studied for MEG
Horizontal Profile
Vertical Profile
Measurements made at:
Collimator System
COBRA Centre
High-intensity (slits “Open”)
No Degrader
Only “High-intensity” Possible if one wants the RATE for MEG II

## Slide 10: High-Rate Measurements (µ+ reaching Target)
Collimator: - High rate Surface muons 27.9 MeV/c
1.23108 Hz at 1.8mA Log11/173-173
1.22108 Hz at 1.8mA Log12/111-113
1.22108 Hz at 1.8mA Log13/36-37
<Rµ> = 1.5108 Hz at 2.2 mA
COBRA Centre: - High rate Surface muons 27.9 MeV/c
Deg 420 µm CH2 5.7107 Hz at 1.8mA Log12/81-86
Deg 335 µm Mylar 8.6107 Hz at 1.8mA Log13/101-113
Deg 300 µm Mylar 9.1107 Hz at 1.8mA Log13/107
Deg 0 µm 1.3108 Hz at 1.8mA Log13/74-75
Deg 300 µm Mylar 8.4107 Hz at 2mA Log14/105
Deg 200 µm Mylar 1.08108 Hz at 2mA Log15/117
Range straggling:
High Rate - 300 µm Deg R =130 µm in l 46 µm in t measured
Normal Rate 300 µm Deg R =80 µm in l 28 µm in t measured MC gets 27µm in t
Rµ = 1.1108 Hz at 2.2 mA
Rµ = (10.1)108 Hz at 2.2 mA

## Slide 11: MC Study of Various Beam-Target Combinations
Running Time normalized to Baseline
MEG soln.
Stopping Quality Factor (SQF) –
measure of the ratio of Target-stops
to Stops elsewhere
Basic Solutions:
Min. Thickness Target for
3 yrs. Running Time
at ~ ≤ 70 MHz µ+-stops
MC-study of «Surface» & «Sub-surface» beams with target thicknesses
Ranging from 250µm «Active Target» to 100µm «Passive Target»
Stop Rates based on MEG-measurements

## Slide 12: Conclusions
Stopping quality better in the case of Sub-surface beam
Separation quality 25% better at Wien-Filter for Sub-surface beam due to larger velocity difference
More gain going to smaller angles in Surface-case since Sub-surface already more optimal
However
For optimal Sensitivity many factors must be taken into account: stopping-density/target thickness, statistics,
multiple scattering, radiative background production
until final background assessment for both scenarios completed
Baseline MEG Solution with the Thinner Target chosen: Surface beam, 140 µm Target at 15
“Sub-Surface”
“Surface”
From extensive MC-study 2 solutions with
minimal target thickness meet the baseline
detector sensitivity/rate goal:
Surface beam, 140 µm Target at 15
Sub-surface beam 160 µm Target at 15
15
20
20
15