## Slide 1
Part I: CLIC
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Lasers for CLIC and AWAKE projects at CERN
Mikhail Martyanov
EN-STI-LP, CERN

## Slide 2
Photo-injector Team @ CERN
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Valentine Fedossev (section leader)
Eric Chevallay
Christoph Hessler
Mikhail Martyanov
Irene Martini
I acknowledge and thank my present and former colleagues for the input to this presentation !

## Slide 3
Photo-injector Team Aims
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Photo-cathodes development (Cs2Te, Cs3Sb, …)
Photo-injectors operation and maintenance
Laser system maintenance and upgrade
CLIC feasibility studies (photo-injector, laser, stability …)
Photo-emission lab
Laser lab
2 Photo-injector installations

## Slide 4
Photo-injectors at CLIC Test Facility (CTF3): CALIFES and PHIN
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Photo-injector laser lab
(1st floor) and optical transfer lines to PHIN and CALIFES
Drive Beam Accelerator
Delay Loop: x2
Combiner Ring: x4
CLEX: 2 beams test area
CALIFES: Main beam photo-injector
Drive Beam Injector thermionic gun
PHIN
PHIN: Drive beam photo-injector test stand
An alternative to CTF3 drive beam injector
CTF3 Photo-injector laser specifics:
Burst mode operation
Burst rep.rate 1-50Hz
Intra-burst rep.rate 1.5GHz (phase-locked to klystron sub-harmonic)
Pulses in the burst should be equal (stability)
 | Main beam |  | Drive beam |  | 
 | CALIFES/CLIC |  | PHIN |  | CLIC
 | Design | Achieved | Design | Achieved | Design
Bunch rep.rate, GHz | 1.5 | 1.5 | 1.5 | 1.5 | 0.5
Bunch duration, ps | 8-10 | 8-10 | 8-10 | 8-10 | 8-10
Burst duration max, us | 0.14 | 0.2 | 1.27 | 1.27 | 140
Burst rep.rate, Hz | 5 | 5 | 5 | 5 | 50
Charge/bunch, nC | 0.6 | 0.6 | 2.3 | 9.2 | 8.4
Charge stability, % rms | <3 | <3 | <0.25 | 1-2 | <0.1
Photocathode QE, % | 0.3 | 0.3 | 3 | 3 | 1
Cathode lifetime, h |  |  | >50 | >100 | >150
EUV, uJ/pulse | 1 | 2 | 0.6 | 1 | 8
WUV, kW | 1.5 | 3 | 0.9 | 1.5 | 4

## Slide 5
Laser Setup Layout
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
High-Q front end:
Nd:YLF passively mode-locked oscillator and preamplifier
1047 nm, 10W, 1.5 GHz, phase-locked to the external signal (3GHz klystron sub-harmonic)
Nd:YLF PA
10 W 6.7 nJ
Nd:YLF MO
1047nm, 1.5GHz
320 mW 0.2 nJ
Nd:YLF AMP1
3-pass, 2.2 μJ
Nd:YLF AMP2
2-pass, 6 μJ
667 ps
~8 ps
~400 μs
~250 μs
Nd:YLF CALIFES
3-pass, 6 μJ
PC
1-200 ns
I.Ross, “Feasibility Study for the CERN "CLIC" Photo-Injector Laser System”, CERN-OPEN-2000-301 ; CLIC-Note-462, https://cdsweb.cern.ch/record/467721

## Slide 6
CALIFES Amplifier and Harmonics
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
5 pumping diodes (Dilas Gmbh.)
Max 5.5 kW pumping power
Pump pulse duration 500us
1-pass gain 12 (3-pass 1700)
IR input: 4nJ/pulse
IR output: 6uJ/pulse
Peak intensity: ~ 100MW/cm2
SHG efficiency: 67%, 4uJ/pulse
FHG efficiency: 53%, 2uJ/pulse
Pulsed mode operation
Nd:YLF rod, 5mm diam, 70 mm long
SHG: KTP II-type (oe-e), 10 mm
FHG: BBO I-type (oo-e), 4 mm
G. Kurdi et al. “Development of the CTF3 photo-injector laser system”, Central Laser Facility Annual Report 2006/2007

## Slide 7
PHIN Amplifiers and Harmonics
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
AMP1
AMP2
Steady-state operation:
AMP1 - Nd:YLF 7 x 90 mm, diode pump 16kW @ 500 s
AMP2 – Nd:YLF 10 x 120 mm, dioide pump 22kW @ 500 s
IR input: 5 nJ/pulse, 7.6 W
IR output AMP1: 2.3 J/pulse, intra-burst 3.5 kW
IR output AMP2: 6 J/pulse, intra-burst 9 kW
M. Divall, et al. “Design and testing of amplifiers for the CTF3 Photo-Injector Laser”, CARE-Report-2006-021-PHIN, (https://cdsweb.cern.ch/record/1089233)
M. Petrarca et al. “Study of the Powerful Nd:YLF Laser Amplifiers for the CTF3 Photo-injectors”, IEEE J. Quant. El. 47 (2011) 306-313

## Slide 8
PHIN Harmonics (last PHIN run)
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Burst duration for PHIN photo-injector, max 5 s - short burst!
IR input to harmonics: max 5.3 J/pulse, intra-burst 8 kW
IR Peak intensity on SHG crystal: 50 ~ 100 MW/cm2
SHG: 10 mm KTP II-type (oe-e), efficiency up to 50%, 2 J/pulse
FHG: 48 mm BBO I-type (oo-e), efficiency up to 50%, 1 J/pulse

## Slide 9
PHIN Harmonics: Beam shapes
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Burst duration for PHIN photo-injector, max 5 s - short burst!
IR Peak intensity on SHG crystal: 50 ~ 100 MW/cm2
2nd Harmonic:
10 mm KTP II-type (oe-e)
Up to 2 J/pulse
burst energy stability 0.65% rms
Peak intensity ~32 MW/cm2
8 meter focusing onto the photo-cathode
2nd Harmonic beam on the cathode

## Slide 10
PHIN Harmonics: Beam shapes
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Burst duration for PHIN photo-injector, max 5 s - short burst!
4th Harmonic: 2 x 4 mm BBO I-type (oo-e)
Up to 1 J/pulse, burst energy stability 11.5% rms
Peak intensity ~30 MW/cm2
8 meter focusing onto the photo-cathode
4th Harmonic beam on the cathode
1 x 4 mm BBO
4th Harmonic beam on the cathode
2 x 4 mm BBO

## Slide 11: FHG, BBO 4.2 mm UV and Green bursts oscillograms
High-power 4th Harmonic for CLIC
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Model of induced linear absorption, caused by weak 2-photon absorption
2 incident
4
2 residue

## Slide 12: FHG, BBO 4.2 mm UV beam shape for different burst duration
High-power 4th Harmonic for CLIC
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
10us, 4.5mJ
20us, 8.4mJ
40us, 15.1mJ
60us, 20.8mJ
80us, 26mJ
120us, 34.6mJ
UV peak intensity 40 MW/cm2

## Slide 13: FHG, BBO 12 mm UV beam shapes for different burst duration
High-power 4th Harmonic for CLIC
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
10us, 4.4mJ
40us, 14.2mJ
80us, 25mJ
100us, 27mJ
140us, 41mJ
UV peak intensity 30 MW/cm2
2 incident
4
2 residue

## Slide 14: FHG, BBO 11 mm Beam size increased ! UV beam shapes for different burst duration
b) 20 s
High-power 4th Harmonic for CLIC
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
UV peak intensity 12 MW/cm2
2 incident
4
2 residue
f) 60 s
j) 100 s
n) 140 s
h) 80 s
20 s, 13.3 mJ

## Slide 15: - Increase SHG / FHG efficiency keeping the intensity low - Total SHG crystal length – 20 mm BiBO - Total FHG crystal length – 16 mm BBO - Expected overall efficiency >30% - max peak UV intensity 10 MW/cm2
High-power 4th Harmonic for CLIC:
Further Improvements
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN

## Slide 16
Feed-back Stabilization (MHz Bandwidth)
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Yellow – optical pulse
Red – error signal
Green – driving voltage
feed-back off
feed-back on
working point
operating range
To reduce an optical load on the feed-back PC it is installed between amplifiers 1 and 2

## Slide 17
Feed-back Stabilization (MHz Bandwidth)
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
0
16.7
33.4
50.1
66.8
83.5
0
0.02
0.04
0.06
0.08
0.1
V
ns
Chart: 140us pulse train with a feedback
Chart: t, us
“Fast” noise from the oscillator (GHz bandwidth)
Zoom, “Slow” noise (MHz bandwidth)
Optical noise:
“Fast” – from the oscillator
“Slow” – from the oscillator and amplifiers
Stabilization is needed to suppress the noise

## Slide 18
Feed-back Stabilization Test
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Cathode #193
3% rms
Cathode #188
0.97% rms
1.34 % rms
factor 3
improvement !
0.43 % rms
Laser beam
Electron beam
Feedback OFF
Feedback ON

## Slide 19
Upgrade of the Laser System
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Current laser setup:
Common 1.5 GHz, 10 W HighQ front-end
Simultaneous laser operation of CALIFES and PHIN photo-injectors is possible (with limitations)

## Slide 20
Upgrade of the Laser System
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Future laser setup:
CALIFES and PHIN lasers are completely decoupled
Simultaneous laser operation of CALIFES and PHIN photo-injectors
PHIN laser timing parameters pushed towards CLIC requirements due to new front-end ordered from OneFive company.
ORDERED

## Slide 21
Part II: AWAKE
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Advanced Proton Driven Plasma Wake Field Acceleration Experiment (AWAKE) at CERN Mikhail Martyanov, CERN on behalf of AWAKE Collaboration

## Slide 22
Who Is AWAKE?
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
AWAKE - is an international collaboration formed to carry on a
Proton Driven Plasma Wake Field Acceleration Experiment
at CERN site with SPS proton bunches.
from AWAKE CDR, CERN 2013
leading institute

## Slide 23
Who Is AWAKE?
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
AWAKE Structure:
Spokesperson: Allen Caldwell (MPP)
Deputy Spokesperson: Matthew Wing (UCL)
Technical Coordinator: Edda Gschwendtner (CERN)
Physics and Experiment Coordinator: Patric Muggli (MPP)
Simulation Coordinator: Konstantin Lotov (BINP)
Some useful links:
https://www.mpp.mpg.de/~muggli/AWAKE@MPP/AWAKEatMPP.html
http://indico.cern.ch/category/4278/
AWAKE Design Report:
https://edms.cern.ch/nav/P:CERN-0000094988:V0/P:CERN-0000097681:V0/TAB3

## Slide 24
Where AWAKE at CERN?
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
AWAKE experiment
AWAKE
beam dump
~1100m
~100 meters deep underground, former CNGS facility

## Slide 25
Where AWAKE at CERN?
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN

## Slide 26
AWAKE Timeline
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
2 years until physics ! Very tight schedule

## Slide 27
AWAKE Basics
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Four Ingredients:
Protons (from SPS, 400 GeV)  energy source
Plasma Wake  transformer to an E-field (a few GV/m)
Electrons (from photo-gun, 20 MeV)  enjoy a gradient

## Slide 28
AWAKE Basics
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Fourth important Ingredient:
Laser (short pulse)  To ionize Rb vapor  To seed an instability with a stable phase by co-propagating ionization front

## Slide 29
AWAKE Experiment at CERN
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Picture taken from AWAKE CDR, CERN 2013

## Slide 30
AWAKE Experiment at CERN
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
~100 meters deep underground,
former CNGS facility
Laser
e-gun
p+ beam 400GeV
e- beam
20 MeV
laser beam
120fs, 450mJ
Fast valves
10 meters Rb vapor / plasma
e- spectrometer
up to 2 GeV e-
p+ / e-
diagnostics
CV
SAS
AWAKE gallery
Control room 1km
Laser / p+ merging point

## Slide 31
AWAKE “Submarine”
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Arms until Rb vapor cell:
Ionizing laser ~ 30m
Photo-injector laser + e-beam ~ 30m
Ionizing laser beam transport:
Complete UHV vacuum system up to 10-8mbar
starting from the optical compressor
Motorized 3 inch mirrors in the corner chambers
Long focal length (35m) focusing geometry through the compressor
Thanks to
Frederic Galleazzi

## Slide 32
AWAKE “Submarine”
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Thanks to
Frederic Galleazzi

## Slide 33
AWAKE Baseline Parameters
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Plasma | Rb plasma density | 1014  1015 cm-3 7(10-3  10-2) mBar at 500K
 | Uniformity | <0.1%
 | Length | 10 meters
Proton bunch | Energy | 400 GeV  64 nJ/p+  19.2 kJ/bunch
 | Charge | 31011 particles  48 nC
 | Length, z | 12 cm  400 ps
 | Radius, r | 200 m
Electron bunch | Energy | 20 MeV  3.2 pJ/e-  4 mJ/bunch
 | Charge | 1.25109 particles  200 pC
 | Length, z | 0.25 cm  8 ps
 | Radius, r | 200 m
Laser | Energy | up to 450 mJ
 | Pulse duration | 120 fs
 | Beam size at Rb vapor (focused from 40m) | a few mm
 | Focused intensity | > 50 TW/cm2

## Slide 34
Plasma Wake Field: Short Driver
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Charge density
Simulation done by Alberto Martinez de la Ossa
ne = 2 1015 cm3 pe = 402 GHz
λpe = 750 μm E0max = 4.3 GV/m
Taken from the talk by Matthias Gross
at Proton-Driven PWA Meeting
Lisbon, 22 June 2012
Longitudinal E field
Transverse E field
Witness bunch
Short driver
Maximum acceleration gradient
Some radial focusing
As a short driver:
Focused powerful fs-laser pulse
High energy particle bunch (p+, e-)

## Slide 35
Plasma Wake Field: Long Particle Bunch Driver
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
If the driving bunch is long – no efficient wake excitation.
But … there are instabilities!
Presented by J. Vieira, 8 March 2013, CERN, Geneva
at AWAKE Collaboration Meeting

## Slide 36
Self Modulation Instability
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Space charge of drive beam displaces plasma electrons.
Plasma ions exert restoring force.
e-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
Ez
e-
proton
bunch
Short proton bunch driver
No SMI
Long proton bunch driver
SMI develops

## Slide 37
AWAKE Experiment: Principle
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Ionization front is co-propagating with a short laser pulse and seeds Self Modulation Instability (SMI)
laser ~ 100 fs << wake ~ 3 ps
100% Rb plasma
100% Rb vapor
e- are injected
accelerated and focused e-
Ionization front
Picture taken from AWAKE CDR, CERN 2013

## Slide 38
AWAKE Experiment: SMI Details
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Picture taken from AWAKE CDR, CERN 2013
NB! No longitudinal (velocity) bunching
Only radial (envelope) “bunching”!
Total current is concerved

## Slide 39
Proton Bunch Evolution
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Presented by K.Lotov at AWAKE Collaboration Meeting, CERN 08.03.2013
Beam portrait (2nd half)
Excited field Ez
 = z - ct , cm
0
30
r , mm
Ez , a.u.
0
0.4

## Slide 40
On-axis e- injection, trapping and acceleration
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Presented by K.Lotov at AWAKE Collaboration Meeting, CERN 10.04.2014
Features to note:
  Electrons are trapped from the very beginning by the wake field of seed perturbation
  At r~3 c/wp there is a defocusing region for any . Reason – incomplete neutralization of the beam current  plasma lens effect for protons, defocusing lens for electrons
  Trapped electrons make several synchrotron oscillations in their potential wells.
  After L=4 m the wake field moves forward in the light velocity frame (newly discovered effect)
black points – injected electrons, false colors – wake field potential
 = z - ct, cm
-16.4
-17
r, mm
0
2

## Slide 41
Resulting e- Energy and Spread
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Presented by K.Lotov at AWAKE collaboration meeting, CERN 10.04.2014
Comparison of best simulation results
Side injection (CDR baseline): 5% trapping, 3% energy spread
Off-axis injection (collinear electron beam shifted radially by 1.8 mm): ~5% in the main spike
On-axis injection: 40% trapping, 12% energy spread
Improved Side injection: 30% in the main spike, 4% energy spread 45% trapping, 6.5% energy spread

## Slide 42
AWAKE Laser Overview
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Ti:Sa laser system comprises:
- laser with 2 beams (for Rb-vapor ionization and for the e-gun)
- delay line is possible in either of both beams
- focusing telescope (lenses, in air) before vacuum compressor
- long 35 meter focusing to Rb-vapor cell
- optical compressor (in vacuum)
- optical in-air compressor and 3rd harmonics generator for e-gun

## Slide 43
AWAKE Laser Overview
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Ti:Sa laser parameters for Rb-vapor ionization:
- max energy after compression 450 mJ
- pulse duration 100 fs after compression
- max beam diameter 40 mm
Laser energy required for Cu cathode and 1nC @ 3rd harmonic with some margin = 0.5 mJ
Only reflective optics on the
compressed pulse way
Rule of thumb (B<1):
I[GW/cm2]L[cm]<36

## Slide 44
How to Ionize Rubidium?
Basic Types of Laser Ionization
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
x
i
(x)
h
Single photon (photo-effect)
h > i
 >> t
field E is small,
 << i
Multi-photon
nh > i
 >> t
field E is small,
 << i
Tunneling
 < ~ > t
field E is high,
 < i
Strong field
 << t
field E is high,
 > i
h
(x)
i
(x)
i
Ex ~ sin(t)


(x)
i
Ex ~ sin(t)
lifetime =1/t
Rubidium i = 4.2 eV = 300 nm
Laser h = 1.6 eV = 785 nm

## Slide 45
AWAKE: Strong Field Ionization
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Strong field ionization threshold for Rubidium < 2 TW/cm2
Focused laser beam intensity > 50TW/cm2
Well above threshold, really strong field ionization

## Slide 46
AWAKE Laser Room: Cooling & Ventilation
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Design of ventilation system is on-going.
Open question: Which humidity level can be accepted?

## Slide 47
Vacuum Laser Transfer Line
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Thanks to
Nicolas Chritin

## Slide 48
Vacuum Laser Transfer Line
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Thanks to
Nicolas Chritin

## Slide 49
Vacuum Laser Shutter
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Thanks to
Nicolas Chritin

## Slide 50
UHV Compatible Optical Mounts
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
UHV - PicomotorTM ClearEdge Optical Mounts Features:
Customized Picomotor 1.0, 2.0”, and 3.0” in (25.7, 50.8, 76.2 mm) mirror mounts – Clear Edge
ΘX, ΘY Adjustments with angular resolution of <0.7urad
UHV Compatible 10^-9 Torr
Kapton wires ideal for X-ray, UV or EUV applications
All vented holes
Integrated polished carbide pads
Currently under vacuum test

## Slide 51
SMARACT: UHV Compatible Linear Translator
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
“Piezo-walk” technology
Second parallel passive guide-way at the side of the active positioner
Travel 100 mm
Step size ~1 um
Max. vertical load 20 kg
UHV up to 1e-11 mBar, KAPTON wires
Roll, Pitch and Yaw < 100 urad
Currently under vacuum test

## Slide 52
AWAKE Summary
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
AWAKE is scientifically and technically challenging experiment with a tight schedule
Main challenges are:
  10 meters long extremely uniform (<0.1%) Rb plasma channel  oil bath
  Hot (500K) Rb vapor vessel v.s. ultra high vacuum outside  fast valves
  Synchronization in time and space of 3 beams (p+, e-, laser)
  Seeding of Self Modulation Instability (SMI)
  Diagnostics of SMI and others
  Long focal waste Rb vapor strong field ionization by Ti:Sa laser
  And many more ...
  First physics – end 2016

## Slide 53
Part II: AWAKE
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Thank you!

## Slide 55
Laser & Plasma Parameters Glossary
Paul Scherrer Institute Seminar: “Lasers for CLIC and AWAKE projects at CERN”
13.10.2014 Mikhail Martyanov, CERN
Plasma oscillations (Langmuir oscillations) frequency
for ne=1015 cm-3
pe = 284 GHz
pe = 1.06 mm
Charge density oscillations in a cold plasma
Response to any local break of quasi-neutrality
Collective motion of plasma electrons with Langmuir frequency
Wake oscillations
Caused by a “driver” moving fast in plasma
Wake fields are intrinsic property of wake oscillations
Simple theory: maximum electric field in plasma
for ne=1015 cm-3
E0 max = 3 GV/m