## Slide 1: Data size
MEG I
  Trigger rate : ~10Hz
  Event size : 1MB after bzip2 compression
MEG II
  Trigger rate : a few Hz* or ~30 Hz**
  Event size ?
    Much more number of channels (~3500 → ~10000)
    More particles in the DAQ time window (Data reduction more difficult ? ).
* could be achivable with 2nd-level TRG ** conservative assumption
Assumed event size (unit of MEG I) | Required minimum event rate to be written on disk
1/4 | 30 Hz
1 | 7.5 Hz
3 | 2.5 Hz
5 | 1.5 Hz
10 | < 1 Hz
likely to be

## Slide 2: Event selection in MEG I
TRG0
Time TC-γ
Time TC-DC
γ acceptance
γ CR, pileup
Track fitted
nhit per track
Track fit quality
Vertex on target
TC-DC match
Time e+-γ
Theta e+-γ
Phi e+-γ
Energy e+
Energy γ
Relative size after selection
Reduction factor of each selection
Eγ and TC-DC match reduction factors are modified for this plot to take into account the situation of MEG II
These selections are necessary to reduce by factor 10—20.

## Slide 3: Data flow in MEG I
DAQ backend
Offline storage
Tape archive
Raw data is stored here permanently
Raw data is stored here for 1—2 years until the pre-selection is done.
(need to prepare calibration)
Pre-selected raw data (~40% of events) are stored here permanently

## Slide 4: Where the software trigger can be?
DAQ backend
Offline cluster
Tape archive
Raw data is stored here permanently
(If we need,)
The “Software TRG” system can consist of multiple PC
Select events using the regular or dedicated analyzer
  We already have a similar selection mechanism in MEG I analyzer
Multiple CPU cores in S-TRG for parallel processing (10—20 jobs)
Required disk access speed is reduced as the number of S-TRG computer increase
Network traffic to the offline cluster is reduced by the event-selection in S-TRG computer
S-TRG computer
S-TRG computer
S-TRG computer
the number of S-TRG computer can be O(10)