## Slide 1: MEG-II CDCH status
Marco Grassi
PSI, 9 Feb 2015

## Slide 2: MEGII Cylindrical Drift CHamber
The new MEGII chamber will be
single volume gaseous detector
U – V wire stringing for hit positioning along the wire
low mass gas (He : iC4H10 - 85% : 15%)
thin wires and small cell size
Final goals
Single hit resolution ~100 mm in r
Momentum resolution ~150 KeV
Angular resolution ~5 mrad
DC-TC matching eff. ~90 %

## Slide 3: Chamber structure
He / iB
He
vacuum
air
air

## Slide 4: Technical and geometrical parameters
The parameters with impact on the chamber performances are
  2p
  Rmin e Rmax
  L
  Cell structure
  Wire types
  Gas mixture
  FE
  Double readout
294 mm
157 mm
R_safe_ext
R_safe_int
1932 mm
wires
Costraints on wires |  | 
R_ext_max | 294.000 | mm
Fiber_thick | 2 | mm
Screws_thick | 3 | mm
R_safe_fiber | 5.000 | mm
R_wire_max | 284.000 | mm
R_ext_min | 157.000 | mm
R_safe_foil | 10.000 | mm
R_wire_min | 167.000 | mm

## Slide 5: Technical and geometrical parameters
The parameters with impact on the chamber performances are
  2p
  Rmin e Rmax
  L
  Cell structure
  Wire types
  Gas mixture
  FE
  Double readout
Geometry used of the chamber
10 layers of cells
  Radius of the outermost anode layer R0 = 275 mm
  Fixed sector width 2f = 60 deg
  Planar EndPlate at Z0 = 966 mm
  Total F coverage = 360 deg
  Equal number of cells per sector nC = 32
  Cell Width CW from nC
  Cell Thickness CT equal to CW
  Radial position R from CT
  Stereo angle q fixed by R

## Slide 6: Technical and geometrical parameters
Item | Description | Thickness | 
 |  | 10-3 X0 | 
MEG target | (140 mm plastic) | 0.28 | 0.28
Sense wires | (20 mm W) | 0.41 | 0.78
Field wires | (40 and 50 mm Al) | 0.33 | 
guard ring wires | (40 mm Al) | 0.04 | 
protective foil | (20 mm Kapton) | 0.21 | 0.21
Inner gas | (pure He) | 0.06 | 0.59
Tracker gas | (He/iBut. 85/15) | 0.53 | 
Total | 1 full turn w/o target | 1.58 | 
The parameters with impact on the chamber performances are
  2p
  Rmin e Rmax
  L
  Cell structure
  Wire types
  Gas mixture
  FE
  Double readout

## Slide 7: Wires
Selected wires
  Anodes - 20 mm W (Au)
  Cathodes - 40 mm Al (Ag)
  Cathodes - 50 mm Al (Ag)
Producer
  California Fine Wires
Procurement
  Wire procurement was on critical path in 2014
  California Fine wires solved all production issues
  All wires have been delivered in autumn
  Wires respect our specifications

## Slide 8: Gas selection and aging
Again dominated by the need of very low X0
He/iB (85/15) (the He/Eth 50/50 of MEG is unusable)
Chamber ageing is under control up to 3 years operation (0.5 C/cm)
20x aging speed with x-ray source
Effect at operation gain (1-2x105) spatially limited and at 15% / year
Accum. charge [C/cm]
Norm. current

## Slide 9: FE preamplifier
Requirements
High bandwidth >700 MHz
Good gain: ~20
High density < 7mm width
Layout
Double stage (ADA4927 and THS4509)
Direct connection to DRS WaveDream
Satisfactory used on all prototypes
The parameters with impact on the chamber performances are
  2p
  Rmin e Rmax
  L
  Cell structure
  Wire types
  Gas mixture
  FE
  Double readout

## Slide 10: Double side readout
MEGII environment will be crowded and event filter might require large computational time Tracking is greatly simplified and a redundancy margin is added if a coarse longitudinal hit position is obtained by a double wire readout
Longitudinal hit position with time difference
0.5 ns Dt resolution
<10 cm resolution
13.2 cm/ns signal speed
Longitudinal hit position with charge division
170 ohm/m anode resistivity
<10 cm resolution

## Slide 11: Simulation performances
Impact parameter smear of 120 mm
gara
All requirements to the new MEGII tracker are obtained

## Slide 12: Single hit resolution
True impact parameter defined by an
external silicon tracker
sb-TRUE ~ 30 mm
Average single hit resolution
106 ± 2 mm
for the three cells

## Slide 13: Possible improvements
Cluster timing
  The requirements for a full exploitation of the cluster-timing technique are included in the chamber design
High bandwidth FE with large amplification
  Low ionisation density gas
Waveform digitisation in the GSPS region
  Better performances are expected
b [cm]
s(b) [cm]
130 mm first cluster
60 mm cluster timing

## Slide 14: Constructive details 2014
To be confirmed/defined
  Adhesive tape
  End-plates sealant
  Kapton foil structure
  Gas distribution
  FE – WirePCB connection
  Cables to DRS
  FE cooling
Defined
  Carbon fiber support
  Connection to endplates
  Endplates structure
  Gas tightness
  Chamber extensions
  Location of target support
  Connections to BTS and Insertion System

## Slide 15: Constructive details 2015
Defined
  Adhesive tape
  End-plates sealant
  Kapton foil structure
  Gas distribution
  FE – WirePCB connection
  Cables to DRS
  FE cooling
Defined
  Carbon fiber support
  Connection to endplates
  Endplates structure
  Gas tightness
  Chamber extensions
  Location of target support
  Connections to BTS and Insertion System
The production of the chamber is started

## Slide 16: End-Plates
End Plates produced in house
Production precision: better than 50 um
Deformation under load: maximum of 130 +30 um
completed
Mounting procedure
Wires soldered to WirePCB
Placed in the EndPlates
Sequence of peek spacers and WirePCB

## Slide 17: WirePCB
Review of all 35 different PCBs
  Increased electrical insulation (2.8 mm)
  Simplified connection to FE
Design completed
First bunch delivery on Friday Feb 06
  Guard03
  Cath10
  Anod09
  Cath09
Delivery completion in 2 bunches: begin of April and middle of June

## Slide 18: Spacers
End-Plate mechanical design completed
WirePCB spacers designed
Material peek already procured
Production method machined from 29 mm slab
Required precision a surface roughness achieved

## Slide 19: Wire stringing
q
a
Db
Dp
DB
Rf
Z
-
b
Wire wound and soldered on WirePCB at nominal length and stress on a rotating cylinder
Computer controlled rotation, wire translation and tension
Coupling with transport trays
Winding the wire on a cylinder where WirePCB are properly placed permit correct spacing, stereo angle and correct length

## Slide 20: Wiring Machine
Laser Controller
Motor and Torque
Cylinder
Wiring digital camera
Last pulley
Laser, Laser camera and pyrometer
Main slide
Coil, clutch
Control system
The template for the inner layer of the guard wires is ready for wiring.
Sensors and monitoring systems (torque, clutch, brake) were connected to the control system.
Control software development is in progress

## Slide 21: Assembly machine
Machine delivered
Acceptance measurements completed
Mounting completed
System test half of February
  Behaviour under simulating
  load of 350 + 20 Kg
Assembly sequence
Place layer of spacers
Reduce the endplate distance
Mount the wirePCB with wires
Place endplates at nominal distance
Check wire tension and make mechanical survey

## Slide 22: Assembly machine

## Slide 23: CDCH extensions
Provide coupling to BTS and target support
Hold the FE electronics
First set delivered
Fit with mock-up endplates
Final set production started

## Slide 24: FE electronics
FE PCB dimensions are fixed
The single channel layout fits in a 5.2 mm x 30 mm rectangle
All components have been already ordered

## Slide 25: FE electronics
8 channels are accommodated in a single FE board
A cooling slit can be added
The electrical performances are preserved

## Slide 26: Carbon fiber support
Designed and simulated
Currently in production
Delivery expected by April 2015

## Slide 27: Auxiliary systems
HV system
  Upgrade of the present system
  High performance
  Delivered and tested
  Control software already developed
Gas system
  Requirements similar to the present system
  Better control of the gas quality
    O2
    H2O
    Hydrocarbones
  All parts already procured
  Assembly started
Wire tension measurement
  Use during chamber assembly
  Working prototype
  Final system in production
FE cooling system
  Total FE power 2x400 W
  Limited space available
  Cooling by mean of refrigerated water
  Chillers already delivered

## Slide 28: Time plan
The entire production plan has been reviewed
This includes tasks
Laser soldering system setup
Tooling preparation
Wire winding
Wire PCB production
Spacers milling
Mechanical assembly
Chamber survey
Chamber full and extensive test
Shipping
resources
Italian working calendar
Technician manpower
Tooling machines
and some contingency
40 working days for spare part production

## Slide 29: Gantt chart

## Slide 30: Conclusions
The single-volume stereo drift chamber fulfils the MEG II requirements
MC simulation is based on solid prototypes results
All critical decisions have been taken
All parts are delivered or under production
The final assembly is expected to start before end of February
The chamber delivery at PSI is foreseen by March 2016
A working mock up chamber will be delivered at PSI by July 2015

## Slide 31: Backup slides

## Slide 32: MEG tracker
16 chambers
Each chamber is composed of
  4 x12 mm of kapton (cathodes)
  50 mm BeCu cathode wires
  25 mm NiCr anode wires
  2 x 7 +3 mm He:C2H6 (50/50)
Single chamber x ~ 0.23 10-3 X0
Full e+ turn : x ~ 1.7 10-3 X0

## Slide 33: Performance summary
Single hit resolution
sR (mm) 250 (core) 300 (RMS)
sZ (mm) 700 (core) 1000 (RMS)
Track resolution
s (p) 310 KeV (core)
s(f) 7. mrad (at f = 0, 10 mrad aver.)
s(q) 11. mrad
s(Y) 1.3 mm
s(Z) 3.0 mm
TC – DC reconstruction
DC-TC matching eff. 45 %

## Slide 34: Gain vs Z
Expected gain variation with Z given the hyperbolic geometry

## Slide 35: WirePCB: connections
Wire connection
Double pad stucture
Thin line for wire positioning check
Via hole for cathode wire on the second pad
FE connection
EdgeConnector: 12 contact at 2.54 mm
Limit FE wing length
Ensure FE –Wire PCBs alignment
Cope with limited space
Sullins connectors is the main option

## Slide 36: WINDING/SOLDERING SLIDE
The pulley system has been equipped with micrometric slides to allow the adjustments of the position for the different layers.
A real-time control for the wire tension during the process of winding is introduced.
SYSTEM PULLEYS
TENSION SENSOR

## Slide 37: CONTROL SYSTEM
The control system of the cylinder and the slide was mounted and connected.
The control system for PCB wire extraction is on the way.
Different sensors and monitoring systems (torque, clutch, brake) was connected with the control system.
The control software development is in progress.

## Slide 38: Details

## Slide 39: Details

## Slide 40: Details

## Slide 41: Details