## Slide 1
W.S. Graves
MIT and Arizona State University
presented at Paul Scherrer Institute, July 2015
Tabletop source of intense hard x-rays
toward a
Compact XFEL

## Slide 2
X-ray tube from 1917
X-ray tube today
Flux of 5 X 109 photons/sec
Brilliance* of 109
Factor of ~100 better than 100 years ago
X-ray flux of 107 photons/sec from source of few mm2 and large opening angle
From Rontgen’s tube to today’s best laboratory-scale sources
*Brilliance is in units
photons/(sec mm2 mrad2 0.1%)
Tubes are primitive low energy (0.1 MeV) electron accelerators

## Slide 3
Particle accelerators in the 20th century
Synchrotron radiation from relativistic beams first developed around 1960 and is now mature 50 years later
X-ray flux of 1015 photons/sec into a 50 X 50 micron spot
X-ray brilliance of 1021 photons/(sec mm2 mrad2 0.1%)
Roughly a trillion times brighter than a laboratory source!
Advanced Photon Source (APS) at Argonne Nat’l Lab
kilometers in size
$1 billion in cost
7,000 MeV electron energy
1000’s of users

## Slide 4
X-ray Free Electron Laser (XFEL)
X-ray bursts of 1012 photons in 100 fs
Peak x-ray brilliance of 1033 photons/(sec mm2 mrad2 0.1%)
Transverse coherence (not yet temporally coherent)
kilometers in size
$1 billion in cost
14,000 MeV electron energy
100’s of users
Linac Coherent Light Source (LCLS) at Stanford

## Slide 5
Generational advances in beam brilliance
X-ray Lasers
Synchrotron
Radiation
X-ray Tubes
Relativity
Coherent
Emission

## Slide 6
Compact size (1900)
Synchrotron radiation from relativistic beams (1975)
Coherent emission from XFEL (2010)
Blueprint for an intense compact x-ray source
Compact X-ray Light Source

## Slide 7
Undulator Radiation
X-ray radiation
Laser field
Electron beam
Inverse Compton Scattering
Use relativistic electrons but shrink the undulator period from cm to microns
Switch from static B-field to propagating EM field (laser)
How to make a compact source?

## Slide 8
Basic Layout for ICS
RF gun
1 meter long linac
Quads
Dipole
X-ray optic
Electron dump
ICS
Laser cavity
Laser amplifier
Sample
Detector
<4 m

## Slide 9
Yb:KYW amp #1
Yb:KYW amp #2
Oscillator
Yb:KYW compressor
Yb:YAG regen
Yb:YAG compressor
UV for cathode
Cryo Yb:YAG
RF transmitter
Power supplies for magnets, UHV equipment, lasers
Linac
RF gun
Chicane
Interaction area for ICS
Beam dump
X-ray experiments
Compact X-ray Light Source (CXLS)

## Slide 10
2MW of RF power
Impedance transformer
Matched splitter
Input cell with race-track shape to minimize
quadrupole fields
Laser beam in
Electrons out
Photo-cathode
surface
High shunt impedance
accelerating cell
9.3 GHz RF photoinjector
Thermal profile at 2 kW avg power
V.A. Dolgashev, SLAC

## Slide 11
CIRCUIT ‘HALF’
PRECISION ALIGNMENT HOLES
ACCELERATOR CELL
FEED WAVEGUIDE
AXIAL COOLANT HOLES
INCONEL SPRING PIN
CUT-AWAY VIEW OF BRAZE ASSEMBLY
FEED WAVEGUIDE
COUPLING HOLE
TUNING PIN
(2 PER CELL)
Novel 9.3 GHz SW Linac Structure
S. Tantawi, SLAC
Very high efficiency standing wave structure at 9.3 GHz
1 kHz rep rate
Every cell coupled from waveguide
Inexpensive to build

## Slide 12
Two lasers, cathode and ICS
F. Kaertner group DESY and MIT

## Slide 13
ICS Interaction Point (IP)
Quadrupole magnets
Interaction point
Montel x-ray optic
Linear laser cavity with harmonic conversion
ebeam out
x-rays out
ebeam in
Dipole
Electron dump
Detector

## Slide 14
Slice ebeam parameters at IP

## Slide 15
Electron beam at IP
PARMELA simulations

## Slide 16
Opening angle of 12 keV radiation
Intensity vs angle for 5% bandwidth
Flux is 5x1011 per second
Intensity vs angle for 0.1% bandwidth
Flux is 2x1010 per second
COMPTON simulations

## Slide 17
Flux and brilliance
0.1% BW
5% BW
0.1% BW
5% BW
Brilliance
7e12 in 0.1% BW
2e12 in 5% BW
Flux
2e10 in 0.1% BW
5e11 in 5% BW
ICS can put 1010 – 1011 photons/sec into a 5 X 5 micron spot
Synchrotron bend is typically 1010 – 1011 photons/sec in 100 X 100 micron spot

## Slide 18
Focusing Optics
RMS source size and divergence are 2 microns and 4 mrad
Nested Si K-B optic with graded multilayer magnifies factor of 3
Optic collects 84% of light within 5% bandwidth.
Detector is ~1.2 m from source.

## Slide 19
Collimating Optics

## Slide 20
Summary of 12 keV parameters
Parameter | 0.1% Bandwidth | 5% Bandwidth | Units
Average flux | 2x1010 | 5x1011 | photons/s
Average brilliance | 7x1012 | 2x1012 | photons/(s .1% mm2mrad2)
Peak brilliance | 3x1019 | 9x1018 | photons/(s .1% mm2mrad2)
RMS horizontal size | 2.4 | 2.5 | microns
RMS vertical size | 1.8 | 1.9 | microns
RMS horizontal angle | 3.3 | 4.3 | mrad
RMS vertical angle | 3.3 | 4.3 | mrad
Photons per pulse | 2x105 | 5x106 | 
RMS pulse length | 490 | 490 | fs
Repetition rate | 100 | 100 | kHz
(incoherent ICS, undulator-like radiation)

## Slide 21: Toward an XFEL using coherent ICS
Randomly distributed electron beam
Bunched electron beam
Regular:
Ix-ray ~ N
Coherent:
Ix-ray ~ N2
N > 106
Graves et al, Phys Rev Lett 108, 263904 (2012)

## Slide 22
Transmission Electron Microscopy (TEM)
Perfect Si Crystal
Fringes from Stacking Faults in Al-Cu-Mg-Ag
0.23 nm
TEMs routinely achieve sub nm resolution (density modulation) with electron energy < 1 MeV

## Slide 23
Emittance Exchange
Diffracted beamlets
x
x’
t
Current
t
Current
x
x’
t
Energy
EEX
t
Energy
x
y
Bunched beam emits coherent ICS
x
y

## Slide 24
Electron Diffraction
Emittance Exchange (EEX)
Compact XFEL layout
“Nano-modulated electron beams via electron diffraction and emittance exchange for coherent x-ray generation”
E.A. Nanni, W.S. Graves, F.X. Kaertner, D.E. Moncton
arXiv:1506.07053v1, submitted to Phys Rev Lett
“Intense Superradiant X Rays from a Compact Source Using a Nanocathode Array and Emittance Exchange”
W.S. Graves, F.X. Kaertner, D.E. Moncton, and P. Piot
Phys Rev Lett 108, 263904 (2012)

## Slide 25
Tune the modulation spacing of the diffracted beam with patterned Si substrate
Diffraction Contrast Image
Modulated Electron Beam
Bunching Factor
Si
675 nm
150 nm
675 nm
Incident Beam
0th Order
1st Order
Emittance at IP:
εx = 9 nm-rad
εy = 9 nm-rad
εz = 10 nm-rad
~2000 Modulations

## Slide 26
Electron Optics to the Interaction Point
Accelerate electron bunch to the desired energy
Match resonance condition
Magnification of modulation to match
Exchange emittance (phase space) with aberration correcting geometry*
Diffraction
Sample
Electron
Diffraction
Nanni, E. A., and W. S. Graves. "Aberration Corrected Emittance Exchange." arXiv:1503.03493 (2015), submitted to Phys Rev ST-AB

## Slide 27: 1.24 nm Modulation at Interaction Point (IP)
Electron beam simulated from photo-cathode to IP
Electron beam accelerated to 22.5 MeV after diffraction
Acceleration, Telescope and EEX result in M=1/120
0.35 pC of reaches IP
Emittance at IP:
εx = 10 nm-rad
εy = 10 nm-rad
εz = 10 nm-rad
Bunching Factor
~2000 Modulations
~3 µm or ~10 fs
Modulated Electron Beam

## Slide 28
Parameter | Value | Units
Photons per pulse | 3.1x107 | 
Pulse energy | 5.0 | nJ
Average flux* | 3.1x1012 | photons/s
Bandwidth (FWHM) | 0.1 | %
Average brilliance* | 1018 | #
Peak brilliance | 1028 | #
Opening angle | 0.5 | mrad
Source size | 0.5 | µm
Pulse length | 28 | fs
Repetition rate | 100 | kHz
Average current | 50 | nA
*average values for 100 kHz rep rate
#photons/(s .1% mm2mrad2)
Simulation Results
1.24 nm Modulation – 1 keV X-ray
Pulse in Time
Spectrum

## Slide 29
Brilliance of Compact Light Sources
X-ray Lasers
X-ray Tubes
CXLS
Compact XFEL (avg)
Compact XFEL (peak)

## Slide 30
Conclusions
A low-risk hard x-ray compact source can outperform today’s lab sources by a factor of 10,000
CXLS flux/brilliance similar to synchrotron bending magnet beamline
CXLS has many applications inaccessible to a synchrotron
A fully coherent compact XFEL based on this technology is likely within 5 years

## Slide 31
People
MIT
K. Berggren, J. Bessuille, P. Brown, W. Graves, R. Hobbs, K.-H. Hong, W. Huang, E. Ihloff, F. Kärtner, D. Keathley, D. Moncton, E. Nanni, M. G. Resta, Swanwick, L. Vasquez-Garcia, L. Wong, Y. Yang, L. Zapata
DESY
J. Derksen, A. Fallahi, F. Kärtner
Northern Illinois University
D. Mihalcea, P. Piot, I. Viti
SLAC
V. Dolgashev, S. Tantawi
Jefferson Lab
F. Hannon, Feisi He, J. Mammosser