RF Upgrade Plans at DELTA
P. Hartmann
DELTA, TU Dortmund
DELTA parameters:
Beam energy: 550 MeV – 1.5 GeV
Beam current: 130mA @ 1.5GeV
Beam lifetime: 12h @ 130 mA
Availability: 95 %
Operational: 3000 h / year
Personnel:
2 Professors
4 Accelerator physicists
2 Beamline scientists
1,5 Administration
9 Engineers / Technicians
X Students
[Speaker Notes: Delta is a 1.5 GeV... We run the Accs with a staff of 20 person and students]

---
DELTA 500 MHz RF Systems
Analog LLRF @ 499,82 MHz
Klystron amplifier YK-1265 (42 kW)
DORIS type single-cell cavity
DESY HOM-Antenna damper
Analog LLRF @ 499,82 MHz
Klystron amplifier YK-1265 (15 kW)
DESY type 3-cell cavity
[Speaker Notes: Delta: Speicherring und Vorbeschleuniger Linac und BoDo Linac 80MeV, BoDo 80-1500MeV, Delta 1500 MeV Full energy injection Delta users from federal country, beamlines overbooked 500 MHz RF-systems for the booster and the SR 20 years old]

---
DELTA Users
[Speaker Notes: SAW will be replaced]

---
Wiggler upgrade
	Unit	Current wiggler	New wiggler
Type		asymmetric	symmetric
Periods		5	9
Magnetic field	T	5,3	7
Critical energy	keV	7,9	10,5
Irrad. power @ 100 mA	kW	2,2	9,8
Call for tender in spring 2016
Order to Budker Institute / Novosibirsk
Delivery expected end of 2018

---
Storage ring RF upgrade options
	Unit	1	2	3	4	5
Total power loss	kW	20,44	31,2	31,2	31,2	31,2
Power loss wiggler	kW	2,86	13,6	13,6	13,6	13,6
Energy loss / turn	keV	157,2	240	240	240	240
Number of resonators		1	1	2	3-cell	2
RF power per cavity	kW	41	50	25	50	50
Cavity voltage	keV	350	330	240	582	455
Power loss resonator	kW	20,4	18,8	9,6	18,8	34,5
Coupling factor β		2	2,7	2,7	2,7	1,4
Synchrotron frequency	kHz	15,1	14,8	17,4	19,7	17,8
Synchronouos phase	°	26,7	46,6	29,9	24,3	15,3
Momentum compaction		0,0053	0,0053	0,0053	0,0053	0,0053
Energy acceptance	%	0,76	0,43	0,83	1,03	2,2
Damping time long.	ms	3,67	2,4	2,4	2,4	2,4
Bunch length	ps	46,2	61,3	52,2	46,2	25,2
Quantum lifetime	h	>1010	<10-4	>104	>1011	>1080
Touschek lifetime	h	24	8	33	48	157
T. Weis, DELTA Internal Report 2013
[Speaker Notes: Thomas Weis generated a table with many upgrade options. This is an extract. 1: Current system with old SAW 2: New wiggler, increase power 3: 2 cavities, 1 amp 4: 3-cell cavity, 1 amp 5: 2 cavities, 2 amps]

---
Already in the queue: Booster RF Upgrade
Solid state
amplifier
Klystron
Power
supply
LLRF

---
RF upgrade for Booster and SR:
2 power amplifiers (75kW + 20kW):
Call for tender in spring 2016
4 bidders, net price range from ~500 k€ to ~1,3 M€ for 2 amps + spare parts
Order to Cryoelectra GmbH,	- lowest price,
- presumably most sustainable/maintainable system
Thanks to W. Anders from BESSY for support.
1 EU-cavity (HOM damped):
Call for tender in summer 2016
1 bidder
Order to Research Instruments GmbH
Thanks to V. Dürr from BESSY for support.
Infrastructural and other upgrades:
- 150 kW additional power from university transformers
- 150 kW additional water cooling power
- Cavity support, waveguides, tapers, ...
Thanks to the DELTA Team, the university administration and technical institutions for support.
Required:
20 years of operation
- with or
- without company support
Problems:
Local console based on Win XP / LabView
Devices w/ proprietary firmware
Spare parts
Solution:
- Use parts w/ longtime support if possible
- Complete documentation of hardware (NDA)
- More spare parts when proprietary firmware
- Virtualization of local console
- Only network communication in VM
- Still: What about activation of XP ?

---
Positions and Schedule
Week 08-10/2017 (3 week shutdown)
- Delivery of amplifiers
- Installation and commissioning of booster amplifier
- Installation of SR amp (outside the ring)
Nov. 2017
- Delivery of EU-Cavity
- Installation of Cavity in Weis-Bunker (outside the ring)
- Commissioning and burn-in of cavity with amp indep. of accelerator. operation
Feb. 2018:
- Installation of cavity in the storage ring
- Re-commissioning

---
Cavity sketch courtesy Research Instruments GmbH

---
Analog Low Level RF
?

---
Digital Low Level RF
500 MHz
Analog
Frontend
ADC
FPGA
DAC
Analog
Frontend
Motor
driver
Cav 1
Klystron
?
Motor
driver
Cav 2
SSA

---
Do we need a power circulator for the storage ring ?
What is your advice ?
Thank you !